## Slide 1
System Design: Complete Guide
Based on the System Design Primer
418 Slides · 11 Sections · Fundamentals → Advanced

## Slide 2
Section 1: Fundamentals

## Slide 3
Topic 1: What is System Design?

## Slide 4
What is System Design? (Concept Introduction)
▸ The discipline of defining components, interfaces, and data flow for a system
  ↳ It is the bridge between abstract requirements and concrete code that must run reliably at scale.
▸ A decision-making process under constraints (cost, latency, traffic, team)
  ↳ Every choice trades one property for another; design is choosing which trade-offs to accept consciously.
▸ Operates at the "macro" level above class/function design
  ↳ It answers questions like "how do services talk?" rather than "how do I sort this list?"
▸ Output is typically a blueprint: diagrams, contracts, capacity plans
  ↳ Engineers then implement that blueprint; without it, teams build incompatible pieces.
📊 Pyramid with three layers - bottom "Code (functions/classes)", middle "Architecture (services/modules)", top "System Design (cr...

## Slide 5
Why System Design Matters (Deep Explanation)
▸ Mistakes at the design layer are the most expensive to fix
  ↳ A wrong database choice may require months of dual-writes and migrations; a wrong function is a 10-line patch.
▸ Non-functional requirements (NFRs) usually decide success, not features
  ↳ Users abandon a correct app that takes 8 seconds to load; latency, availability, and cost are first-class citizens.
▸ It forces explicit reasoning about failure
  ↳ In a single process, failure means a crash; in a distributed system, failure means partial, partial, partial - and design must say what each partial means.
▸ It aligns the team on shared mental models
  ↳ Without a design doc, two engineers will independently invent two incompatible queue contracts and discover the conflict in production.
📊 Cost-of-change curve - x-axis "Time (Idea -> Design -> Build -> Deploy -> Production)", y-axis "Cost to fix" rising exponentially

## Slide 6
Scope of System Design (Deep Explanation)
▸ Functional scope: what the system does (APIs, workflows, features)
  ↳ Defines the contract with users; e.g., "upload a video, get a transcoded URL within 60 seconds."
▸ Non-functional scope: how well it does it (latency, availability, durability, cost, security)
  ↳ These are measurable targets like "p99 < 200 ms" or "99.95% monthly uptime."
▸ Operational scope: how it is run (deployment, observability, on-call, capacity)
  ↳ A design that cannot be debugged at 3 AM is not a finished design.
▸ Evolution scope: how it changes (versioning, migrations, deprecations)
  ↳ Real systems live for years; design must allow swapping a database without a rewrite.
📊 4-quadrant diagram labeled Functional / Non-Functional / Operational / Evolution, each with example bullet points

## Slide 7
System Design as a Restaurant (Analogy)
▸ The menu is the API contract
  ↳ It tells customers what they can order and what they will receive; you cannot change it on a whim mid-service.
▸ The kitchen layout is the service topology
  ↳ Where the prep station, grill, and pass are placed determines throughput; a bad layout creates bottlenecks no recipe can fix.
▸ Reservations and waitlists are rate limiting and queueing
  ↳ Without them, a popular Saturday night collapses the entire restaurant; with them, the experience degrades gracefully.
▸ Health inspectors are observability and SLOs
  ↳ You cannot only check the kitchen when the customers complain; you instrument continuously so you catch issues before they reach the diner.
📊 Restaurant floor plan with labels mapping kitchen-to-services, host-to-load-balancer, menu-to-API

## Slide 8
Topic 2: Performance vs Scalability

## Slide 9
Performance vs Scalability (Concept Introduction)
▸ Performance: how fast the system responds for a single unit of work
  ↳ Measured per request - latency, response time, time-to-first-byte for one user.
▸ Scalability: how the system behaves as load grows
  ↳ Measured by how performance and cost change as users, data, or traffic multiply.
▸ They are related but independent properties
  ↳ A system can be fast for one user yet collapse at 1,000 users; another can be slow per request but handle a million in parallel.
▸ Optimizing one does not automatically improve the other
  ↳ Caching can boost performance without helping scalability; sharding scales but may worsen single-request latency.
📊 Two side-by-side gauges: "Performance = speed of one car" vs "Scalability = how the highway handles 100,000 cars"

## Slide 10
Defining Performance Precisely (Deep Explanation)
▸ Performance is a distribution, not a number
  ↳ "Average latency 100 ms" hides that 1% of users wait 10 seconds; always think p50, p95, p99, p999.
▸ Response time = service time + waiting time
  ↳ Even a 5 ms operation feels slow if it queues 200 ms behind other work; queueing is often the real culprit.
▸ Tail latency dominates user experience in distributed calls
  ↳ If one request fans out to 100 services, the slowest one defines the user-perceived latency.
▸ Performance is bounded by the critical path
  ↳ Optimizing code that is not on the critical path adds complexity without speeding anything up.
📊 Latency histogram with marked p50, p95, p99 lines and a long tail to the right

## Slide 11
Defining Scalability Precisely (Deep Explanation)
▸ Vertical scaling: bigger machine (more CPU, RAM, disk)
  ↳ Simple but bounded by hardware limits and a single point of failure; doubling cost rarely doubles capacity past a point.
▸ Horizontal scaling: more machines working together
  ↳ Effectively unbounded but introduces coordination, partitioning, and network failure as new problems.
▸ Linear scalability: 2x resources -> 2x throughput (the gold standard)
  ↳ Most real systems achieve sub-linear scaling because of contention, coordination, and shared state.
▸ Scalability is about the slope, not the intercept
  ↳ A system starting at 100 RPS that grows to 1M RPS scales well; one at 10K RPS that caps at 12K does not.
📊 Two graphs: vertical scaling curve plateauing, horizontal scaling line continuing upward; x-axis "load", y-axis "throughput"

## Slide 12
Highway Analogy for Performance vs Scalability
▸ Performance is the speed limit on the road
  ↳ A faster sports car (better algorithm) lets one driver get there quicker - that is single-request performance.
▸ Scalability is the number of lanes
  ↳ Adding lanes lets more cars travel simultaneously without slowing each other down - that is horizontal scaling.
▸ A 10-lane highway with a 30 mph limit moves more total people than a 1-lane road at 200 mph
  ↳ High throughput does not require low latency; mass transit beats sports cars for moving cities.
▸ Bottlenecks (toll booth, on-ramp) ruin both
  ↳ One unscaled component caps the whole system; the slowest stage defines real-world performance.
📊 Top-down highway diagram showing 1 lane vs 10 lanes, with a toll booth bottleneck collapsing both

## Slide 13
Performance vs Scalability Trade-offs
▸ Caching boosts performance but can mask scaling problems
  ↳ A hot cache hides that the underlying database cannot handle the real workload when the cache is cold.
▸ Sharding improves scalability but adds cross-shard latency
  ↳ Single-key reads stay fast; queries that span shards now require fan-out and merging - slower per query.
▸ Replication improves read scalability and availability but hurts write performance
  ↳ Each write must propagate; stronger consistency means more coordination and higher write latency.
▸ Asynchronous processing trades per-request latency for system throughput
  ↳ The user sees an instant "queued" response, but the actual work happens later - good for throughput, bad for synchronous needs.
📊 2x2 matrix - axes "Per-Request Latency" and "Total Throughput" - placing caching, sharding, replication, async in their respect...

## Slide 14
Topic 3: Latency vs Throughput

## Slide 15
Latency vs Throughput (Concept Introduction)
▸ Latency: the time a single operation takes from start to finish
  ↳ Measured in time units (ms, s); answers "how long do I wait?"
▸ Throughput: the number of operations completed per unit time
  ↳ Measured in rate units (req/s, MB/s); answers "how much can the system do per second?"
▸ They are not opposites - they are orthogonal axes
  ↳ You can have low latency and low throughput (slow single user), or high latency and high throughput (batch pipelines).
▸ Both are needed; the right balance depends on the workload
  ↳ A trading system prioritizes latency; a backup system prioritizes throughput.
📊 2D plot - x-axis "Latency (lower is better)", y-axis "Throughput (higher is better)" - with examples plotted: HFT (low lat, low...

## Slide 16
Why Latency and Throughput Diverge (Deep Explanation)
▸ Throughput = concurrency / latency (Little's Law)
  ↳ If each request takes 100 ms and you run 50 in parallel, throughput is 500 req/s; you can grow throughput by lowering latency or adding concurrency.
▸ Batching increases throughput at the cost of latency
  ↳ Grouping 100 small writes into one large write amortizes overhead per item but makes the first item wait for the last.
▸ Pipelining hides latency without reducing it
  ↳ While one stage waits, another processes; total wall time per request is unchanged but units-per-second goes up.
▸ Network and disk have very different latency/throughput profiles
  ↳ SSDs: 100 microsecond latency, GB/s throughput; spinning disk: 10 ms latency, 100 MB/s throughput - design must respect both numbers.
📊 Pipeline diagram showing 4 stages processing different requests simultaneously, with a single request's latency highlighted as ...

## Slide 17
Latency Sources You Must Know (Deep Explanation)
▸ Speed of light is non-negotiable
  ↳ Light needs about 5 ms to cross the US one way; no software optimization beats geography for cross-continent calls.
▸ Network round trips are the usual culprit
  ↳ Each TCP handshake and TLS negotiation adds RTTs; reducing chattiness often beats optimizing CPU.
▸ Disk I/O is orders of magnitude slower than memory
  ↳ Memory access is nanoseconds; SSD is microseconds; spinning disk is milliseconds; design data placement accordingly.
▸ Garbage collection, context switches, and locks add jitter
  ↳ These are why p99 is so much worse than p50; fixing the median rarely fixes the tail.
📊 "Latency numbers every engineer should know" log-scale chart - L1 cache 1ns, RAM 100ns, SSD 100us, network 1ms, cross-continent...

## Slide 18
Coffee Shop Analogy for Latency vs Throughput
▸ Latency is how long one customer waits for their coffee
  ↳ A pour-over latte takes 4 minutes regardless of how many baristas you hire for one customer.
▸ Throughput is how many coffees the shop serves per hour
  ↳ Adding baristas, espresso machines, and a second register grows throughput without changing one customer's wait.
▸ Drive-through windows trade latency for throughput
  ↳ Pre-batching milk, simplifying the menu, and parallel windows raise cups-per-hour but add steps that could be slower per cup.
▸ A queue forming is a sign throughput is below arrival rate
  ↳ When customers arrive faster than the shop serves them, latency grows unboundedly even though the baristas are at full speed.
📊 Coffee shop diagram with one register (low throughput), three registers (high throughput), and a growing queue when arrival rat...

## Slide 19
Latency vs Throughput Trade-offs
▸ Optimizing for low latency often caps throughput
  ↳ Dedicating resources to fast single-request paths (no batching, low queue depth) leaves capacity unused under load.
▸ Optimizing for high throughput often raises latency
  ↳ Batching, buffering, and queueing increase efficiency but make any single request wait longer.
▸ Synchronous APIs prioritize latency; asynchronous pipelines prioritize throughput
  ↳ REST/RPC give immediate answers; Kafka/SQS process backlogs but the producer does not see the result.
▸ Workload matters: real-time vs analytics have opposite design pressures
  ↳ A search box must answer in 50 ms per query; a nightly ETL must finish 1 TB by morning - same data, different systems.
📊 Two side-by-side architectures: "Low Latency Path" (sync, in-memory, no batch) vs "High Throughput Path" (async, batch, queue)

## Slide 20
Topic 4: Availability vs Consistency Trade-off (CAP)

## Slide 21
Availability vs Consistency (Concept Introduction)
▸ Consistency (C in CAP): every read sees the most recent write
  ↳ All nodes agree on the same value at the same time, as if there were a single copy.
▸ Availability (A in CAP): every request gets a non-error response
  ↳ The system stays responsive even if some replicas are unreachable, even if data is stale.
▸ Partition tolerance (P): system continues despite network failures between nodes
  ↳ In any real distributed system, partitions will happen, so P is not optional - it is reality.
▸ CAP theorem: during a partition, you must choose C or A - you cannot have both
  ↳ This is the core trade-off; understanding it shapes every distributed data decision.
📊 Classic CAP triangle with C, A, P at corners; arrow showing "you pick 2 sides during a partition"

## Slide 22
What Consistency Really Means (Deep Explanation)
▸ Strong consistency: a read after a write always returns the new value
  ↳ Implemented via consensus (Raft, Paxos) or single-leader writes; expensive because nodes must agree before returning.
▸ Eventual consistency: replicas converge given no new writes
  ↳ Reads may return stale data temporarily; cheap and highly available, but applications must tolerate disagreement.
▸ Causal consistency: operations that are causally related are seen in order
  ↳ "Reply" must appear after "comment"; unrelated operations can be observed in any order.
▸ Consistency is not a binary - it is a spectrum
  ↳ Read-your-writes, monotonic reads, and bounded staleness are middle-ground guarantees with real production value.
📊 Spectrum from "Strong Consistency" (linearizable) on the left to "Eventual" on the right, with milestones - Sequential, Causal,...

## Slide 23
What Availability Really Means (Deep Explanation)
▸ Availability is measured in 9s of uptime
  ↳ 99.9% = ~8.7 hours downtime/year; 99.99% = 52 minutes; 99.999% = 5 minutes - each "9" costs roughly 10x more.
▸ Availability includes "responds with a useful answer," not just "responds"
  ↳ A 500 error is technically a response but counts as unavailable; SLOs measure successful responses.
▸ Highly available systems must tolerate partial failure gracefully
  ↳ When a replica is down, the system serves from another; when a region is down, traffic shifts to another region.
▸ Availability is harder than it looks because of dependency chains
  ↳ A service with 99.9% uptime that depends on three other 99.9% services has at best 99.7% effective availability.
📊 Stacked bar showing how dependencies multiply downtime; table of "9s" mapped to allowed downtime per year

## Slide 24
Bank vs Social Feed Analogy
▸ A bank chooses consistency over availability
  ↳ If the network partitions, an ATM should refuse the withdrawal rather than risk double-spending; "service unavailable" beats incorrect balance.
▸ A social feed chooses availability over consistency
  ↳ Users seeing slightly stale likes is fine; a blank feed is unacceptable, so each region serves its local replica.
▸ A shopping cart blends both at different layers
  ↳ Adding to cart is AP (it just works); checkout is CP (must agree on inventory and price exactly).
▸ The right choice depends on the cost of being wrong
  ↳ Wrong money is a lawsuit; wrong like count is a shrug; design the trade-off per feature, not per system.
📊 Two columns - "Bank (CP): refuse if uncertain" vs "Social Feed (AP): always show something" - with example error and stale-data...

## Slide 25
PACELC - Beyond CAP (Deep Explanation)
▸ CAP only describes behavior during a partition
  ↳ But partitions are rare; most of the time the network is fine, and CAP says nothing about that case.
▸ PACELC: if Partition then A vs C, Else (normal operation) Latency vs Consistency
  ↳ It captures that even without partitions, stronger consistency costs more latency due to coordination.
▸ Example: Dynamo-style stores are PA/EL (available during partition, low latency normally)
  ↳ They sacrifice consistency in both regimes for speed and uptime.
▸ Example: Spanner-style stores are PC/EC (consistent during partition, consistent normally)
  ↳ They accept higher latency from cross-region consensus to keep correctness everywhere.
📊 PACELC matrix - rows "Partition / No Partition", columns "Consistency vs Availability/Latency" - with real systems mapped

## Slide 26
Availability vs Consistency Trade-offs in Practice
▸ Strong consistency requires coordination, which limits scale and uptime
  ↳ Quorum reads/writes and consensus protocols add latency and create unavailability when too many nodes are down.
▸ Eventual consistency enables scale and uptime but pushes complexity to the application
  ↳ The app must handle conflicts (last-write-wins, CRDTs, user merge), which is real engineering work.
▸ The choice is feature-by-feature, not system-wide
  ↳ The same product may store user profiles eventually but billing strongly; design each data flow on its own merits.
▸ Read your SLA, not the marketing
  ↳ "Highly available" and "consistent" are vague; quantify required uptime, max staleness, and conflict resolution explicitly.
📊 Decision tree - "Is incorrect data acceptable for this feature?" -> Yes (AP) / No (CP) - with example features at each leaf

## Slide 27
Section Wrap-Up

## Slide 28
Key Takeaways
▸ System design is about trade-offs under constraints, not about finding the "best" answer
  ↳ Every choice gives up something; the goal is to give up the right thing for your context.
▸ Performance and scalability are independent - measure and optimize them separately
  ↳ Fast for one user does not imply fast for a million; design for the actual workload, not the demo.
▸ Latency and throughput are orthogonal - know which one your workload demands
  ↳ Real-time systems chase latency; batch systems chase throughput; mixing the two confuses design.
▸ CAP/PACELC force explicit decisions about consistency, availability, and latency
  ↳ Distributed systems will partition; deciding in advance how the system behaves is the core of system design.
▸ All four concepts compose - real systems navigate every trade-off simultaneously
  ↳ A single feature may demand low latency, high throughput, strong consistency, and high availability - acknowledge what gives.
📊 Mind map with "System Design" center node, branches to Performance/Scalability/Latency/Throughput/Consistency/Availability, eac...

## Slide 29
Interview Tips
▸ Always clarify functional and non-functional requirements before designing
  ↳ Asking "what is the read:write ratio?" or "what latency is acceptable?" signals senior thinking and prevents wasted whiteboard work.
▸ State assumptions out loud and write them down
  ↳ Interviewers grade reasoning, not memorized answers; explicit assumptions show you understand the trade-off space.
▸ Use back-of-envelope numbers to justify choices
  ↳ "10M DAU * 100 events = 1B events/day = 12K events/sec" turns vague design into a concrete capacity argument.
▸ Name the trade-off you are choosing and why
  ↳ Saying "I am picking AP here because stale reads are acceptable for this feed" is stronger than "I'll use Cassandra."
▸ Start simple, then scale - do not over-engineer round one
  ↳ A monolith that works beats a microservice diagram that does not; show you can evolve a design instead of premature complexity.
📊 Whiteboard checklist: Clarify -> Estimate -> Sketch high-level -> Identify bottlenecks -> Apply trade-offs -> Discuss evolution

## Slide 30
Common Pitfalls
▸ Confusing performance with scalability
  ↳ Adding a faster CPU does not help when the database is the bottleneck; profile first, optimize the right axis.
▸ Optimizing average latency while ignoring tail latency
  ↳ Users feel p99, not p50; a "fast" service with bad p99 fans out into terrible end-to-end experiences.
▸ Treating CAP as a one-time choice for the whole system
  ↳ It is per data flow and per failure mode; saying "we are AP" hides where you actually need C.
▸ Using "highly available" or "scalable" without numbers
  ↳ These are aspirations, not requirements; without SLOs, you cannot tell if the design meets the need.
▸ Adding caches/queues/microservices before the simple version is exhausted
  ↳ Each adds operational burden, failure modes, and consistency complications; only introduce them when the simpler design provably fails.
▸ Forgetting the cost dimension
  ↳ A design that meets all NFRs at 100x the budget is wrong; design includes "is this cost-effective at our scale?"
📊 List of red-flag phrases ("we'll just cache it", "Mongo is web scale", "we need microservices") with the underlying mistake ann...

## Slide 31
Section 2: CAP Theorem, Consistency & Availability Patterns

## Slide 32
Part A: CAP Theorem

## Slide 33
CAP Theorem — Concept Introduction
▸ CAP stands for Consistency, Availability, Partition Tolerance
  ↳ A theorem by Eric Brewer (2000) about distributed data stores
▸ A distributed system can guarantee at most TWO of the three at the same time
  ↳ You cannot escape the trade-off when a network partition occurs
▸ Partition Tolerance is non-negotiable in real distributed systems
  ↳ Networks fail; you must handle dropped or delayed messages between nodes
▸ Therefore the realistic choice is between CP and AP, not CA
  ↳ CA only exists in single-node or assumed-perfect-network systems
▸ CAP guides architectural decisions for databases, caches, and messaging systems
  ↳ Different workloads (banking vs social feed) tolerate different sacrifices
📊 a triangle with C, A, P at the corners; three overlapping circles; highlight that during a partition you must drop either C or A

## Slide 34
CAP — Defining the Three Properties Precisely
▸ Consistency (C): every read receives the most recent write or an error
  ↳ Equivalent to linearizability — all clients see the same data at the same time
▸ Availability (A): every request receives a non-error response (no guarantee it is the latest)
  ↳ The system stays responsive even if data is stale
▸ Partition Tolerance (P): the system continues to operate despite network message loss between nodes
  ↳ The cluster does not collapse when a link breaks
▸ "Pick 2" is misleading — it really means "during a partition, pick C or A"
  ↳ When the network is healthy, you can have both C and A
▸ CAP is about the worst-case behavior, not steady-state behavior
  ↳ The trade-off shows up only when partitions happen
📊 a 2-column comparison: "Healthy network → C + A possible" vs "Partition → choose C or A"

## Slide 35
CAP Theorem — Deep Explanation (How the Trade-off Plays Out)
▸ Imagine two replicas separated by a broken link receiving conflicting writes
  ↳ Replica A gets value X=10, replica B gets value X=20, neither can sync
▸ A CP system refuses one of the writes (or blocks reads) to preserve correctness
  ↳ Sacrifices availability — the client gets an error or timeout
▸ An AP system accepts both writes and reconciles later (last-write-wins, vector clocks, CRDTs)
  ↳ Sacrifices consistency — clients may read stale or divergent data temporarily
▸ The choice is fundamentally about user experience and business risk
  ↳ "Wrong answer" vs "no answer" — pick which one your domain can survive
▸ CAP is not binary in practice; tunable consistency (Cassandra, DynamoDB) lets you slide along the spectrum
  ↳ You set quorum levels per operation: stricter for money, looser for likes
📊 timeline showing partition at T=5s; CP path shows "request blocked"; AP path shows "request served, reconcile at T=12s"

## Slide 36
CP Systems — Concept and Examples
▸ CP = Consistent + Partition Tolerant; sacrifices availability during partitions
  ↳ The system would rather return an error than risk stale data
▸ Use when correctness matters more than uptime
  ↳ Banking ledgers, inventory counts, distributed locks, leader election
▸ HBase: built on HDFS, uses a single RegionServer per region — strong consistency, no split-brain
  ↳ If the RegionServer is unreachable, that region becomes unavailable until failover
▸ ZooKeeper: coordination service using ZAB protocol; majority quorum required for writes
  ↳ Loses availability when fewer than (N/2)+1 nodes are reachable, but never lies
▸ etcd, Google Spanner (with Paxos), MongoDB (in majority write concern) follow the same pattern
  ↳ All choose to halt rather than serve potentially incorrect data
📊 5-node ZooKeeper cluster, 2 nodes partitioned off; minority side rejects writes, majority continues

## Slide 37
AP Systems — Concept and Examples
▸ AP = Available + Partition Tolerant; sacrifices strict consistency during partitions
  ↳ Always returns a response, even if the data might be stale
▸ Use when uptime and responsiveness matter more than perfect freshness
  ↳ Social feeds, shopping carts, DNS, content delivery, analytics
▸ Cassandra: peer-to-peer ring, tunable consistency, gossip-based replication
  ↳ Writes accepted at any node; conflicts resolved by last-write-wins timestamp
▸ DynamoDB: AWS's managed AP store with eventual consistency by default
  ↳ Optional "strongly consistent reads" trade availability for freshness
▸ Riak, CouchDB, Voldemort follow Amazon's Dynamo paper design
  ↳ All embrace temporary divergence and reconcile via vector clocks or merge functions
📊 Cassandra ring with 6 nodes; partition splits 3 vs 3; both sides keep accepting writes; arrows show later reconciliation

## Slide 38
CA Systems — Why They Are Not Realistic in Distributed Systems
▸ CA = Consistent + Available, but only when there are no partitions
  ↳ In practice, distributed networks always partition eventually
▸ A single-node relational database (PostgreSQL, MySQL standalone) is "CA"
  ↳ But it is not actually distributed — there is no partition to tolerate
▸ Two-phase commit clusters are sometimes called CA, but they freeze under partitions
  ↳ That freezing IS sacrificing availability, so they are really CP
▸ Believing you have CA usually means you have unaccounted-for risk
  ↳ Your "always-on" assumption breaks the moment a switch flaps
▸ The honest framing: distributed systems must pick between CP and AP
  ↳ CA is a marketing label, not an engineering reality
📊 a triangle with "CA" corner crossed out and labeled "single-node only"; arrow pointing to "real distributed = CP or AP"

## Slide 39
CAP — Banking vs Social Media Analogy
▸ ATM withdrawal (CP): bank refuses to dispense cash if it cannot verify your balance
  ↳ Better to say "service unavailable" than to let you overdraw
▸ Twitter timeline (AP): you see tweets even if the count is slightly stale
  ↳ "37 likes" vs "39 likes" — nobody dies, the app stays usable
▸ DNS (AP): cached records may be stale but resolution always succeeds
  ↳ Eventual propagation across the globe is acceptable for name lookups
▸ Stock trading exchange (CP): a trade must reflect the true order book
  ↳ Showing wrong prices could cause millions in losses, so halt instead
▸ Picking CP vs AP is fundamentally a product decision, not a tech decision
  ↳ Engineering serves the cost of being wrong vs the cost of being down
📊 split panel — left "ATM screen showing Service Unavailable", right "Twitter feed loading with stale like counts"

## Slide 40
CAP Theorem — Diagram Slide
▸ Draw the canonical CAP triangle with three vertices
  ↳ C (Consistency), A (Availability), P (Partition Tolerance)
▸ Show three overlapping regions on the edges
  ↳ CP edge: HBase, ZooKeeper, etcd, Spanner
  ↳ AP edge: Cassandra, DynamoDB, Riak, CouchDB
  ↳ CA edge: traditional RDBMS (single node) — mark as "not truly distributed"
▸ Add a horizontal "partition occurred" line through the middle
  ↳ Above it: healthy state, all three achievable
  ↳ Below it: must drop either C or A
▸ Annotate each system with its trade-off rationale
  ↳ e.g., "ZooKeeper: blocks minority side to avoid split-brain"
📊 equilateral triangle with vertex labels, system logos placed on edges, dashed "partition line" cutting across the middle

## Slide 41
CAP Theorem — Trade-offs Slide
▸ CP trade-off: stronger correctness, but you must tolerate downtime windows
  ↳ Failover is slow because the system pauses until quorum re-forms
▸ AP trade-off: always-on UX, but clients must handle stale or conflicting data
  ↳ Application code becomes more complex (conflict resolution, retries)
▸ Latency cost in CP: every write waits for quorum acknowledgment
  ↳ Cross-region writes can take 100s of ms or fail outright
▸ Operational cost in AP: you need monitoring for replication lag and divergence
  ↳ Hidden bugs show up only under partition or load
▸ The trade-off is not permanent; it is per-operation when using tunable consistency
  ↳ Read at quorum for the cart total, read at ONE for product images
📊 a 2x2 matrix — rows: CP/AP; columns: Pros/Cons — filled with bullet points above

## Slide 42
Part B: Consistency Patterns

## Slide 43
Consistency Patterns — Concept Introduction
▸ Consistency defines what guarantees a system makes about read-after-write visibility
  ↳ "If I write X=5, when will I (or others) see X=5?"
▸ Three main models on a spectrum: weak, eventual, strong
  ↳ From "no promises" to "immediately and forever"
▸ The right model depends on the data's tolerance for staleness
  ↳ Likes count → eventual; bank balance → strong
▸ Stronger consistency costs more latency, throughput, and availability
  ↳ You pay in coordination overhead for every write
▸ Many real systems mix models per data type within the same application
  ↳ User profile (eventual) + payment record (strong) in one product
📊 horizontal bar from "Weak" → "Eventual" → "Strong" with example workloads under each

## Slide 44
Weak Consistency — Deep Explanation
▸ After a write, reads may or may not see the new value, with no guarantee at all
  ↳ The system makes a best-effort attempt and moves on
▸ Common in real-time systems where freshness beats correctness
  ↳ Live video, VoIP, online multiplayer game state
▸ Implementation: no replication coordination, no read-after-write guarantee
  ↳ Each node serves whatever it has locally; missed updates are simply lost or ignored
▸ Memcached without invalidation is effectively weak consistency
  ↳ Stale entries linger until TTL expires; nobody guarantees freshness
▸ Trade you accept: lowest latency, highest throughput, but unpredictable correctness
  ↳ Acceptable when the user can re-issue the request or the data self-corrects
📊 client writes X=5; three subsequent reads return 5, undefined, 3 — with arrows showing no coordination between replicas

## Slide 45
Weak Consistency — Example and Analogy
▸ Live sports score broadcast: if you miss a goal, you don't replay it — next update overrides
  ↳ The system never blocks waiting for stragglers
▸ Voice over IP: dropped audio packets are skipped, not retransmitted
  ↳ Latency budget is too tight to wait
▸ Multiplayer game position updates: only the latest position matters
  ↳ Old "I was at (10, 20)" packets are useless once "I am at (15, 25)" arrives
▸ Stock ticker on a public site: shows approximate prices, not authoritative
  ↳ The actual trade settlement uses a different (strong) system
▸ Analogy: shouting across a noisy room — receivers hear what they hear, no acknowledgments
  ↳ You rely on the next shout to overwrite any miss
📊 a stadium with thousands listening to a live commentator; if your audio glitches, you just hear the next sentence

## Slide 46
Eventual Consistency — Deep Explanation
▸ After a write, replicas will converge to the same value if no new writes occur
  ↳ Given enough time, all nodes will agree, but "eventually" can mean ms to minutes
▸ Reads can return stale data temporarily — your own write may not be visible immediately
  ↳ Read-your-writes is a stronger sub-guarantee that some systems add on top
▸ Implementation: asynchronous replication, gossip protocols, anti-entropy repair
  ↳ Background processes propagate updates and reconcile divergence
▸ Conflict resolution strategies needed when two replicas accept conflicting writes
  ↳ Last-Write-Wins (timestamp), vector clocks, CRDTs, application-level merge
▸ DynamoDB, Cassandra, DNS, S3 (historically), email all operate eventually consistent
  ↳ Each chose availability and partition tolerance over instant consistency
📊 3 replicas; write at T=0 to replica 1; gossip arrows propagate at T=2s, T=5s; all converged by T=10s

## Slide 47
Eventual Consistency — DNS Analogy
▸ DNS records have TTLs (Time To Live); changes propagate over hours
  ↳ You change an A record, but resolvers worldwide still serve the old IP until cache expires
▸ Eventually all DNS resolvers converge to the new value
  ↳ There is no global lock, no coordination — just timeout-based refresh
▸ This is acceptable because DNS prioritizes availability and scale over instant updates
  ↳ Internet-wide propagation in milliseconds would require a coordination layer DNS doesn't have
▸ Email is similar: a sent message may take seconds to minutes to appear in the inbox
  ↳ Spam filters, routing, and delivery agents add latency without breaking the system
▸ Shopping cart in Amazon's original Dynamo: if two devices add items, both items end up in the cart
  ↳ "Add to cart" is mergeable — eventual consistency works because conflicts are union-able
📊 world map; DNS update originates in US-East; clock ticks show propagation reaching EU at T=2min, Asia at T=5min

## Slide 48
Strong Consistency — Deep Explanation
▸ After a write completes, every subsequent read returns that value or a newer one
  ↳ Equivalent to having a single, atomic copy of the data globally
▸ Linearizability: operations appear to execute instantaneously in a total order
  ↳ This is the "ideal" but expensive guarantee
▸ Implementation requires coordination: consensus protocols (Paxos, Raft, ZAB)
  ↳ A majority quorum must agree before a write is acknowledged
▸ Examples: Google Spanner (TrueTime + Paxos), CockroachDB, etcd, ZooKeeper, traditional RDBMS
  ↳ All pay latency cost for guaranteed correctness
▸ Cost: every write incurs at least one round-trip to a quorum
  ↳ Cross-region clusters add tens to hundreds of ms per write
📊 client → leader → 2 of 3 followers must ACK → leader responds OK; show the latency arrow grow with each hop

## Slide 49
Strong Consistency — Banking Analogy
▸ Bank balance must reflect every deposit and withdrawal immediately
  ↳ You cannot "eventually" have $500; either you have it now or you don't
▸ Two ATMs withdrawing from the same account must coordinate
  ↳ Otherwise both succeed, the balance goes negative, and the bank loses money
▸ Inventory in an e-commerce checkout (last unit) — must be strongly consistent
  ↳ Selling the same physical item twice creates customer-service disasters
▸ Distributed locks (ZooKeeper, etcd) — only one client can hold the lock
  ↳ Eventual consistency would let two clients both think they have it (split-brain)
▸ Strong consistency = "the truth is one, and everyone sees it the same way"
  ↳ Worth the latency for correctness-critical workloads
📊 two ATMs both trying to withdraw $100 from a $150 account; coordinator allows one and rejects the other

## Slide 50
Consistency Patterns — Comparison Diagram
▸ Draw three horizontal lanes representing the three models
  ↳ Lane 1: Weak — write at T=0; reads return random values, no guarantees
  ↳ Lane 2: Eventual — reads return old values briefly; converge to new value at T=convergence
  ↳ Lane 3: Strong — read at any T after write returns the new value, always
▸ Add latency bars showing relative write cost
  ↳ Weak: lowest; Eventual: medium; Strong: highest
▸ Add availability bars showing tolerance to partitions
  ↳ Weak/Eventual: high availability; Strong: drops during partition
▸ Mark example systems on each lane
  ↳ Weak: VoIP, live video; Eventual: DNS, Cassandra, S3; Strong: Spanner, etcd, RDBMS
▸ Add a "tunable consistency" callout for systems like Cassandra and DynamoDB
  ↳ Same system can shift between lanes per operation via quorum settings
📊 3 horizontal timelines stacked vertically with color-coded write/read events and latency bars

## Slide 51
Consistency Patterns — Trade-offs Slide
▸ Weak: maximum performance, but data may be silently wrong
  ↳ Only safe when staleness is invisible or self-correcting
▸ Eventual: high availability and scalability, but app must handle stale reads
  ↳ Need conflict resolution and possibly read-your-writes guarantees
▸ Strong: developer-friendly correctness, but latency and availability costs
  ↳ Cross-region strong consistency can make writes 10x slower
▸ Mixed strategies are typical in production
  ↳ Strong for money flows, eventual for feeds, weak for telemetry
▸ Choosing too strong is a common over-engineering trap
  ↳ Costs throughput and availability for guarantees you didn't actually need
📊 3-column table — Weak | Eventual | Strong — rows: Latency, Availability, Complexity, Use cases

## Slide 52
Part C: Availability Patterns

## Slide 53
Availability Patterns — Concept Introduction
▸ Availability = the percentage of time the system is operational and serving requests
  ↳ Measured as uptime divided by total time, expressed as "nines"
▸ Two main techniques to achieve high availability: fail-over and replication
  ↳ Fail-over swaps in a backup; replication keeps multiple live copies
▸ Availability is multiplicative across dependencies in a chain
  ↳ 99.9% × 99.9% × 99.9% = 99.7% — each hop reduces overall availability
▸ High availability requires eliminating single points of failure (SPOFs)
  ↳ Redundancy in compute, storage, network, and even regions
▸ Availability is expensive — each additional "nine" costs roughly 10x more
  ↳ 99% to 99.9% is doable; 99.999% requires multi-region active-active and obsessive ops
📊 pyramid showing cost vs nines — base "99%" wide; tip "99.999%" narrow with $$$$ label

## Slide 54
Fail-over — Concept and Mechanisms
▸ Fail-over = automatically switching to a standby system when the primary fails
  ↳ Detection (heartbeats, health checks) → promotion (standby takes over) → traffic redirect
▸ Two flavors: active-passive and active-active
  ↳ Differ in whether the standby is idle or already serving traffic
▸ Detection time + promotion time = recovery time objective (RTO)
  ↳ Faster detection means faster recovery but more false positives
▸ Common mechanism: virtual IPs, DNS failover, load balancer health checks, leader election
  ↳ Each adds latency and complexity to the failover path
▸ Fail-over is reactive — it kicks in after something breaks
  ↳ Replication is proactive — multiple copies always serve in parallel
📊 primary server with heartbeat to standby; primary fails (red X); standby promoted; clients redirected via VIP

## Slide 55
Active-Passive Fail-over — Deep Explanation
▸ One active node serves all traffic; the passive node stands by, often replicating data
  ↳ Passive does no useful work until the active dies
▸ Cheaper to operate (less load on standby) but slower to recover
  ↳ Promotion can take seconds to minutes depending on the technology
▸ Common in traditional RDBMS clusters (PostgreSQL streaming replication, MySQL with MHA)
  ↳ Read replicas may serve read-only traffic while waiting to promote
▸ Risk: split-brain if both nodes think they are active simultaneously
  ↳ Mitigated with fencing (STONITH), witness nodes, or quorum-based election
▸ RTO is typically 30 seconds to 5 minutes; RPO depends on replication mode
  ↳ Synchronous replication = zero data loss; async = potential lag
📊 client → load balancer → active DB; passive DB receives async replication; on failure, LB switches arrow to passive

## Slide 56
Active-Active Fail-over — Deep Explanation
▸ Multiple nodes serve traffic concurrently; if one fails, the others absorb the load
  ↳ No promotion delay — surviving nodes continue without interruption
▸ Higher cost (all nodes provisioned for full capacity) but near-zero RTO
  ↳ Used when downtime tolerance is in the milliseconds (financial trading, large web apps)
▸ Requires data to be replicated in all directions (multi-master) or sharded with redundancy
  ↳ Conflict resolution becomes mandatory if writes go to multiple primaries
▸ Examples: Cassandra rings, DynamoDB global tables, Galera Cluster for MySQL
  ↳ All nodes accept reads and writes, gossip changes, reconcile conflicts
▸ Capacity planning: must size each node to handle the failure load
  ↳ If you have 3 active nodes and one fails, the remaining 2 must absorb 50% more traffic
📊 3 active nodes behind LB, all serving traffic; one fails; arrows redistribute to remaining 2 with thicker stroke

## Slide 57
Fail-over — Banking and Web Analogy
▸ Active-passive: a backup generator at a hospital — silent until the power cuts out
  ↳ Costs money to maintain but only kicks on when needed
▸ Active-active: multiple cashiers at a bank counter — if one leaves, others keep serving
  ↳ All are working all the time; no waiting period when one disappears
▸ Active-passive in web infra: PostgreSQL primary + hot standby with pgpool or Patroni
  ↳ Standby promotes on failure, DNS or VIP redirects clients
▸ Active-active in web infra: AWS Route 53 latency routing across us-east-1 and us-west-2
  ↳ Both regions live; user routed to nearest healthy region
▸ Choose based on RTO budget and operational maturity
  ↳ Active-active is more powerful but harder to get right
📊 split panel — left "hospital with backup generator (active-passive)"; right "supermarket checkout lanes (active-active)"

## Slide 58
Replication — Master-Slave (Primary-Replica) Pattern
▸ One master accepts writes; one or more slaves replicate the master's data
  ↳ Reads can be load-balanced across slaves to scale read throughput
▸ Replication can be synchronous (master waits for slave ACK) or asynchronous (fire and forget)
  ↳ Sync = stronger durability, higher latency; async = faster writes, possible data loss on failover
▸ Slave promotion is required if the master dies — this is the failover path
  ↳ Slaves are often consistent with the master with some replication lag
▸ MySQL replication, PostgreSQL streaming replication, MongoDB replica sets
  ↳ All variants of master-slave with different lag and consistency semantics
▸ Read-write split is a common pattern: app routes writes to master, reads to slaves
  ↳ Beware of read-your-writes anomalies caused by replication lag
📊 master in center; 3 slaves with replication arrows; client writes go to master, reads fan out to slaves

## Slide 59
Replication — Master-Master (Multi-Master) Pattern
▸ Multiple masters all accept writes; changes replicate to each other
  ↳ No single write bottleneck; geographic distribution feels local to each region
▸ Conflict resolution is mandatory because two masters can write the same key concurrently
  ↳ Strategies: last-write-wins, custom merge, CRDTs, application-level resolution
▸ Active-active deployments often use master-master to avoid promotion delays
  ↳ Examples: MySQL Galera, CockroachDB, Cassandra (no master at all — peer-to-peer)
▸ Stronger availability and write scalability, but harder to reason about
  ↳ You must design schemas and writes to be idempotent and conflict-aware
▸ Replication lag still exists; cross-region writes may not be visible everywhere immediately
  ↳ Treat the system as eventually consistent unless explicitly using strong consistency mode
📊 3 masters in a triangle, all replicating to each other; clients in each region write to nearest master

## Slide 60
Replication — Failure Modes and Diagrams
▸ Replication lag: slaves fall behind under heavy write load
  ↳ User writes a comment, reads back, sees nothing — confusing UX
▸ Split-brain: in master-master, network partition causes both sides to accept conflicting writes
  ↳ Reconciliation can lose data unless conflict-free types are used
▸ Cascading failure: master dies, all reads go to a single overloaded slave, slave dies too
  ↳ Mitigate with capacity headroom and read-traffic shedding
▸ Stale replicas serving reads: caused by lag or partition
  ↳ Use "read from primary" for critical reads, "read from replica" for non-critical
▸ Replication topology choices: chain, tree, star, mesh
  ↳ Affect propagation latency and resilience
📊 master with a queue showing 30s of unreplicated writes piling up; one slave shown as "lagging"

## Slide 61
Replication — Diagram Slide
▸ Top half: master-slave topology
  ↳ 1 master with arrows to N slaves; client write arrow to master; client read arrows split
▸ Bottom half: master-master topology
  ↳ 3 nodes in a ring with bidirectional arrows; clients connect to any node for read/write
▸ Annotate with lag indicators on the replication arrows
  ↳ "async ~50ms" or "sync ~5ms" labels
▸ Show a failover scenario in a side panel
  ↳ Master fails (red X); one slave promoted (gold star); clients re-route
▸ Add a legend distinguishing sync vs async arrows
  ↳ Solid line = sync, dashed line = async
📊 layered diagram with master-slave above and master-master below, sharing a legend on the right

## Slide 62
Availability in Numbers — Concept Introduction
▸ Availability is expressed in "nines": 99%, 99.9%, 99.99%, 99.999%
  ↳ Each extra nine represents 10x less downtime
▸ 99% = 3.65 days of downtime per year (acceptable for non-critical internal tools)
  ↳ 8.76 hours per month; ~1.68 hours per week
▸ 99.9% (three nines) = 8.76 hours per year (typical web service SLA)
  ↳ 43.2 minutes per month; ~10 minutes per week
▸ 99.99% (four nines) = 52.6 minutes per year (high-availability systems)
  ↳ 4.38 minutes per month; ~1 minute per week
▸ 99.999% (five nines) = 5.26 minutes per year (telecom, financial systems)
  ↳ 26 seconds per month — requires multi-region active-active and very mature ops
📊 table with columns "Nines | Downtime/year | Downtime/month | Downtime/week | Examples"

## Slide 63
Availability in Numbers — Deep Explanation and Math
▸ SLA (Service Level Agreement): contractual availability promise to customers
  ↳ Often comes with credits if breached (e.g., 10% refund if monthly uptime <99.9%)
▸ SLO (Service Level Objective): internal target, usually stricter than SLA
  ↳ Engineering aims for 99.95% to safely meet a 99.9% SLA
▸ SLI (Service Level Indicator): the actual measured metric (success rate, latency)
  ↳ SLO is "this metric must be ≥ X%" over a window
▸ Availability composes multiplicatively in series, additively in parallel
  ↳ 3 services chained at 99.9% each = 99.7% overall
  ↳ 2 redundant 99% services in parallel ≈ 99.99% combined (1 - 0.01²)
▸ Always count dependency availability: DNS, CDN, load balancer, database
  ↳ Your max possible uptime is the product of your weakest links
📊 chain of 3 boxes labeled "99.9%" with the result "99.7%" at the end; below: 2 parallel boxes "99%" with result "99.99%"

## Slide 64
Availability in Numbers — Real-World SLA Examples
▸ AWS S3: 99.99% (four nines) availability SLA for standard storage
  ↳ Backed by multi-AZ replication and erasure coding
▸ AWS EC2: 99.99% for instances within a region; multi-AZ deployment recommended
  ↳ Single-AZ deployments fall to ~99.95% in practice
▸ Google Cloud Spanner: 99.999% (five nines) for multi-region instances
  ↳ Achieved via Paxos quorums and TrueTime synchronization
▸ Most SaaS products: 99.9% on standard tier, 99.95-99.99% on enterprise tier
  ↳ Enterprise tiers cost significantly more, often 3-5x
▸ Banking core systems: target 99.999% but rarely advertise SLAs to end users
  ↳ Maintenance windows are scheduled during off-hours to preserve apparent uptime
📊 bar chart of common services and their SLA percentages, with downtime budget labeled in minutes/year

## Slide 65
Availability — Trade-offs Slide
▸ Higher availability = exponentially higher cost
  ↳ Each additional nine roughly 10x in infra, ops, and engineering time
▸ Active-passive: cheaper, simpler, slower failover, lower availability ceiling
  ↳ Good fit for ~99.9% targets
▸ Active-active: expensive, complex, fast failover, higher availability ceiling
  ↳ Required for ~99.99%+ targets
▸ Multi-region adds latency and consistency complexity
  ↳ You buy availability with consistency or latency budget
▸ Over-engineering availability is a real risk
  ↳ Five nines is wasted if your dependencies (payment processor, DNS) only offer four
📊 cost vs availability curve — exponential rise; horizontal lines for typical targets at 99%, 99.9%, 99.99%

## Slide 66
Part D: Section Wrap-up

## Slide 67
Section Key Takeaways
▸ CAP forces a choice between consistency and availability under partition
  ↳ In practice it's CP or AP; CA is single-node only
▸ Consistency exists on a spectrum: weak, eventual, strong
  ↳ Pick per-data-type; mix within one application
▸ Availability is achieved via fail-over (active-passive, active-active) and replication (master-slave, master-master)
  ↳ Each has cost, complexity, and recovery-time trade-offs
▸ Availability composes multiplicatively across dependencies
  ↳ Your system's ceiling is the product of every component's nines
▸ Every guarantee costs latency, money, or developer effort
  ↳ The skill is matching the guarantee level to the actual business need
📊 a one-page recap diagram with CAP triangle, consistency spectrum, and availability ladder side by side

## Slide 68
Interview Tips
▸ Lead with "it depends" and ask about the workload before picking CP vs AP
  ↳ Interviewers want to see you reason about trade-offs, not memorize answers
▸ Mention real systems (Cassandra, DynamoDB, Spanner, ZooKeeper) and explain why they chose their model
  ↳ Concrete examples beat abstract claims
▸ Always discuss replication topology and failover behavior together
  ↳ They are two halves of the same availability story
▸ Ask about target availability (SLA) early in the interview
  ↳ Drives architectural choices: single-region vs multi-region, sync vs async replication
▸ Use the "during a partition, what do we do?" framing to expose CAP trade-offs
  ↳ Shows you understand CAP is about partition behavior, not steady state
📊 a bulleted interview cheat-sheet card with these phrases highlighted

## Slide 69
Common Pitfalls
▸ Claiming a system is "CA" — almost always wrong, exposes you as inexperienced
  ↳ Distributed = must tolerate partitions = CP or AP
▸ Defaulting to strong consistency everywhere
  ↳ Costs latency and availability you didn't need to spend
▸ Forgetting replication lag breaks read-your-writes assumptions
  ↳ Users complain "I posted a comment but I can't see it" — classic stale-replica bug
▸ Ignoring the cost of an extra "nine"
  ↳ Promising 99.99% when your DNS only offers 99.9% is mathematically impossible
▸ Treating CAP as static — it's per-operation, not per-system
  ↳ Modern systems (DynamoDB, Cassandra) tune consistency per request
▸ Using master-master without a conflict resolution strategy
  ↳ Silent data loss when both sides write the same key
▸ Overlooking detection time in failover RTO calculations
  ↳ Health-check interval + promotion time + DNS TTL = real recovery time
📊 a "pitfall map" with red flags marked at each common mistake, like a minefield illustration

## Slide 70
Section 3: DNS and CDN

## Slide 71
Section Overview - DNS and CDN
▸ **The two pillars of internet delivery**
  ↳ DNS gets users to the right server; CDN delivers content from the closest server.
▸ **Why these matter together**
  ↳ Before any HTTP request lands, DNS resolves the hostname; the resolved IP often points to a CDN edge.
▸ **What you will learn**
  ↳ Resolution flow, record types, geo-routing, edge caching, push vs pull, real provider trade-offs.
▸ **Mental model**
  ↳ DNS = phone book of the internet. CDN = warehouse network placed near customers.
▸ **Interview relevance**
  ↳ Almost every system design (Netflix, Instagram, e-commerce) mentions DNS routing and CDN caching as first-class citizens.
📊 Split screen - left side shows a phone book with names mapping to numbers labeled "DNS"; right side shows a global map with war...

## Slide 72
PART A: DNS (Domain Name System)

## Slide 73
What is DNS? - Concept Introduction
▸ **DNS = Domain Name System**
  ↳ A distributed, hierarchical database that translates human-friendly hostnames (google.com) into machine-friendly IP addresses (142.250.190.46).
▸ **The core problem it solves**
  ↳ Humans remember names; computers route packets using IP addresses. DNS bridges this gap.
▸ **Distributed by design**
  ↳ No single server owns the entire mapping; responsibility is split across root servers, TLD servers, and authoritative servers worldwide.
▸ **Effectively invisible infrastructure**
  ↳ You never type an IP into a browser; DNS runs silently before every web request, API call, and email delivery.
▸ **A foundational dependency**
  ↳ When DNS breaks (e.g., Facebook outage Oct 2021), the internet looks down even if servers are healthy.
📊 A user typing "google.com" into a browser, with an arrow labeled "DNS lookup" leading to "142.250.190.46", which then arrows to...

## Slide 74
Why DNS Exists - The Phone Book Analogy
▸ **The pre-DNS era (HOSTS.TXT)**
  ↳ In the 1970s ARPANET, every machine had a hosts.txt file mapping all known hostnames to IPs - manually updated and emailed around.
  ↳ This did not scale beyond a few hundred machines.
▸ **DNS introduced in 1983 by Paul Mockapetris**
  ↳ Replaced the flat file with a hierarchical, distributed system.
▸ **Phone book analogy**
  ↳ You know "Alice's Pizza" but not the phone number. You look it up in the directory. DNS is that directory for the internet.
▸ **Why a flat lookup would not work today**
  ↳ With ~360M+ registered domains, no single server can hold or update everything fast enough.
▸ **Hierarchy enables delegation**
  ↳ .com TLD operator manages .com names; example.com owner manages subdomains. Each layer scales independently.
📊 Side-by-side - left shows a single huge phone book labeled "HOSTS.TXT (does not scale)"; right shows a tree with country direct...

## Slide 75
DNS Hierarchy - Deep Explanation
▸ **Root zone (.)**
  ↳ 13 logical root server clusters (A through M) operated by 12 organizations; they know who runs each TLD.
▸ **TLD - Top-Level Domain (.com, .org, .io, .uk)**
  ↳ Run by registries (e.g., Verisign runs .com). They know which authoritative nameserver to contact for each second-level domain.
▸ **Authoritative nameserver**
  ↳ The source of truth for a specific domain (e.g., ns-1.amazon.com holds records for amazon.com).
▸ **Recursive resolver**
  ↳ Usually run by your ISP, Google (8.8.8.8), Cloudflare (1.1.1.1). Does the legwork on behalf of clients.
▸ **Stub resolver**
  ↳ The tiny client built into your OS or browser that asks the recursive resolver.
📊 Pyramid diagram - top labeled "Root (.)", below "TLD (.com, .org, .net)", below "Authoritative NS (example.com)", below "Subdom...

## Slide 76
How DNS Resolution Works - Step by Step
▸ **Step 1: Browser cache check**
  ↳ Browsers cache recent lookups (Chrome holds them for ~60 seconds).
▸ **Step 2: OS cache check**
  ↳ If browser misses, the OS resolver cache is checked next.
▸ **Step 3: Recursive resolver**
  ↳ If still no hit, the OS asks the configured recursive resolver (ISP / 8.8.8.8 / 1.1.1.1).
▸ **Step 4: Iterative climb**
  ↳ Recursive resolver asks Root -> TLD -> Authoritative, walking the hierarchy.
▸ **Step 5: Answer returned and cached**
  ↳ The IP is sent back to the OS and browser; each layer caches it for the TTL duration.
📊 Numbered flow diagram. Browser -> OS -> Recursive Resolver. Then resolver branches to Root -> TLD -> Authoritative with arrows ...

## Slide 77
Recursive vs Iterative Queries
▸ **Recursive query (client to resolver)**
  ↳ "Give me the final answer or fail." The resolver is responsible for doing all the work.
▸ **Iterative query (resolver to nameservers)**
  ↳ "Tell me what you know, or who to ask next." The resolver climbs the tree.
▸ **Why this split exists**
  ↳ Clients are simple; resolvers are smart and well-cached. Splitting work keeps end devices lightweight.
▸ **Performance implication**
  ↳ The first lookup may take 20-120ms; subsequent lookups within the TTL window are sub-millisecond from cache.
▸ **Real example**
  ↳ When you visit youtube.com, your laptop sends 1 recursive query; the resolver may send 3-4 iterative queries upstream.
📊 Two boxes side by side. Left "Recursive": single double-headed arrow between client and resolver labeled "Do everything". Right...

## Slide 78
DNS Resolution Diagram - End-to-End Flow
▸ **Components**
  ↳ Stub resolver (OS), Recursive resolver, Root server, TLD server, Authoritative nameserver, Origin web server.
▸ **Arrow walkthrough**
  ↳ 1: Stub -> Recursive ("What is www.example.com?")
  ↳ 2: Recursive -> Root (".") returns "Ask .com TLD at 192.x.x.x"
  ↳ 3: Recursive -> .com TLD returns "Ask ns1.example.com"
  ↳ 4: Recursive -> ns1.example.com returns "93.184.216.34"
  ↳ 5: Recursive -> Stub returns final IP; browser opens TCP to origin.
▸ **Caching at every hop**
  ↳ Each layer (browser, OS, resolver) stores results until TTL expires.
▸ **Failure modes**
  ↳ If any nameserver in the chain is down, resolution fails or falls back to a secondary NS.
▸ **Total time budget**
  ↳ Cold cache: 50-200ms. Warm cache: <1ms.
📊 Horizontal flow with 6 boxes left-to-right: User -> Stub -> Recursive Resolver. From the Recursive Resolver, three vertical arr...

## Slide 79
DNS Record Types - A and AAAA
▸ **A record (Address record)**
  ↳ Maps a hostname to an IPv4 address. Example: example.com A 93.184.216.34.
▸ **AAAA record (quad-A)**
  ↳ Maps a hostname to an IPv6 address. Example: example.com AAAA 2606:2800:220:1:248:1893:25c8:1946.
▸ **Why both exist**
  ↳ The internet is mid-migration from IPv4 (4.3B addresses, exhausted) to IPv6 (340 undecillion addresses).
▸ **Dual-stack behavior**
  ↳ Modern OSes prefer AAAA when available, fall back to A. Hence websites publish both.
▸ **Real-world example**
  ↳ Run `dig google.com A` and `dig google.com AAAA` - you will see both populated.
📊 Two-column table. Column 1: "A Record" with sample row "example.com -> 93.184.216.34". Column 2: "AAAA Record" with sample row ...

## Slide 80
DNS Record Types - CNAME, MX, NS, TXT
▸ **CNAME (Canonical Name)**
  ↳ An alias from one hostname to another. Example: www.example.com CNAME example.com.
  ↳ Used heavily in CDNs: yourapp.com CNAME d123.cloudfront.net.
▸ **MX (Mail Exchange)**
  ↳ Tells email senders which server handles mail for this domain. Has priority values.
  ↳ Example: example.com MX 10 mail.example.com.
▸ **NS (Nameserver)**
  ↳ Identifies which authoritative nameservers are responsible for the domain.
  ↳ Example: example.com NS ns-1.awsdns-01.org.
▸ **TXT records**
  ↳ Free-form text. Used for SPF, DKIM, domain ownership verification (Google Search Console).
▸ **Other notable types**
  ↳ PTR (reverse DNS), SRV (service discovery), CAA (certificate authority authorization), SOA (zone metadata).
📊 A table with columns "Type | Purpose | Example". Five rows: A, CNAME, MX, NS, TXT each filled with the example values from the ...

## Slide 81
TTL - Time To Live
▸ **What TTL is**
  ↳ A number (in seconds) attached to every DNS record telling resolvers how long they may cache the answer.
▸ **Common TTL values**
  ↳ 60s (rapid failover scenarios), 300s (standard SaaS), 3600s (typical website), 86400s (rarely-changing infrastructure like NS records).
▸ **The trade-off**
  ↳ Low TTL = faster propagation of changes, but more queries hit your authoritative server (cost + load).
  ↳ High TTL = better cache hit ratio + lower cost, but slow to propagate changes during incidents.
▸ **Pre-migration practice**
  ↳ Drop TTL to 60s a day before a planned IP change so old entries expire fast; raise it back afterward.
▸ **Real example**
  ↳ Cloudflare uses ~300s by default; AWS Route 53 lets you set anything from 0 to 172800s.
📊 Slider graphic - left end "Low TTL (60s)" labeled "Fast change, high cost"; right end "High TTL (24h)" labeled "Slow change, lo...

## Slide 82
DNS Caching - Why It Saves the Internet
▸ **Caching happens at every layer**
  ↳ Browser, OS, recursive resolver, sometimes corporate DNS proxies.
▸ **Cache hit ratio is enormous**
  ↳ For popular domains like google.com, ~99% of lookups never reach the authoritative server.
▸ **Why this is essential**
  ↳ Without caching, root servers would be flooded billions of times per second; the internet would buckle.
▸ **Negative caching**
  ↳ "NXDOMAIN" (does not exist) responses are also cached, controlled by the SOA record's minimum TTL.
▸ **Cache poisoning risk**
  ↳ Attackers historically injected fake records into resolver caches; mitigated by DNSSEC and source port randomization.
📊 Layered cake diagram. Bottom layer "Authoritative NS" (small slice). Above it "Recursive Resolver" (larger). Above "OS Cache" (...

## Slide 83
Round Robin DNS - Load Balancing for Free
▸ **What it is**
  ↳ Configure multiple A records for the same hostname. Resolvers rotate which IP they return.
  ↳ Example: api.example.com -> 1.2.3.4, 1.2.3.5, 1.2.3.6 (rotates each query).
▸ **Why it works as a load balancer**
  ↳ Different clients hit different servers, distributing load roughly evenly.
▸ **No infrastructure needed**
  ↳ Pure DNS feature; no L4/L7 load balancer required.
▸ **Limitations**
  ↳ No health checking - if a server is down, DNS still hands out its IP.
  ↳ Caching defeats round-robin: a client may stick to the first IP for the TTL duration.
▸ **Real-world use**
  ↳ Often used as a coarse first layer in front of actual load balancers (DNS round-robin -> regional ALB -> instances).
📊 One DNS server icon with three outgoing arrows to three web servers. Three client icons each receive a different IP, each conne...

## Slide 84
GeoDNS and Latency-Based Routing
▸ **GeoDNS = answer based on requester's geography**
  ↳ Same hostname returns different IPs depending on where you ask from.
  ↳ Example: example.com from Mumbai -> 13.x.x.x (ap-south-1); from Frankfurt -> 18.x.x.x (eu-central-1).
▸ **How the resolver knows your location**
  ↳ Source IP of the recursive resolver, or EDNS Client Subnet (ECS) which forwards a portion of the client IP.
▸ **Latency-based routing**
  ↳ Service measures real-world latency from each region and returns the lowest-latency endpoint, not just the geographically closest.
▸ **Why "closest" is not always "fastest"**
  ↳ Internet routing is messy; a peering link from Sydney to Singapore may beat Sydney to Tokyo even if Tokyo is closer.
▸ **Provider examples**
  ↳ AWS Route 53 (geolocation, geoproximity, latency policies), Cloudflare Load Balancing, NS1, Google Cloud DNS.
📊 World map with three users (NYC, London, Tokyo). Arrows from each user to the nearest data center icon (Virginia, Ireland, Toky...

## Slide 85
DNS-Based Load Balancing - Intuition and Analogy
▸ **Pizza chain analogy**
  ↳ Call 1-800-PIZZA from NYC, you reach the NYC store; call from LA, you reach the LA store. Same number, different store, based on where you called from.
▸ **DNS = the call routing system**
  ↳ It does the geographic dispatch; the actual order/cooking happens at the local store (origin server).
▸ **Combined strategy**
  ↳ Production stacks usually layer: GeoDNS -> Regional Load Balancer -> Service Mesh -> Pod.
▸ **Why DNS is a coarse tool**
  ↳ Granularity is "per resolver" not "per request". Real fine-grained balancing happens at L4/L7 LBs.
▸ **Failover via DNS**
  ↳ Health-checking DNS providers (Route 53, NS1) remove unhealthy IPs from rotation, but propagation depends on TTL.
📊 A user calling a phone with a speech bubble "1-800-PIZZA". Three branching arrows to NYC, LA, Chicago store icons. Caption "Sam...

## Slide 86
DNS Trade-offs and Pitfalls
▸ **TTL vs agility**
  ↳ You cannot fail over faster than the smallest TTL clients are honoring.
▸ **Caching is mostly out of your control**
  ↳ Misbehaving resolvers and browsers may ignore your TTL.
▸ **DNS is UDP-first (port 53)**
  ↳ Default 512-byte limit; larger responses fall back to TCP or use EDNS0.
▸ **Single point of failure if mismanaged**
  ↳ The 2016 Dyn DDoS took down Twitter, Reddit, GitHub. Use multiple DNS providers (multi-NS strategy).
▸ **Security concerns**
  ↳ DNS hijacking, cache poisoning, DNS-over-cleartext eavesdropping. Mitigations: DNSSEC, DNS-over-HTTPS (DoH), DNS-over-TLS (DoT).
📊 A table with columns "Concern | Symptom | Mitigation". Rows: TTL too high (slow failover -> drop pre-change), TTL too low (cost...

## Slide 87
PART B: CDN (Content Delivery Network)

## Slide 88
What is a CDN? - Concept Introduction
▸ **CDN = Content Delivery Network**
  ↳ A globally distributed network of servers that cache and serve content from locations physically near end users.
▸ **The core problem it solves**
  ↳ Speed of light is fixed (~200,000 km/s in fiber). Sydney to Virginia round-trip is ~250ms minimum.
  ↳ Serving a Sydney user from Sydney instead of Virginia turns 250ms into 5ms.
▸ **What CDNs serve**
  ↳ Static assets (images, CSS, JS, video segments), dynamic content (with smart caching), and increasingly compute (edge functions).
▸ **Warehouse analogy**
  ↳ Amazon does not ship every order from Seattle; they place warehouses near population centers. CDNs do the same for bytes.
▸ **Origin protected by edges**
  ↳ The origin server (your real backend) only sees a fraction of traffic - the cache misses.
📊 Globe with a single "Origin" server icon centered, surrounded by ~15 smaller "Edge" server icons distributed across continents....

## Slide 89
Why CDNs Exist - The Latency Problem
▸ **Physics has a hard floor**
  ↳ A packet from London to Sydney crosses ~17,000 km. At light-speed-in-fiber, that is ~85ms one-way, ~170ms RTT - before any compute.
▸ **TCP and TLS amplify it**
  ↳ TCP handshake (1 RTT) + TLS handshake (1-2 RTTs) + HTTP request/response (1 RTT) = 4-5 RTTs before first byte.
▸ **Bandwidth alone does not save you**
  ↳ You can have 1 Gbps and still wait 200ms because latency is independent of bandwidth.
▸ **Real impact on UX and business**
  ↳ Amazon found 100ms of latency cost them 1% in sales. Google saw 20% drop in traffic with 500ms slower search.
▸ **CDN compresses the distance**
  ↳ By moving content close to users, you cut RTTs from hundreds of ms to single digits.
📊 World map with two scenarios. Top: User in Sydney, line to Virginia origin labeled "250ms RTT, 4 RTTs = 1 second". Bottom: same...

## Slide 90
How CDNs Work - Architecture Deep Dive
▸ **PoP (Point of Presence)**
  ↳ A physical location (data center, ISP rack) hosting CDN edge servers. Cloudflare has 300+ PoPs globally.
▸ **Edge server**
  ↳ The cache node a user actually connects to. Holds copies of frequently-requested content.
▸ **Origin server**
  ↳ Your application's source of truth - the backend the CDN pulls from on a cache miss.
▸ **Mid-tier / shield cache**
  ↳ An intermediate caching layer between edges and origin to reduce origin load further (Fastly's "shielding", Cloudflare's "Tiered Cache").
▸ **Anycast routing**
  ↳ The same IP advertised from many PoPs; BGP routes the user to the topologically nearest one automatically.
📊 Three-layer pyramid. Top: "Origin (1 location)". Middle: "Shield/Mid-tier (5-10 locations)". Bottom: "Edge PoPs (100s of locati...

## Slide 91
CDN Request Flow - Step by Step
▸ **Step 1: User DNS lookup**
  ↳ assets.example.com resolves to a CDN-managed IP via CNAME or ALIAS.
▸ **Step 2: Anycast routes to nearest edge**
  ↳ User's TCP/TLS connection terminates at the closest PoP - often within 10-30ms.
▸ **Step 3: Edge cache lookup**
  ↳ Edge checks its cache using the URL + headers as the cache key.
▸ **Step 4a: Cache hit (the common case)**
  ↳ Content served from RAM/SSD on the edge in single-digit ms.
▸ **Step 4b: Cache miss**
  ↳ Edge fetches from origin (possibly through shield), stores it locally, returns to user. Subsequent requests hit cache.
📊 Horizontal flow: User -> Edge PoP. From Edge, two paths: green path "HIT - return cached" (loops back to user), red path "MISS ...

## Slide 92
Push CDN vs Pull CDN
▸ **Pull CDN (lazy, default)**
  ↳ Edge fetches content from origin on first request, caches it, serves subsequent requests.
  ↳ First user pays the latency cost; everyone after benefits.
  ↳ Used by: most web assets, blog images, JS bundles. CloudFront, Cloudflare default behavior.
▸ **Push CDN (eager, manual)**
  ↳ You upload content directly to the CDN; nothing is fetched from origin on demand.
  ↳ You control exactly what is on the edge and when.
  ↳ Used by: very large files, video downloads, software releases, infrequently-changed assets.
▸ **When to choose pull**
  ↳ High-volume, frequently-updated, or unpredictable content. Lower operational overhead.
▸ **When to choose push**
  ↳ Large files (multi-GB game patches), low-traffic but business-critical assets (you do not want the first user to wait), strict cache control.
▸ **Hybrid is common**
  ↳ Big platforms push the "must be hot" content and let everything else pull on demand.
📊 Two side-by-side diagrams. Left "Pull": user requests -> edge -> miss -> origin (arrow on demand). Right "Push": developer uplo...

## Slide 93
CDN Caching Mechanics
▸ **Cache key**
  ↳ Usually URL + selected headers (Vary: Accept-Encoding etc). Two URLs differing by query string may or may not share a key.
▸ **Cache-Control headers drive behavior**
  ↳ max-age, s-maxage, public/private, no-cache, no-store, stale-while-revalidate.
▸ **TTL on the edge**
  ↳ How long the edge serves a copy before checking origin again. Independent from browser's max-age.
▸ **Cache invalidation**
  ↳ Purge by URL, by tag (Fastly surrogate keys), or by wildcard. CloudFront invalidations cost money beyond a free quota.
▸ **Cache hit ratio is the key metric**
  ↳ 90%+ is typical for well-tuned static content; below 70% means you are mostly proxying, not caching.
📊 A cache entry box with fields "Key: /img/logo.png", "Value: <bytes>", "TTL: 86400s", "Tags: [logo, branding]". Arrows show "pur...

## Slide 94
CDN Benefits - Why Everyone Uses Them
▸ **Reduced latency**
  ↳ Single-digit ms TTFB versus hundreds of ms to a far origin. Massive UX win.
▸ **Reduced origin load**
  ↳ 95%+ of requests served from edges; your origin handles only the long tail and writes.
▸ **Bandwidth cost reduction**
  ↳ CDN egress is often cheaper per GB than cloud-origin egress, especially at scale.
▸ **DDoS absorption and WAF**
  ↳ CDNs absorb volumetric attacks across their global capacity (Cloudflare's network is multiple Tbps). Built-in WAFs filter malicious requests.
▸ **TLS termination and modern protocols**
  ↳ CDNs handle HTTP/2, HTTP/3, QUIC, and modern TLS for you; your origin can stay on HTTP/1.1 if you want.
📊 Five-icon row: stopwatch (latency), shield (DDoS), down-arrow (origin load), dollar sign (cost), padlock (TLS). Each labeled wi...

## Slide 95
CDN Trade-offs and Limitations
▸ **Stale content risk**
  ↳ Aggressive caching can serve outdated content; need careful invalidation strategy.
▸ **Cache invalidation complexity**
  ↳ "There are only two hard things in CS: cache invalidation and naming." CDNs make this real.
▸ **Cost at scale**
  ↳ For small sites, CDNs are cheap or free. At petabyte scale, CDN bills become significant - bandwidth, requests, and feature pricing.
▸ **Limited dynamic content acceleration**
  ↳ Personalized or rapidly-changing data is harder to cache; needs ESI, edge compute, or smart cache keys.
▸ **Vendor lock-in and debugging complexity**
  ↳ CDN-specific features (workers, surrogate keys) tie you to one provider. An extra layer between users and your code makes debugging harder (mystery 5xx from edge, regional cache poisoning).
📊 Balance scale icon. Left pan heavy with "Speed, Scale, Security". Right pan also non-trivial with "Staleness, Cost, Complexity,...

## Slide 96
CDN Architecture Diagram - Global Picture
▸ **Components labeled**
  ↳ Origin (1 region), Shield PoP (regional), Edge PoPs (global), Anycast IP, Authoritative DNS.
▸ **Arrow walkthrough**
  ↳ User -> DNS -> Anycast IP -> nearest Edge PoP.
  ↳ Edge -> (on miss) Shield PoP -> (on miss) Origin.
  ↳ Origin -> Shield -> Edge -> User. Cached at every layer on the way back.
▸ **Labels to include**
  ↳ "Cache hit ratio 95%+", "Anycast BGP routing", "TLS terminated at edge", "Origin sees only ~5% of requests".
▸ **Failure isolation**
  ↳ If one PoP fails, BGP withdraws the route; users automatically reroute to the next-closest PoP.
▸ **Real-world scale**
  ↳ Cloudflare: 300+ cities, 13,000+ networks. Akamai: 4,000+ PoPs in 130+ countries.
📊 World map. Single origin pin in us-east-1. Five shield pins (one per continent). 30+ small edge dots scattered globally. Sample...

## Slide 97
Real-World CDN Providers
▸ **Amazon CloudFront**
  ↳ Tightly integrated with AWS (S3, ALB, Lambda@Edge). Pay-per-use, 450+ PoPs. Good default for AWS shops.
▸ **Cloudflare**
  ↳ Massive free tier, security-first (WAF, bot mitigation, DDoS), Workers for edge compute, very developer-friendly.
▸ **Akamai**
  ↳ The original CDN (1998). Enterprise-grade, deepest PoP coverage, expensive, used by banks, airlines, governments.
▸ **Fastly**
  ↳ Programmable VCL config, instant purge (sub-150ms globally), favored by news sites, GitHub, Shopify, Stripe.
▸ **Others worth knowing**
  ↳ Google Cloud CDN, Azure Front Door, Bunny.net (low-cost), KeyCDN, StackPath.
📊 Logo collage of CloudFront, Cloudflare, Akamai, Fastly, Google Cloud CDN, Azure Front Door. Each logo annotated with a one-line...

## Slide 98
When NOT to Use a CDN
▸ **Internal-only services**
  ↳ VPN-protected admin tools have no need for global edges; just adds cost and complexity.
▸ **Highly personalized, uncacheable responses**
  ↳ If every response varies per user (private dashboards), only the connection acceleration helps; content caching does not.
▸ **Compliance / data residency restrictions**
  ↳ Some regulations (GDPR for sensitive data, certain government data) require data to stay in-region; global CDN may complicate this.
▸ **Tiny scale and tight budget**
  ↳ For a hobby blog with 100 visitors/day, CDN setup may not be worth the operational overhead - though free tiers (Cloudflare) often make this moot.
▸ **WebSockets / long-lived connections**
  ↳ Some CDNs support them, some do not. Validate before assuming.
📊 Red "X" icons next to four scenarios: laptop labeled "internal admin", user with personalized dashboard, lock-in-region icon, t...

## Slide 99
PART C: Section Wrap-Up

## Slide 100
Key Takeaways
▸ **DNS is the internet's phone book**
  ↳ Hierarchical, distributed, cache-heavy. TTL controls the agility/cost trade-off.
▸ **DNS doubles as a coarse load balancer**
  ↳ Round-robin, GeoDNS, and latency-based routing steer users before any HTTP request.
▸ **CDNs eliminate distance**
  ↳ Edge PoPs near users turn cross-continent latency into local-loop speed.
▸ **Pull CDN is the default; push for big-or-critical**
  ↳ Pull is lazy and easy. Push is deliberate and pre-warmed.
▸ **Both are infrastructure leverage**
  ↳ Set them up once, get speed, scale, security, and cost wins for the lifetime of the service.
📊 5-point checklist with green checkmarks. Each point in one short line. At bottom, two icons: phone book (DNS) + warehouse netwo...

## Slide 101
Interview Tips - DNS and CDN
▸ **Always mention DNS in your design**
  ↳ "Users hit our domain via DNS, which routes them via GeoDNS to the nearest region." Sets the stage.
▸ **Pair CDN with static assets early**
  ↳ As soon as your design has images, JS, or video, propose a CDN. Interviewers expect it.
▸ **Speak in record types**
  ↳ Drop "A record", "CNAME", "TTL" naturally. Shows depth without being pretentious.
▸ **Discuss TTL trade-offs concretely**
  ↳ "I would use a 60s TTL for failover-critical records and 1 hour for stable assets."
▸ **Know one provider deeply**
  ↳ Pick CloudFront, Cloudflare, or Fastly. Be able to discuss its quirks (CloudFront invalidation cost, Cloudflare Workers cold-start absence, Fastly instant purge).
📊 Numbered list 1-5 styled as an interview cheat-sheet card. Optional: speech bubble with the phrase "users hit our domain via DN...

## Slide 102
Common Pitfalls
▸ **Setting TTL too high before a migration**
  ↳ You announce a new IP but old IP is cached for hours; users see outages. Lower TTL ahead of time.
▸ **Forgetting that browsers and resolvers may ignore TTL**
  ↳ Some browsers cap at 60s; some resolvers extend silently. Plan for it - do not assume strict TTL adherence.
▸ **Treating round-robin DNS as a real load balancer**
  ↳ No health checks, sticky caching - traffic is not even, and dead servers stay in rotation. Use a proper LB.
▸ **Caching authenticated content publicly**
  ↳ Setting Cache-Control: public on a logged-in user's page leaks data to other users. Always scope cache keys correctly.
▸ **Forgetting cache invalidation strategy**
  ↳ "Just cache forever" works until you ship a bad CSS file. Plan purge by URL, tag, or version-in-path (logo.v23.png).
▸ **Single DNS provider risk**
  ↳ 2016 Dyn outage took down half the internet. Use secondary DNS (Route 53 + NS1, or Cloudflare + Dyn).
📊 Six warning-sign icons in a 2x3 grid. Each annotated with a one-line pitfall. Bold red border. Title: "Avoid these in your desi...

## Slide 103
Section Summary - DNS + CDN as a Team
▸ **Together they form the front door of every modern app**
  ↳ DNS picks the right region; CDN serves bytes from the closest edge. Origin handles only the rare/unique work.
▸ **They are the cheapest performance wins available**
  ↳ No code changes, just configuration. ROI is enormous.
▸ **They are also the most common single points of failure**
  ↳ Lose your DNS or your CDN, lose your service. Plan redundancy.
▸ **They unlock global scale**
  ↳ A two-engineer startup can serve users in 100 countries with the same tooling Netflix uses.
▸ **Up next**
  ↳ Section 4: Load Balancers - how requests are distributed once they arrive in your data center.
📊 Two icons (phone book + warehouse) merging into a single shield icon labeled "Front door of the internet". Arrow pointing forwa...

## Slide 104
Section 4: Load Balancers and Reverse Proxies

## Slide 105
Section Overview
▸ What this section covers
  ↳ Load balancers: distributing traffic across many backend servers
  ↳ Reverse proxies: front-door servers that mediate client-server communication
  ↳ Algorithms, configurations, and trade-offs that real systems use
▸ Why it matters
  ↳ Almost every scaled system sits behind an LB and/or reverse proxy
  ↳ Interview staple: "How does traffic reach your service?" expects this knowledge
▸ Mental model
  ↳ LB = traffic cop directing cars to open lanes
  ↳ Reverse proxy = receptionist that screens, redirects, and logs every visitor
📊 Title slide with a network diagram showing clients -> LB/Proxy -> pool of app servers

## Slide 106
What is a Load Balancer?
▸ Definition
  ↳ A device or software that distributes incoming network traffic across multiple backend servers
  ↳ Sits between clients and the server pool, presenting a single endpoint (one IP/DNS name)
▸ Why it exists
  ↳ A single server has finite CPU, memory, and bandwidth; eventually it tips over
  ↳ Horizontal scaling (more servers) only works if traffic is shared evenly
▸ The two jobs of an LB
  ↳ Distribute load so no single server is overwhelmed
  ↳ Detect and route around unhealthy servers automatically
📊 Many client icons -> single LB box -> fan-out to N server icons

## Slide 107
Why You Need a Load Balancer
▸ Scalability
  ↳ Add or remove servers without changing the public endpoint
  ↳ Linear capacity increase as you add backends (in theory)
▸ High availability
  ↳ If one backend dies, the LB stops sending traffic to it; users feel nothing
  ↳ Enables zero-downtime deploys via rolling restarts
▸ Performance and flexibility
  ↳ Route requests intelligently (by region, content type, user)
  ↳ Offload expensive work like SSL termination from app servers
▸ Real-world analogy
  ↳ Grocery store checkout: a single line that feeds whichever cashier opens up next, instead of choosing a lane and getting stuck behind the price-check
📊 Side-by-side - left: 1 server crushed by traffic; right: LB spreading load to 4 healthy servers

## Slide 108
Layer 4 vs Layer 7 Load Balancing - Concept
▸ The OSI model in one breath
  ↳ Layer 4 = Transport (TCP/UDP, IP addresses, ports)
  ↳ Layer 7 = Application (HTTP, gRPC, headers, cookies, URLs)
▸ Layer 4 LB
  ↳ Forwards packets based on IP and port without inspecting payload
  ↳ Fast, cheap, protocol-agnostic
▸ Layer 7 LB
  ↳ Reads the HTTP request and routes based on URL path, headers, cookies, method
  ↳ Smarter but more CPU-intensive
📊 OSI stack with L4 and L7 highlighted, plus an HTTP request being inspected at L7

## Slide 109
Layer 4 Load Balancing - Deep Dive
▸ How it works
  ↳ Operates at the TCP/UDP level; sees source/dest IP and port
  ↳ Performs NAT (Network Address Translation) to forward connections to backends
  ↳ One TCP connection from client maps to one TCP connection to backend
▸ Strengths
  ↳ Very fast, low latency (minimal processing per packet)
  ↳ Works for any TCP/UDP protocol: databases, game servers, MQTT, raw sockets
  ↳ Lower CPU and memory footprint
▸ Limitations
  ↳ Cannot route based on URL or HTTP headers
  ↳ Cannot terminate SSL or inspect content
  ↳ Sticky sessions limited to source IP (coarse)
▸ Examples
  ↳ AWS Network Load Balancer (NLB), HAProxy in TCP mode, IPVS, Linux LVS
📊 Packet flow diagram showing IP/port headers being read and forwarded as opaque bytes

## Slide 110
Layer 7 Load Balancing - Deep Dive
▸ How it works
  ↳ Terminates the client TCP connection, parses HTTP, then opens a new connection to backend
  ↳ Can read URL path, query string, headers, cookies, body
▸ Smart routing examples
  ↳ `/api/*` -> API server pool, `/static/*` -> CDN/static pool, `/admin/*` -> admin pool
  ↳ Route mobile clients to mobile-optimized backend via User-Agent header
  ↳ A/B testing by routing 10% of users to a canary pool based on cookie
▸ Bonus features unlocked
  ↳ SSL/TLS termination, response caching, compression, request rewriting
  ↳ Authentication, rate limiting, web application firewall (WAF)
▸ Examples
  ↳ AWS Application Load Balancer (ALB), Nginx, HAProxy in HTTP mode, Envoy, Traefik
📊 HTTP request being parsed; arrows splitting based on `/api`, `/static`, `/admin` paths

## Slide 111
L4 vs L7 - When to Use Which
▸ Use Layer 4 when
  ↳ Maximum throughput and lowest latency are critical
  ↳ Protocol is non-HTTP (databases, custom TCP, UDP gaming)
  ↳ You don't need content-based routing
▸ Use Layer 7 when
  ↳ You need URL/header-based routing or microservice routing
  ↳ SSL termination, caching, or WAF features are required
  ↳ Cost of extra CPU is acceptable for the flexibility gained
▸ Common pattern
  ↳ L4 LB in front of L7 LB: NLB -> ALB -> services (gets DDoS resilience + smart routing)
▸ Quick rule of thumb
  ↳ HTTP/HTTPS service? Default to L7. Anything else? Default to L4.
📊 Decision tree - "Is it HTTP?" yes->L7, no->L4; "Need content routing?" yes->L7, no->L4

## Slide 112
Load Balancing Algorithms - Why They Matter
▸ The core question
  ↳ Given an incoming request and N healthy backends, which backend gets it?
▸ Why it's not trivial
  ↳ Servers may have different capacities (old vs new hardware)
  ↳ Requests have wildly different costs (a search vs a static asset)
  ↳ Some requests need to land on the same server (session state)
▸ Categories of algorithms
  ↳ Stateless rotation: Round Robin, Random
  ↳ Capacity-aware: Weighted Round Robin
  ↳ Load-aware: Least Connections, Least Response Time
  ↳ Affinity-aware: IP Hash, Sticky Sessions
📊 6 algorithm icons in a 2x3 grid with one-line descriptions

## Slide 113
Round Robin
▸ How it works
  ↳ Send request 1 to server A, request 2 to B, request 3 to C, then back to A
  ↳ Pure rotation; no awareness of load or capacity
▸ Why it exists
  ↳ Simplest possible distribution; trivial to implement (just a counter)
  ↳ Works well when servers are identical and requests are similar in cost
▸ When to use
  ↳ Homogeneous server pool, short-lived stateless requests (e.g., simple REST APIs)
  ↳ Default starting point if you have no other information
▸ Pitfalls
  ↳ Ignores actual server load - one slow request on server A doesn't stop A from getting more
  ↳ Bad fit for variable request costs (some servers can pile up while others are idle)
📊 Circular arrow cycling A -> B -> C -> A with sequential request numbers

## Slide 114
Weighted Round Robin
▸ How it works
  ↳ Assign each server a weight; higher weight = more requests
  ↳ Example: A=3, B=2, C=1 means 6-request cycle goes A,A,A,B,B,C
▸ Why it exists
  ↳ Real fleets are heterogeneous: a 32-core box can handle more than an 8-core box
  ↳ Lets you mix instance sizes during migrations or capacity ramps
▸ When to use
  ↳ Mixed hardware generations, gradual rollouts (give canary 1%, prod 99%)
  ↳ Different cloud regions/zones with different capacities
▸ Pitfalls
  ↳ Weights are static; if server B suddenly slows down, weights don't auto-adjust
  ↳ Operators forget to update weights after hardware changes
📊 Three buckets sized 3x, 2x, 1x with balls falling into them proportionally

## Slide 115
Least Connections
▸ How it works
  ↳ Track the number of active connections per backend; send new request to the server with fewest
▸ Why it exists
  ↳ Long-lived or variable-duration requests cause uneven load with Round Robin
  ↳ "Connections in flight" is a cheap proxy for "current load"
▸ When to use
  ↳ Long-lived connections: WebSockets, database pools, streaming endpoints
  ↳ Variable request durations (some endpoints take 50ms, others 5s)
▸ Pitfalls
  ↳ Connection count != actual CPU work (one heavy request can starve a "lightly loaded" server)
  ↳ LB must track connection state, slightly more overhead than Round Robin
📊 Three servers with connection counts 7, 3, 5; new request arrow points to the "3" server

## Slide 116
Least Response Time
▸ How it works
  ↳ Track each server's recent average response latency; pick the fastest responder
  ↳ Often combined with Least Connections (pick lowest of: connections * avg_latency)
▸ Why it exists
  ↳ Latency directly reflects user experience and true server health
  ↳ Catches partially degraded servers that still accept connections but respond slowly
▸ When to use
  ↳ Latency-sensitive APIs, user-facing endpoints
  ↳ Heterogeneous workloads where some servers might be GC-pausing or thrashing
▸ Pitfalls
  ↳ Requires continuous latency measurement, more LB CPU
  ↳ Can oscillate ("herd" toward a fast server until it gets overloaded)
📊 Three servers showing 50ms, 200ms, 80ms; arrow goes to 50ms one

## Slide 117
IP Hash and Sticky Sessions
▸ How IP Hash works
  ↳ Hash the client IP address; map hash to a backend server
  ↳ Same client IP -> same server (deterministic)
▸ How Sticky Sessions work (L7)
  ↳ LB sets or reads a cookie (e.g., `AWSALB`); same cookie -> same backend
▸ Why they exist
  ↳ When servers store session state in memory, the user must come back to the same one
  ↳ Avoids needing a shared session store (Redis) for simple apps
▸ When to use
  ↳ Legacy stateful apps, in-memory session caches
  ↳ WebSocket connections (you want subsequent messages to land on the same server)
▸ Pitfalls
  ↳ Uneven distribution if a few clients are very heavy (NAT, mobile carriers behind one IP)
  ↳ Server failure loses that user's session entirely
  ↳ Anti-pattern in modern microservices - prefer stateless services with external session store
📊 Hash function mapping IP 1.2.3.4 -> Server B consistently across multiple requests

## Slide 118
Random
▸ How it works
  ↳ Pick a backend uniformly at random for each request
▸ Why it exists
  ↳ Stateless, requires no counters or coordination
  ↳ Statistically converges to even distribution at high request volume
▸ When to use
  ↳ Very high QPS, stateless services where simplicity matters
  ↳ Distributed LBs that can't share state (each instance can pick independently)
▸ Variant: "Power of Two Choices"
  ↳ Pick 2 random servers, send to whichever has fewer connections
  ↳ Surprisingly close to optimal Least Connections, with minimal state
▸ Pitfalls
  ↳ Can produce short-term hotspots due to randomness
  ↳ Less predictable than Round Robin for debugging
📊 Dice rolling and selecting a server from a fan; second panel shows "pick 2, choose the lighter"

## Slide 119
Algorithm Selection Cheat Sheet
▸ Identical servers, short requests -> Round Robin
▸ Mixed hardware or canary deploys -> Weighted Round Robin
▸ Long-lived connections (WebSocket, DB pool) -> Least Connections
▸ Latency-critical user-facing API -> Least Response Time
▸ Stateful session-in-memory app -> IP Hash / Sticky Sessions
▸ Massively parallel stateless service -> Random or Power of Two Choices
▸ Don't know yet?
  ↳ Start with Round Robin, measure, then refine
📊 Decision matrix table with workload characteristics on rows and algorithms on columns

## Slide 120
Load Balancing Algorithm - Real Example
▸ Scenario: e-commerce site on Black Friday
  ↳ 5 app servers (3 new powerful boxes, 2 older boxes), HTTP traffic
  ↳ Some requests are 50ms (browse), some are 3s (checkout/payment)
▸ Naive Round Robin
  ↳ Older boxes get same share as new ones -> they slow down -> users wait
▸ Weighted + Least Connections combo
  ↳ Weights: new=3, old=1; tiebreak by least active connections
  ↳ New servers absorb more load; if new server is mid-checkout, the next request goes elsewhere
▸ Result
  ↳ Even latency across the fleet, no single hotspot
📊 Timeline showing requests flowing; old vs new servers; healthy traffic curves

## Slide 121
Hardware vs Software Load Balancers
▸ Hardware LBs
  ↳ Dedicated physical appliances: F5 BIG-IP, Citrix ADC, A10
  ↳ Pros: extremely high throughput, custom ASICs, vendor support
  ↳ Cons: expensive ($$$), inflexible, slow to upgrade, vendor lock-in
▸ Software LBs
  ↳ Run on commodity servers/VMs/containers: Nginx, HAProxy, Envoy, Traefik
  ↳ Pros: cheap, elastic, scriptable, integrates with CI/CD
  ↳ Cons: you operate it; throughput limited by host hardware
▸ Cloud-managed LBs
  ↳ AWS ELB (ALB/NLB/GWLB), GCP Cloud Load Balancing, Azure Load Balancer
  ↳ Best of both: software-defined, elastic, managed by cloud provider
▸ Today's reality
  ↳ Software/cloud-managed dominates; hardware LBs survive in regulated/on-prem niches
📊 Three columns - hardware appliance icon, server with Nginx logo, cloud provider logos

## Slide 122
Load Balancer Examples in the Wild
▸ Nginx
  ↳ Originally a web server; excellent L7 LB and reverse proxy; huge open-source community
▸ HAProxy
  ↳ Specialist LB; battle-tested at extreme scale (Stack Overflow, GitHub used it heavily)
▸ AWS ELB family
  ↳ ALB (L7, HTTP/HTTPS, host/path routing), NLB (L4, ultra-low latency), GWLB (network appliances)
▸ Envoy
  ↳ Modern L7 proxy; powers service meshes (Istio, Consul Connect); rich observability
▸ Cloudflare Load Balancing
  ↳ Global anycast LB at the edge; geographic + health-based routing
📊 Logo grid with 1-line capability summary under each

## Slide 123
Active-Active Configuration
▸ How it works
  ↳ Two or more LBs handle live traffic simultaneously, each serving a fraction
  ↳ Clients reach them via DNS round robin, anycast, or virtual IPs
▸ Pros
  ↳ Full hardware utilization (no idle standby)
  ↳ Higher aggregate throughput
  ↳ Faster failover - peers already warm
▸ Cons
  ↳ More complex (state sync, session affinity coordination)
  ↳ Capacity planning must assume one node can fail and remaining must absorb load
▸ Common in
  ↳ Cloud-native deployments, anycast CDNs, large-scale ALB/NLB
📊 Two LB boxes both receiving traffic, both forwarding to shared backend pool

## Slide 124
Active-Passive Configuration
▸ How it works
  ↳ One LB (active) handles all traffic; second LB (passive) sits idle, ready to take over
  ↳ Failover via VRRP/keepalived virtual IP, or DNS update
▸ Pros
  ↳ Simpler mental model and configuration
  ↳ No state-sync complexity during normal operation
▸ Cons
  ↳ 50% of capacity is idle (wasted hardware)
  ↳ Failover takes seconds (VIP migration, ARP refresh, DNS TTL)
▸ Common in
  ↳ Traditional on-prem deployments, smaller setups, regulated environments
📊 Active LB with green check serving traffic; passive LB with grey "standby" badge waiting

## Slide 125
Disadvantages of Load Balancers
▸ Added complexity
  ↳ One more system to configure, monitor, secure, and patch
  ↳ Misconfiguration can break the entire fleet at once
▸ Single point of failure (if not redundant)
  ↳ The LB itself can crash; a single LB = entire site down
  ↳ Always deploy redundant LBs (active-active or active-passive)
▸ Latency overhead
  ↳ Every request makes an extra hop through the LB
  ↳ L7 inspection adds CPU time (header parsing, SSL termination)
▸ Cost
  ↳ Cloud LBs are billed per hour + per GB processed; high-traffic sites pay real money
▸ Debugging difficulty
  ↳ Adds a layer to trace through; client IP can get masked (need `X-Forwarded-For`)
📊 Red warning triangle with bullet list of risks; arrow showing extra hop adding latency

## Slide 126
Health Checks
▸ What they are
  ↳ Periodic probes the LB sends to each backend to verify it's alive and serving
  ↳ Unhealthy backends are removed from the rotation automatically
▸ Types of health checks
  ↳ TCP: can the LB open a TCP connection? (L4)
  ↳ HTTP: does GET `/health` return 200? (L7, smarter)
  ↳ Application-aware: check that DB connection works, dependencies are reachable
▸ Best practices
  ↳ Dedicated `/healthz` endpoint that exercises real dependencies
  ↳ Threshold-based: mark unhealthy after N consecutive failures (avoid flapping)
  ↳ Different intervals for different criticality (fast for prod, slower for staging)
▸ Pitfalls
  ↳ Health check that's too cheap returns 200 even when app is broken (false healthy)
  ↳ Health check that's too heavy adds load and can itself cause failures
📊 LB pinging 3 backends; one returns red X and is crossed off the rotation

## Slide 127
Connection Draining (Graceful Shutdown)
▸ The problem
  ↳ You need to remove a server from the pool (deploy, patch, scale-in)
  ↳ Killing it instantly drops in-flight requests -> users see errors
▸ How draining works
  ↳ Mark backend as "draining"; LB stops sending NEW connections to it
  ↳ Existing connections finish naturally up to a timeout (e.g., 30-300 seconds)
  ↳ After all connections close (or timeout), backend is fully removed
▸ Why it matters
  ↳ Zero-downtime deploys, rolling updates, auto-scale-in events
  ↳ Critical for long-lived connections (WebSockets, file uploads)
▸ Configuration knobs
  ↳ AWS: "deregistration delay" on target groups (default 300s)
  ↳ Nginx: `server ... down` directive after reload
  ↳ Kubernetes: `terminationGracePeriodSeconds` + `preStop` hook
📊 Server marked "draining" with hourglass; new arrows blocked, existing connections finishing

## Slide 128
Load Balancer - Architecture Diagram
▸ Components in the diagram
  ↳ Clients (browsers, mobile apps) on the left
  ↳ DNS pointing `api.example.com` to LB's public IP
  ↳ Two redundant LBs in active-active behind a virtual IP / anycast
  ↳ Backend pool of N app servers in private subnet
  ↳ Health check arrows from LB to each backend
  ↳ Monitoring/metrics pipe to Datadog/CloudWatch
▸ Flow labels
  ↳ 1: Client DNS lookup -> LB IP
  ↳ 2: Client TCP/TLS handshake terminates at LB
  ↳ 3: LB picks healthy backend per algorithm (e.g., least-conn)
  ↳ 4: LB opens connection to backend, proxies request
  ↳ 5: Response returns through LB to client
  ↳ 6: Periodic health checks (dotted lines) to all backends
📊 Full architecture diagram with the components and numbered flow labels above

## Slide 129
Load Balancer - Trade-offs
▸ Performance vs flexibility
  ↳ L4 = fast/dumb; L7 = smart/slower; pick based on need
▸ Cost vs availability
  ↳ Active-active = full capacity but complex; active-passive = simple but half-capacity idle
▸ Stickiness vs even distribution
  ↳ Sticky sessions help legacy apps but cause hot spots and lose state on failover
▸ Health-check sensitivity
  ↳ Aggressive checks catch failures fast but cause flapping; lax checks miss issues
▸ DIY vs managed
  ↳ Self-hosted (HAProxy/Nginx) = control + ops burden; cloud LB = convenience + cost + lock-in
📊 Five balance-scale icons, each showing one trade-off

## Slide 130
What is a Reverse Proxy?
▸ Definition
  ↳ A server that sits in front of one or more backend servers and forwards client requests to them
  ↳ Clients believe they're talking to the proxy; backends are hidden
▸ The "reverse" part
  ↳ Forward proxy: hides the CLIENT from the server (e.g., corporate proxy filtering employee web traffic)
  ↳ Reverse proxy: hides the SERVER from the client (the public-facing front door)
▸ Why "reverse"
  ↳ The direction of "who is being represented" is flipped vs a forward proxy
▸ Real-world analogy
  ↳ Reverse proxy = hotel concierge: you ask "I want room service," concierge calls the right department; you never deal with kitchen directly
📊 Two diagrams side by side - forward proxy (clients hidden) vs reverse proxy (server hidden)

## Slide 131
Forward Proxy vs Reverse Proxy
▸ Forward proxy
  ↳ Lives near the client; client explicitly configures it
  ↳ Use cases: corporate firewall, content filtering, anonymity (VPN-ish), caching outbound traffic
  ↳ Examples: Squid, corporate web proxies
▸ Reverse proxy
  ↳ Lives near the server; clients are unaware of backends
  ↳ Use cases: hide backend topology, SSL termination, caching, load balancing, security
  ↳ Examples: Nginx, HAProxy, Cloudflare, Apache mod_proxy
▸ One-line distinction
  ↳ Forward proxy = "I'll fetch the internet for you" (client-side)
  ↳ Reverse proxy = "I'll hand your request to the right server" (server-side)
📊 Two-panel diagram - forward proxy between many clients and the internet; reverse proxy between internet and many backend servers

## Slide 132
Reverse Proxy Benefits - SSL Termination
▸ What it is
  ↳ Reverse proxy holds the SSL/TLS certificates and decrypts HTTPS traffic at the edge
  ↳ Forwards plaintext (or re-encrypted) HTTP to backends inside the trusted network
▸ Why it matters
  ↳ SSL handshakes are CPU-intensive; centralizing them spares backend CPU
  ↳ One place to manage certificates, renewals, cipher suites (instead of N servers)
  ↳ Backends speak simple HTTP, easier to develop and debug
▸ Trade-off
  ↳ Internal traffic is plaintext unless you re-encrypt (zero-trust networks usually re-encrypt)
📊 HTTPS arrow from client to proxy (locked), HTTP arrow from proxy to backends (unlocked, inside private network bubble)

## Slide 133
Reverse Proxy Benefits - Caching
▸ What it is
  ↳ Proxy stores recent responses; future identical requests served from cache without hitting backend
▸ Why it matters
  ↳ Massive reduction in backend load (especially for static assets, API responses)
  ↳ Lower latency for users (cached response is microseconds)
▸ What to cache
  ↳ Static files (images, CSS, JS): cache for hours/days
  ↳ API responses with short TTL (10-60 seconds) for dashboards and feeds
  ↳ Respect HTTP cache headers (`Cache-Control`, `ETag`, `Vary`)
▸ Real-world
  ↳ Nginx with `proxy_cache`, Varnish, Cloudflare edge cache
📊 First request goes through proxy to backend (slow); second request returns from proxy cache (fast)

## Slide 134
Reverse Proxy Benefits - Compression and Performance
▸ Compression
  ↳ Proxy gzip/brotli-compresses responses before sending to client
  ↳ Reduces bandwidth by 60-80% for HTML/JSON/CSS
  ↳ Backends don't waste CPU on compression
▸ Connection pooling / multiplexing
  ↳ Proxy keeps long-lived connections to backends, reuses them across many client requests
  ↳ Reduces backend connection-setup overhead
▸ HTTP/2 and HTTP/3 termination
  ↳ Proxy speaks modern protocols to clients while backends stay on simple HTTP/1.1
▸ Buffering
  ↳ Proxy absorbs slow clients; backends only see fast, complete requests
📊 Compressed payload icons; pool of reusable connections between proxy and backends

## Slide 135
Reverse Proxy Benefits - Security
▸ Hides backend topology
  ↳ Attackers see only the proxy IP; internal IPs, ports, and architecture are masked
▸ Centralized security policy
  ↳ WAF (web application firewall) rules: block SQL injection, XSS, bot patterns
  ↳ Rate limiting per IP / per token to defend against abuse and DDoS
▸ TLS hygiene
  ↳ Modern cipher suites, HSTS, OCSP stapling enforced once at the proxy
▸ Authentication offload
  ↳ JWT validation, OAuth2 introspection, mTLS done at the proxy; backends trust forwarded identity
📊 Shield icon over the proxy; arrows of attacks bouncing off; clean traffic continuing inward

## Slide 136
Reverse Proxy Benefits - Centralized Logging and Observability
▸ Single place to log everything
  ↳ Every request and response passes through the proxy -> uniform access logs
  ↳ Backend servers can stay focused on business logic
▸ Metrics for free
  ↳ Request rate, latency percentiles (p50/p95/p99), error rates, status code distribution
  ↳ Per-route, per-host, per-upstream breakdowns
▸ Distributed tracing
  ↳ Inject `X-Request-Id` and trace headers at the proxy; propagate downstream
▸ Examples
  ↳ Nginx access logs -> Loki/ELK; Envoy metrics -> Prometheus + Grafana
📊 Proxy with three streams emerging: logs, metrics, traces, each going to its respective tool

## Slide 137
Reverse Proxy vs Load Balancer - The Difference
▸ Reverse proxy
  ↳ Primary job: mediate and enhance client-server communication (SSL, caching, security)
  ↳ Can sit in front of just ONE backend (no load balancing needed)
▸ Load balancer
  ↳ Primary job: distribute requests across MANY backends
  ↳ Specifically picks which server gets each request via an algorithm
▸ The overlap
  ↳ Most modern reverse proxies (Nginx, HAProxy, Envoy) ALSO load balance
  ↳ Most modern L7 load balancers (ALB, Envoy) ALSO act as reverse proxies
▸ The honest answer
  ↳ In practice the terms blur; the same software fills both roles
  ↳ The distinction is conceptual: "what's its primary purpose in this deployment?"
📊 Venn diagram - "Reverse Proxy" circle, "Load Balancer" circle, large overlap labeled "Nginx, HAProxy, Envoy, ALB"

## Slide 138
Reverse Proxy Examples in the Wild
▸ Nginx
  ↳ Most popular open-source reverse proxy; powers half the internet's top sites
  ↳ Strong at HTTP, static serving, caching; config-file driven
▸ HAProxy
  ↳ Reverse proxy + LB heavyweight; preferred for raw performance and TCP workloads
▸ Apache HTTPD (mod_proxy)
  ↳ Older but still common; heavily used in legacy enterprise stacks
▸ Cloudflare
  ↳ Global reverse proxy as a service; DDoS protection, CDN, WAF baked in
▸ Envoy / Traefik
  ↳ Modern cloud-native reverse proxies; great for Kubernetes and service meshes
📊 Logo strip with 1-2 word descriptors of strengths

## Slide 139
Reverse Proxy - Architecture Diagram
▸ Components
  ↳ Client (browser/mobile)
  ↳ DNS -> Reverse Proxy public IP (often Cloudflare or Nginx fronted)
  ↳ Reverse Proxy box with: TLS termination module, cache, WAF, log/metrics export
  ↳ Backend services in private subnet (web app, API, microservices)
  ↳ Optional: separate static asset origin (S3) and DB cluster behind app servers
▸ Flow labels
  ↳ 1: Client makes HTTPS request to `app.example.com`
  ↳ 2: TLS terminates at proxy; request decrypted and inspected
  ↳ 3: WAF rules evaluated; bad requests rejected with 403
  ↳ 4: Cache lookup; if hit, return immediately
  ↳ 5: If miss, forward to appropriate backend (per path-based routing)
  ↳ 6: Backend responds; proxy may cache, then compresses and re-encrypts to client
  ↳ 7: Access log + metrics emitted to observability stack
📊 Full architecture diagram with numbered arrows for the 7-step flow

## Slide 140
Reverse Proxy - Trade-offs
▸ Added latency vs feature richness
  ↳ Every request goes through extra processing; usually milliseconds, but it adds up
▸ Centralization vs single point of failure
  ↳ One config to manage = nice; one outage to break everything = scary (run redundant)
▸ Cache freshness vs hit rate
  ↳ Long TTLs = great hit rate, but stale data risks; short TTLs = fresh, but more backend load
▸ SSL termination vs end-to-end encryption
  ↳ Offload is faster, but internal traffic is plaintext unless you re-encrypt (mTLS)
▸ Operational complexity
  ↳ Powerful config languages (Nginx, Envoy YAML) = power and footguns
📊 Five mini scales similar to LB trade-offs slide

## Slide 141
Combined Architecture - LB + Reverse Proxy in Production
▸ A typical large web service stack (top to bottom)
  ↳ DNS / Anycast (Route53, Cloudflare DNS)
  ↳ Edge CDN + WAF (Cloudflare / AWS CloudFront)
  ↳ L4 Load Balancer (AWS NLB) for raw TCP and DDoS resilience
  ↳ L7 Load Balancer / Reverse Proxy (ALB or Nginx) for path routing, SSL, caching
  ↳ Service mesh sidecar proxies (Envoy) for internal service-to-service calls
  ↳ Application servers / microservices
▸ What each layer does
  ↳ Each layer adds a specific capability; you don't need every layer for every system
▸ Lesson
  ↳ "Load balancer" and "reverse proxy" are roles, not products; real systems compose multiple instances
📊 Vertical stack diagram with each layer labeled and its role annotated on the right

## Slide 142
Key Takeaways
▸ A load balancer distributes traffic; a reverse proxy mediates and enhances it
  ↳ Same software often plays both roles - distinction is by purpose
▸ L4 vs L7 is the most important LB choice
  ↳ L4 for raw speed and non-HTTP; L7 for content-aware routing and HTTP features
▸ Algorithm choice depends on workload shape
  ↳ Round Robin for uniform; Least Connections for variable; IP Hash for stateful
▸ Always run redundant LBs/proxies
  ↳ The thing that makes you highly available cannot itself be a single point of failure
▸ Reverse proxies unlock SSL termination, caching, compression, security, and observability
  ↳ These are why almost every public service has one
📊 5 numbered icons representing each takeaway

## Slide 143
Interview Tips
▸ Always start with "what kind of traffic?"
  ↳ HTTP -> L7; raw TCP/UDP -> L4; clarify before picking products
▸ Justify your algorithm choice
  ↳ Don't just say "Round Robin"; explain why given the workload (uniform vs variable)
▸ Mention redundancy explicitly
  ↳ Interviewers love hearing "active-active LBs" or "redundant proxies with failover"
▸ Bring up health checks and connection draining
  ↳ Demonstrates you've thought about the operational lifecycle, not just the happy path
▸ Differentiate reverse proxy benefits clearly
  ↳ Listing SSL termination, caching, and WAF separately shows depth
▸ Use real product names
  ↳ "ALB for L7, NLB for L4, Nginx as reverse proxy" sounds way more credible than "a load balancer"
▸ When asked "LB or reverse proxy?"
  ↳ Say "Often the same box; LB if I emphasize distribution, reverse proxy if I emphasize the proxying features"
📊 Checklist style with green ticks next to each interview tip

## Slide 144
Common Pitfalls
▸ Forgetting LB redundancy
  ↳ Single LB = single point of failure; always run >=2 in active-active or active-passive
▸ Using sticky sessions in modern microservices
  ↳ Anti-pattern; prefer stateless services with external session store (Redis)
▸ Bad health checks
  ↳ "/healthz returns 200 statically" -> LB sends traffic to a server with a broken DB
  ↳ Always exercise real dependencies in health checks (with sane timeouts)
▸ Ignoring connection draining
  ↳ Causes user-facing 5xx errors during deploys and scale-in events
▸ Mismatching SSL between LB and backend
  ↳ Forgetting `X-Forwarded-Proto` -> app generates HTTP redirects in HTTPS context, infinite loop
▸ Caching authenticated responses by mistake
  ↳ Leaks private data to other users; always vary on auth cookies/headers
▸ Treating L7 as free
  ↳ Heavy header parsing, regex routing, WAF rules add real CPU; profile and size accordingly
▸ Single LB doing everything
  ↳ Mixing public ingress, internal routing, and service mesh on one LB makes blast radius huge
📊 Red triangle warnings next to each pitfall in a 2-column layout

## Slide 145
Section 5: Application Layer and Microservices

## Slide 146
Section Overview - The Brains of the System
▸ The application layer is where business logic lives
  ↳ It sits between the web layer (HTTP handling) and the data layer (storage)
▸ Microservices are the modern evolution of this layer
  ↳ Breaking a giant codebase into small, focused, independently deployable services
▸ This section answers: how do we structure code so it scales with traffic AND with team size?
  ↳ Both technical scaling and organizational scaling matter
▸ Real systems we will reference: Netflix, Amazon, Uber, Airbnb
  ↳ All started as monoliths and evolved into microservices over time
📊 Roadmap graphic showing journey from single monolith box to a constellation of microservice nodes, with milestones labeled.

## Slide 147
What Is the Application Layer? (Concept Introduction)
▸ The application layer is the tier that executes business logic
  ↳ It receives parsed requests, applies rules, coordinates data, and returns results
▸ It is distinct from the web layer (which handles HTTP, TLS, routing, auth tokens)
  ↳ And distinct from the data layer (which persists state)
▸ Think of it as the "kitchen" in a restaurant
  ↳ The waiter (web layer) takes orders, the kitchen (app layer) cooks, the pantry (data layer) stores ingredients
▸ In classic 3-tier architecture: Presentation -> Application -> Data
  ↳ Each tier has one job and can scale based on its own bottleneck
📊 Three horizontal layers stacked - Web Layer (top, blue), Application Layer (middle, green, highlighted), Data Layer (bottom, or...

## Slide 148
Why Separate Web Layer from Application Layer? (Deep Explanation)
▸ Different layers have different bottlenecks and scaling profiles
  ↳ Web layer is I/O-bound (network, TLS); app layer is CPU-bound (logic, computation)
▸ Independent scaling lets you add capacity only where needed
  ↳ 100 web servers can fan out to 20 app servers if business logic is light
▸ Independent deployment reduces blast radius
  ↳ Deploying new business logic does not require restarting TLS termination
▸ Security boundary: web tier is internet-facing, app tier sits behind it
  ↳ Compromised web server cannot directly access the database
▸ Technology flexibility: web tier in Nginx, app tier in Java or Go
  ↳ Each tier picks the best tool for its job
📊 Two columns - "Coupled" (single box doing everything) vs "Separated" (two boxes with independent autoscaling groups). Show diff...

## Slide 149
Stateless vs Stateful Services (Concept Introduction)
▸ A stateless service stores no client-specific data between requests
  ↳ Every request contains everything the service needs to process it
▸ A stateful service remembers context across requests
  ↳ Session data, in-memory caches, user-specific state lives on the server
▸ Stateless is the gold standard for application servers
  ↳ Any instance can serve any request - load balancers can route freely
▸ Stateful services have affinity requirements
  ↳ Sticky sessions, consistent hashing, or external state stores become necessary
▸ The shift: move state OUT of app servers, INTO Redis, databases, or client tokens (JWT)
  ↳ Application code stays stateless; state lives in dedicated state stores
📊 Two diagrams side by side. Left: Stateful (each server has a database icon attached). Right: Stateless (servers are identical, ...

## Slide 150
Why Stateless Wins for Scaling (Deep Explanation)
▸ Horizontal scaling becomes trivial
  ↳ Spin up 10 more instances behind the load balancer - no special routing needed
▸ Failures are graceful
  ↳ If a server dies, the next request hits another server with no data loss
▸ Deployments are smoother (rolling updates work cleanly)
  ↳ Drain traffic from one instance, restart it, return it to the pool
▸ Auto-scaling is responsive
  ↳ New instances become productive instantly, no warm-up of session data
▸ The cost: every request must carry or fetch its context
  ↳ Slightly more bandwidth, slightly more cache lookups - but vastly more scalable
📊 Animation-style diagram showing a server crash - on left "stateful" version users get logged out, on right "stateless" version ...

## Slide 151
Real-World Example - Netflix Stateless Services
▸ Netflix runs thousands of microservices, nearly all stateless
  ↳ User session data lives in EVCache (Memcached fork) and Cassandra
▸ When you press play, the request can hit any instance of the playback service
  ↳ That instance fetches your watch history from a cache, computes recommendations, returns
▸ This enables Netflix to deploy thousands of times per day
  ↳ Any instance can be killed without user impact (Chaos Monkey proves it)
▸ During regional failures, traffic shifts to another AWS region instantly
  ↳ Because no app server holds unique state, regional failover is just a DNS change
📊 Netflix architecture sketch - many identical stateless service instances pulling from shared Cassandra and EVCache clusters. Sh...

## Slide 152
Horizontal vs Vertical Scaling of App Servers
▸ Vertical scaling (scale up): make one server bigger
  ↳ More CPU, more RAM, faster disk on the same machine
▸ Horizontal scaling (scale out): add more servers
  ↳ 10 medium servers instead of 1 huge server
▸ Vertical limits: hardware ceiling, single point of failure, expensive at the top end
  ↳ A 128-core machine costs more than 16x an 8-core machine
▸ Horizontal advantages: linear cost, fault tolerance, virtually unlimited
  ↳ Lose one server out of 100? Capacity drops 1%, not 100%
▸ Modern systems prefer horizontal scaling for app tier
  ↳ Stateless design + load balancer + autoscaling = elastic capacity
📊 Left side - one tall thick server labeled "Vertical: 128 cores, $$$$". Right side - row of 16 small identical servers labeled "...

## Slide 153
Trade-offs - Vertical vs Horizontal Scaling
▸ Vertical pros: simple, no distributed systems complexity, low latency between components
  ↳ All in one process - no network calls, no coordination
▸ Vertical cons: hardware ceiling, expensive scaling curve, single point of failure
  ↳ You eventually hit the biggest box money can buy
▸ Horizontal pros: elastic, fault tolerant, cost effective at scale
  ↳ Add or remove capacity in minutes
▸ Horizontal cons: requires stateless design, distributed system complexity, network overhead
  ↳ Suddenly you need service discovery, load balancing, distributed tracing
▸ Decision rule: start vertical for simplicity, go horizontal when you hit limits or need HA
  ↳ Most production systems eventually go horizontal
📊 Decision tree - "Single point of failure acceptable?" -> "Need >1 server's capacity?" -> "Cost matters?" leading to vertical or...

## Slide 154
Single Responsibility Principle at System Level (Concept Introduction)
▸ SRP at code level: a class should have one reason to change
  ↳ At system level: a service should own one business capability
▸ Each service has a clear, narrow purpose
  ↳ "Payments service" handles payments - not user profiles, not search, not email
▸ This makes the system understandable, testable, and changeable
  ↳ Each piece can be reasoned about in isolation
▸ It mirrors organizational structure (Conway's Law)
  ↳ One team owns one service that owns one capability
▸ The opposite is the "god service" or monolith
  ↳ One huge service that does everything and breaks every time anyone touches it
📊 Comparison diagram - Left: one large blob labeled "Order/User/Payment/Inventory/Email". Right: clean separated boxes - "Order S...

## Slide 155
Microservices - What They Are (Concept Introduction)
▸ Microservices = an architectural style where applications are built as a suite of small, independently deployable services
  ↳ Each service runs in its own process and communicates over the network
▸ Each service is built around a business capability
  ↳ Owned end-to-end by one team, deployed independently
▸ Contrast with monolith: one codebase, one deployable, shared database
  ↳ Monolith = one giant application doing everything
▸ Analogy: microservices are like specialized departments in a company
  ↳ HR, Finance, Sales, Engineering each have their own staff, processes, and tools, but coordinate to deliver the company's products
▸ Not just smaller code - it is about ownership, deployment, and runtime independence
  ↳ Code structure alone (modular monolith) is not microservices
📊 Left side - a single box labeled "Monolith" containing many features stacked together. Right side - a network of small connecte...

## Slide 156
Benefits of Microservices (Deep Explanation - Part 1)
▸ Independent deployment
  ↳ Push the payments service at 3pm without redeploying the entire platform
▸ Fault isolation
  ↳ If recommendations service crashes, checkout still works (graceful degradation)
▸ Technology diversity ("polyglot" architecture)
  ↳ Use Python for ML services, Go for high-throughput APIs, Java for legacy integration
▸ Team autonomy and parallel development
  ↳ 50 teams can ship 50 features in parallel without merge conflicts
▸ Independent scaling per service
  ↳ Scale the search service to 1000 instances, keep email service at 5
📊 Five icon-bullet rows. Each icon paired with a benefit. Use a deployment rocket, a fire-shield, a polyglot speech bubble (multi...

## Slide 157
Benefits of Microservices (Deep Explanation - Part 2)
▸ Easier onboarding for new engineers
  ↳ A new hire learns one service (10K lines), not the entire monolith (10M lines)
▸ Clearer ownership and accountability
  ↳ "Who owns checkout latency?" has a clear answer - the checkout team
▸ Reusability across products
  ↳ Auth service serves the website, mobile app, partner APIs, internal tools
▸ Better resilience patterns
  ↳ Circuit breakers, retries, bulkheads work cleanly at service boundaries
▸ Aligns with cloud-native infrastructure
  ↳ Containers, Kubernetes, serverless all assume small, independent units
📊 Org chart morphed with service architecture - team boxes mapped 1:1 to service boxes, showing Conway's Law alignment.

## Slide 158
Real-World Example - Amazon's Service Decomposition
▸ 2002: Jeff Bezos issued the famous "API mandate"
  ↳ All teams must expose data and functionality through service interfaces
▸ Result: thousands of services, each owned by a "two-pizza team" (small enough to feed with two pizzas)
  ↳ Order service, Inventory service, Recommendation service, Pricing service, etc.
▸ Each service is independently deployed and scaled
  ↳ Amazon deploys code every 11.7 seconds on average
▸ This enabled AWS itself to be born
  ↳ Internal services were so well-defined they could be sold externally as products
▸ The lesson: microservices enabled both engineering speed AND new business models
  ↳ Architecture is strategy, not just implementation
📊 Amazon services constellation diagram with key services labeled. Side note showing "11.7 seconds between deployments" stat. Sma...

## Slide 159
Real-World Example - Uber's Microservices Evolution
▸ 2014: Uber had a monolith called "core-services" - one Python codebase
  ↳ Hard to deploy, slow tests, every change risked breaking everything
▸ They migrated to ~2,200 microservices over several years
  ↳ Trip service, dispatch service, pricing/surge service, payments, notifications
▸ Each city-team and product-team could ship independently
  ↳ Surge pricing changes did not require coordinating with the payments team
▸ The downside: they eventually had too many services - "microservice sprawl"
  ↳ Now they consolidate where it makes sense (the pendulum swings back)
▸ Lesson: microservices are powerful but have an optimal granularity
  ↳ Too few = monolith problems, too many = operational chaos
📊 Timeline graphic - 2014 (one big box "core-services"), 2018 (cloud of ~2200 small services), 2022 (consolidated medium-sized cl...

## Slide 160
Microservices Trade-offs - Network Complexity
▸ Every service call is now a network call
  ↳ In-process method call (~nanoseconds) becomes RPC (~milliseconds)
▸ Network is unreliable: timeouts, retries, partial failures
  ↳ The 8 fallacies of distributed computing apply with full force
▸ Cascading failures become possible
  ↳ Service A waits for B which waits for C - if C is slow, A times out
▸ Mitigations: circuit breakers, timeouts, bulkheads, retries with jitter
  ↳ These patterns are mandatory, not optional
▸ Operational tools required: distributed tracing (Jaeger, Zipkin), centralized logging
  ↳ You cannot debug what you cannot see across service boundaries
📊 Diagram showing a request flowing through 5 services with latency annotations. Highlight one slow service causing cascade failu...

## Slide 161
Microservices Trade-offs - Data Consistency
▸ In a monolith, transactions span the entire business operation
  ↳ "Place order" and "decrement inventory" happen in one ACID transaction
▸ In microservices, each service owns its database - no shared transactions
  ↳ You cannot ROLLBACK across services
▸ Solutions are eventual consistency patterns
  ↳ Sagas (compensating transactions), event sourcing, outbox pattern
▸ The Saga pattern: a sequence of local transactions with compensating actions on failure
  ↳ Reserve inventory -> charge card -> if charge fails, release inventory
▸ This is hard - distributed data consistency is one of the toughest problems in software
  ↳ Many bugs in microservices systems trace back to consistency assumptions
📊 Two flows side by side. Left: "Monolith" - single transaction box with inventory + payment inside. Right: "Microservices Saga" ...

## Slide 162
Microservices Trade-offs - Operational Complexity
▸ One monolith deploy = one CI pipeline, one rollback button
  ↳ 200 microservices = 200 pipelines, 200 dashboards, 200 on-call runbooks
▸ Observability becomes critical
  ↳ Logs, metrics, traces must be correlated across services (correlation IDs everywhere)
▸ Service contracts must be versioned and backward-compatible
  ↳ Breaking the user service breaks every consumer of it
▸ Local development is harder
  ↳ Running 50 services on a laptop requires Docker Compose, mocks, or shared dev clusters
▸ The tooling tax is real
  ↳ Companies build platform engineering teams just to manage this complexity
📊 Operational complexity graph - X-axis is number of services, Y-axis is operational overhead. Steep curve showing exponential gr...

## Slide 163
Service Discovery (Concept Introduction)
▸ Problem: Service A needs to call Service B - but B's IP and port can change
  ↳ Containers come and go, autoscaling adds/removes instances, deployments shuffle hosts
▸ Service discovery = the mechanism by which services find each other dynamically
  ↳ "Where is the payments service right now?" answered at runtime, not compile time
▸ Two main patterns: client-side discovery and server-side discovery
  ↳ Differ in WHO knows about the registry of healthy instances
▸ Common service registries: Consul, etcd, ZooKeeper, Eureka, Kubernetes DNS
  ↳ Plus cloud-native: AWS Cloud Map, Service Connect
▸ Health checks are essential - registry only returns healthy instances
  ↳ Periodic pings ensure dead instances are removed quickly
📊 Central "Service Registry" box. Multiple service instances registering themselves. Caller queries registry to find available in...

## Slide 164
Client-Side vs Server-Side Discovery
▸ Client-side discovery: caller queries registry directly, picks an instance, calls it
  ↳ Caller is "smart" - it has discovery logic and load balancing built in
  ↳ Examples: Netflix Eureka + Ribbon, Consul with smart clients
▸ Server-side discovery: caller hits a load balancer, which queries the registry
  ↳ Caller is "dumb" - just calls a known endpoint, LB handles routing
  ↳ Examples: AWS ELB, Kubernetes Service (kube-proxy), Nginx with upstream
▸ Client-side pros: fewer hops, more flexible routing logic, no LB single point of failure
  ↳ Cons: each language needs a discovery client library
▸ Server-side pros: language-agnostic, simpler clients, centralized policy
  ↳ Cons: extra network hop, LB itself becomes critical infrastructure
📊 Two diagrams stacked. Top "Client-Side": Caller talks to Registry, then directly to Service. Bottom "Server-Side": Caller talks...

## Slide 165
API Gateway Pattern (Concept Introduction)
▸ Problem: clients (mobile, web, partners) need to talk to many microservices
  ↳ Without a gateway: clients need to know all service endpoints, handle auth, retries, etc.
▸ API Gateway = single entry point for all client requests, routing to backend services
  ↳ Sits at the edge of the system
▸ Responsibilities:
  ↳ Routing, authentication, rate limiting, request/response transformation, caching, logging
▸ Examples: Kong, AWS API Gateway, Apigee, Netflix Zuul, Envoy
  ↳ Modern alternative: BFF (Backend for Frontend) - one gateway per client type
▸ Hides internal architecture from clients
  ↳ You can refactor microservices without breaking mobile apps
📊 Funnel diagram - many clients (mobile, web, IoT, partners) on the left, single API Gateway in middle, many microservices on the...

## Slide 166
API Gateway - Deep Explanation
▸ Cross-cutting concerns are handled in one place
  ↳ Auth (verify JWT once at the gateway, pass user context downstream)
  ↳ Rate limiting (per-user, per-API quotas)
  ↳ SSL/TLS termination (one cert at the edge instead of per-service)
▸ Request aggregation reduces chattiness
  ↳ Mobile asks for "home page data" - gateway calls 5 services and combines responses
▸ Protocol translation
  ↳ External REST/GraphQL, internal gRPC - gateway bridges the two
▸ Caution: gateway can become a bottleneck or single point of failure
  ↳ Run multiple gateway instances behind a load balancer
▸ Caution: avoid putting business logic in the gateway
  ↳ Gateways should be thin - logic belongs in services
📊 Annotated gateway box showing concerns inside (Auth, Rate Limit, TLS, Aggregation, Caching, Logging). Warning labels around it:...

## Slide 167
Inter-Service Communication - Synchronous (REST, gRPC)
▸ Synchronous = caller blocks until response arrives
  ↳ Request-response model, immediate feedback
▸ REST over HTTP: ubiquitous, human-readable, easy to debug
  ↳ Good for external APIs, simple internal services
  ↳ JSON payload, URL-based routing, standard verbs (GET, POST, PUT, DELETE)
▸ gRPC: high-performance binary protocol over HTTP/2
  ↳ Protocol Buffers for schemas, code generation in many languages
  ↳ 5-10x faster than JSON/REST for internal traffic, supports streaming
▸ Use sync when caller NEEDS the response to continue
  ↳ "Get user profile", "validate payment", "check inventory"
▸ Risks: latency adds up, failures cascade, tight coupling
  ↳ Each sync call increases tail latency and failure surface
📊 Comparison table - REST vs gRPC across columns: Format (JSON vs Protobuf), Transport (HTTP/1.1 vs HTTP/2), Speed, Streaming Sup...

## Slide 168
Inter-Service Communication - Asynchronous (Events/Queues)
▸ Asynchronous = caller does not wait, communication happens via messages
  ↳ Producer publishes a message, consumer processes it later
▸ Patterns: message queues (RabbitMQ, SQS), event streams (Kafka, Kinesis), pub/sub
  ↳ Decouples producers from consumers in time and space
▸ Use async when:
  ↳ Action does not need immediate response (send email, update analytics)
  ↳ You want to broadcast to many consumers (event-driven architecture)
  ↳ You need buffering against load spikes
▸ Benefits: resilience, scalability, natural retry handling, loose coupling
  ↳ Producer does not care if consumer is up
▸ Trade-offs: eventual consistency, harder to reason about, debugging is harder
  ↳ "Did my message get processed?" requires tracing infrastructure
📊 Producer service publishing to a Kafka/Queue icon, multiple consumer services pulling from it independently. Show timestamp dif...

## Slide 169
Sync vs Async - Choosing the Right Pattern
▸ Sync when:
  ↳ You need an immediate answer to proceed (read paths, validations)
  ↳ Simple request/response semantics fit naturally
  ↳ Latency budgets allow the chained calls
▸ Async when:
  ↳ Fire-and-forget actions (notifications, analytics, audit logs)
  ↳ Workflows that span multiple services or take time (saga, batch processing)
  ↳ You need to absorb traffic spikes (queues smooth the load)
▸ Real systems mix both
  ↳ Checkout flow: sync calls for inventory + payment, async events for shipping + email
▸ Rule of thumb: minimize sync hops, prefer async for everything that does not block the user
  ↳ Each sync hop is a reliability tax
📊 Decision flowchart - "Need immediate answer?" -> Yes (Sync) / No (Async). Branch with "Spike protection?" / "Many consumers?" -...

## Slide 170
Data Isolation Principle (Concept Introduction)
▸ Each microservice owns its database - no other service may access it directly
  ↳ "Database per service" is one of the core microservices rules
▸ Why? Sharing a database recreates the monolith's coupling
  ↳ Schema changes ripple across services, transactions span services, ownership blurs
▸ Access only through the service's API
  ↳ Want order data? Call the Order service - do not query the orders table
▸ This enables independent schema evolution, technology choice, and scaling
  ↳ Order service uses Postgres, Search service uses Elasticsearch, Cart uses Redis
▸ Cost: data duplication and eventual consistency
  ↳ Multiple services may keep their own view of "user" - kept in sync via events
📊 Each service in its own bounded context with its own database icon. Red X over an arrow showing one service trying to access an...

## Slide 171
Real-World Example - Netflix Data Isolation
▸ Netflix has hundreds of services, each with its own data store
  ↳ User profile (Cassandra), Viewing history (Cassandra), Recommendations (multiple)
▸ A new feature like "skip intro" is a new service with its own DB
  ↳ Created without touching the user service or the playback service
▸ Cross-service data needs are handled via events
  ↳ When you finish a show, an event is published; analytics, recommendations, billing all consume it
▸ This isolation is what enables 1000s of deploys per day
  ↳ No team blocks on another team's database migration
▸ Lesson: data ownership boundaries are the most important boundaries in microservices
  ↳ Get this wrong, and the architecture collapses back into a distributed monolith
📊 Netflix services map showing each service with its own DB. A "viewing complete" event flowing to multiple consumers (recs, bill...

## Slide 172
Microservices Architecture Diagram (Putting It Together)
▸ Layered view of a typical microservices system:
  ↳ Edge: CDN -> Load Balancer -> API Gateway
  ↳ Services: dozens of small services, each with own DB
  ↳ Communication: sync (gRPC/REST) for queries, async (Kafka) for events
  ↳ Cross-cutting: service registry, distributed tracing, centralized logging, metrics
▸ Each service has identical operational shape
  ↳ Health endpoint, metrics endpoint, structured logs, container image, autoscaling
▸ Platform layer abstracts infrastructure
  ↳ Kubernetes runs everything, service mesh handles network concerns
▸ Observability stack ties it all together
  ↳ Without traces and dashboards, you cannot understand the system
📊 Full architecture diagram - top: clients; second row: CDN + LB + Gateway; third row: ~6 representative services with their DBs;...

## Slide 173
Microservices Trade-offs Summary
▸ Gains:
  ↳ Independent deployment, fault isolation, technology diversity, team autonomy, scalability per service
▸ Costs:
  ↳ Network complexity, distributed data consistency, operational overhead, debugging difficulty
▸ Hidden costs:
  ↳ Need for platform team, observability tooling, on-call rotation per service, distributed system expertise
▸ The famous quote: "Microservices give you a distributed system - and distributed systems are hard"
  ↳ Martin Fowler's MicroservicePremium concept: only worth it past a certain scale
▸ Microservices are a tool, not a goal
  ↳ The goal is independent teams shipping value - microservices are one way to enable that
📊 Two-column scorecard - Gains (green checkmarks) vs Costs (red warnings). Bottom: scale slider showing "Small team/Simple produc...

## Slide 174
Monolith vs Microservices - When to Use Each
▸ Choose monolith when:
  ↳ Small team (under ~20 engineers), early-stage product, unclear domain boundaries
  ↳ Need fast iteration without distributed systems overhead
  ↳ Strong transactional consistency requirements across the domain
▸ Choose microservices when:
  ↳ Multiple teams need to deploy independently
  ↳ Different parts of the system have very different scaling needs
  ↳ You have the operational maturity (CI/CD, monitoring, on-call)
▸ Modular monolith is often the right middle ground
  ↳ Single deploy, but well-bounded modules with clear interfaces - easy to extract later
▸ Do NOT choose microservices because:
  ↳ It is trendy, your favorite blog post said so, or you are pre-product-market-fit
  ↳ Premature decomposition is one of the most common architecture mistakes
📊 Decision matrix - X-axis: Team size (small to large), Y-axis: Domain complexity (simple to complex). Quadrants labeled with rec...

## Slide 175
Migration Path - Start Monolith, Extract Services
▸ Almost every successful microservices system started as a monolith
  ↳ Amazon, Netflix, Uber, Airbnb all began as single applications
▸ Reasons to start monolithic:
  ↳ Domain is unclear early - drawing service boundaries prematurely is wrong
  ↳ Single deploy = fast iteration during product-market fit search
  ↳ Less infrastructure investment up front
▸ Once the monolith hurts, extract services around pain points
  ↳ Slow deploys, deployment risk, scaling bottlenecks, team friction = signals
▸ Extract along clear bounded contexts
  ↳ Don't slice arbitrarily - find natural seams in the domain
▸ Done correctly, this is evolutionary architecture
  ↳ Architecture grows with the business, not ahead of it
📊 Timeline graphic - Year 1: Monolith. Year 3: Monolith + 1-2 extracted services. Year 5: Monolith shrinking, ~10 services. Year ...

## Slide 176
Strangler Fig Pattern (Concept Introduction)
▸ Named after the strangler fig vine that gradually grows around a tree
  ↳ Eventually replacing the tree entirely while leaving the original shape intact
▸ Pattern: incrementally replace pieces of a legacy monolith with new services
  ↳ Route traffic for specific functionality to the new service while monolith handles the rest
▸ Steps:
  ↳ Identify a slice of functionality (e.g., user authentication)
  ↳ Build a new service that handles it
  ↳ Use a routing layer (gateway/proxy) to direct traffic to the new service
  ↳ Once stable, remove that code from the monolith
  ↳ Repeat until monolith is "strangled"
▸ Benefits: low risk, incremental, no big-bang rewrite
  ↳ You can always roll back by routing traffic back to the monolith
📊 Three-panel evolution diagram. Panel 1: Monolith with feature highlighted. Panel 2: Gateway routes feature to new service, rest...

## Slide 177
Real-World Example - Amazon's Strangler Migration
▸ Amazon's monolith "Obidos" handled the original Amazon.com
  ↳ In early 2000s, it became the bottleneck slowing all teams
▸ They didn't do a big-bang rewrite
  ↳ Each new feature was built as a new service; old features were extracted one by one
▸ The API mandate forced every team to expose service interfaces
  ↳ This made strangling possible - the rest of the system could call services without caring if they were inside or outside the monolith
▸ Took years, but resulted in:
  ↳ Thousands of services, two-pizza teams, AWS as a side effect
▸ Lesson: incremental beats revolutionary when the system is critical to the business
  ↳ You cannot stop deliveries to rebuild the truck
📊 "Obidos" monolith shrinking over time across multiple stages, with extracted services blooming outward. AWS logo emerging at th...

## Slide 178
Service Mesh (Concept Introduction)
▸ Problem: as you add more microservices, every service needs the same cross-cutting features
  ↳ Retries, timeouts, mTLS, traffic shaping, observability, circuit breaking
▸ Without a mesh: each service implements these in its own code
  ↳ Different languages = different libraries = inconsistent behavior
▸ Service Mesh = a dedicated infrastructure layer that handles service-to-service communication
  ↳ Implemented as sidecar proxies (one per service instance) controlled by a central control plane
▸ The application code is unaware of the mesh
  ↳ Mesh handles networking; service just makes a local call to its sidecar
▸ Examples: Istio, Linkerd, Consul Connect, AWS App Mesh
  ↳ All built on Envoy proxy or similar
📊 Two services each with a small "sidecar proxy" attached. Arrows show service -> own sidecar -> other sidecar -> other service. ...

## Slide 179
Service Mesh - Why It Exists and Trade-offs
▸ Why it exists:
  ↳ Standardize networking, security, and observability across all services regardless of language
  ↳ Centralized policy (mTLS everywhere, rate limits, traffic splits for canary deploys)
▸ Capabilities:
  ↳ mTLS encryption between services (zero-trust networking)
  ↳ Traffic management (canary, blue/green, A/B routing)
  ↳ Resilience (retries, timeouts, circuit breakers) without code changes
  ↳ Observability (every call is traced and metered automatically)
▸ Trade-offs:
  ↳ Operational complexity - the mesh itself is non-trivial to run
  ↳ Latency overhead from sidecar (~1-5ms per hop)
  ↳ Steep learning curve, especially for Istio
▸ Use when: you have many services in many languages and need consistent policy
  ↳ Don't use for: small systems with a handful of services - it is overkill
📊 Pros/Cons split. Left: list of mesh capabilities (lock icon for mTLS, traffic split icon, retry icon, eye icon for observabilit...

## Slide 180
Real-World Example - Lyft and Envoy
▸ Lyft built Envoy proxy in 2016 as their service mesh data plane
  ↳ Same problem we discussed: inconsistent networking across hundreds of services
▸ Envoy gave them:
  ↳ Uniform observability across Python, Go, Java services
  ↳ Automatic retries and circuit breaking
  ↳ Zero-trust mTLS between services
▸ Envoy is now the industry standard sidecar
  ↳ Powers Istio, AWS App Mesh, Consul Connect, and many others
▸ Lesson: service mesh patterns came from real operational pain at scale
  ↳ Even if you don't adopt a full mesh, you should know what problems it solves
📊 Lyft logo with diagram of their service mesh. Envoy proxy logo prominently shown. Arrows pointing to other tools that use Envoy...

## Slide 181
Key Takeaways
▸ Separate web, application, and data layers
  ↳ Each scales independently and has different bottleneck profiles
▸ Make application servers stateless
  ↳ Move state to dedicated stores (Redis, DBs, JWTs); horizontal scaling becomes trivial
▸ Microservices = independent deployability + business-capability ownership
  ↳ Not just smaller code - it is about teams, deployment, and runtime independence
▸ Microservices are a trade-off, not a free win
  ↳ You exchange code complexity for operational and distributed-system complexity
▸ Start monolithic, extract services along bounded contexts as pain emerges
  ↳ Use the Strangler pattern for safe incremental migration
▸ Service discovery, API gateways, and async messaging are the connective tissue
  ↳ Service mesh is the heavy-duty option for large polyglot fleets
📊 Six numbered takeaway cards in a 2x3 grid, each with an icon and one-line summary. Use a "cheat sheet" visual style.

## Slide 182
Interview Tips
▸ Always ask about scale before recommending microservices
  ↳ "What is the team size? Traffic? Deployment frequency?" determines the right answer
▸ Be ready to articulate trade-offs in both directions
  ↳ Microservices are not always better - interviewers want nuance
▸ Use the magic phrase: "It depends on the bounded contexts"
  ↳ Shows you understand domain-driven design and service boundaries
▸ Mention specific real-world systems to anchor your reasoning
  ↳ "Like how Netflix moved playback to a stateless service backed by Cassandra..."
▸ Discuss data ownership early
  ↳ "Each service owns its data" - this signals senior-level thinking
▸ Talk about evolution and migration, not just end-state architecture
  ↳ Show you understand strangler pattern, modular monolith, gradual extraction
▸ For inter-service communication, justify sync vs async based on the use case
  ↳ Don't default to one - explain the trade-off
📊 Interview chat bubble illustration with key phrases highlighted. Stopwatch icon emphasizing "ask before answering". Bullet list...

## Slide 183
Common Pitfalls
▸ Distributed monolith
  ↳ Microservices that must be deployed together = worst of both worlds (slow + complex)
▸ Premature decomposition
  ↳ Splitting into services before domain boundaries are clear
▸ Shared databases across services
  ↳ Recreates monolith coupling at the database level
▸ Synchronous chains too deep
  ↳ A -> B -> C -> D -> E means cumulative latency and failure probability multiply
▸ Ignoring data consistency
  ↳ Assuming distributed transactions exist (they don't, practically)
▸ No observability before microservices
  ↳ You will be flying blind; always invest in tracing/logging/metrics first
▸ Microservices for resume-driven development
  ↳ Don't choose architectures to look fancy - choose them to solve actual problems
▸ Treating microservices as a goal
  ↳ The goal is shipping value safely; microservices are one means to that end
📊 Eight warning signs (red triangle icons) each with a one-line pitfall. Title "Avoid These Traps". Use cautionary visual style w...

## Slide 184
Summary - Application Layer and Microservices
▸ The application layer carries business logic and is the heart of system design
  ↳ Stateless, horizontally scalable services are the modern default
▸ Microservices enable team and technical scaling
  ↳ At the cost of distributed-system complexity that you must engineer for
▸ Choose architecture based on team size, domain clarity, and operational maturity
  ↳ Not on trends, blog posts, or perceived prestige
▸ Start with a monolith or modular monolith, evolve toward microservices when pain demands it
  ↳ Strangler pattern is your friend during migration
▸ Master the connective tissue: service discovery, API gateways, async messaging, service mesh
  ↳ These patterns repeat across every microservices system you will ever see
▸ Up next: Section 6 - Communication and APIs (REST, GraphQL, gRPC, WebSockets) deep-dive
📊 Recap infographic - 3 layers (Web, App, Data) at top, microservices constellation in middle, key patterns (gateway, mesh, disco...

## Slide 185
Section 6: Databases — RDBMS and NoSQL

## Slide 186
Section Overview — Why Databases Matter
▸ The database is the system's memory
  ↳ It is the single most important component for correctness, durability, and scale.
▸ Choice of database shapes architecture
  ↳ Schema model, scaling strategy, and consistency guarantees ripple through every service.
▸ Two dominant families: RDBMS and NoSQL
  ↳ RDBMS = structured, relational, ACID; NoSQL = flexible, distributed, BASE.
▸ Real systems use both
  ↳ Polyglot persistence: pick the right tool for each workload (orders in Postgres, feed in Cassandra).
▸ This section covers RDBMS, NoSQL types, SQL vs NoSQL, and scaling techniques
  ↳ With trade-offs, examples, and interview-ready framing.
📊 Split-screen graphic — left half shows a structured spreadsheet labeled "RDBMS", right half shows a JSON document, key-value pa...

## Slide 187
Part 1: Relational Databases (RDBMS)

## Slide 188
What Is an RDBMS — Concept Introduction
▸ Data stored in tables (rows and columns)
  ↳ A table is a 2D structure where each row is a record and each column is a typed attribute.
▸ Strict schema enforced before writes
  ↳ Every row in a table conforms to the same column definitions and data types.
▸ Relationships expressed via foreign keys
  ↳ One table references another's primary key, modeling 1:1, 1:N, and N:M relationships.
▸ Manipulated using SQL (Structured Query Language)
  ↳ Declarative: you describe what you want, not how to fetch it.
▸ Examples: PostgreSQL, MySQL, Oracle, SQL Server
  ↳ Decades of maturity, tooling, and ecosystem support.
📊 Two tables side by side. Users(id, name, email) connected by a foreign key arrow to Orders(order_id, user_id, total). Highlight...

## Slide 189
RDBMS Deep Dive — Tables, Keys, and Relations
▸ Primary key uniquely identifies a row
  ↳ Typically an auto-incrementing integer or UUID; enforces uniqueness and indexes by default.
▸ Foreign key enforces referential integrity
  ↳ Database refuses to insert an Order with a user_id that does not exist in Users.
▸ Normalization eliminates redundancy
  ↳ Splitting data across tables (3NF) so each fact lives in exactly one place.
▸ Joins reassemble normalized data at query time
  ↳ INNER, LEFT, RIGHT, FULL — the cost of normalization is paid on reads.
▸ Constraints encode business rules
  ↳ NOT NULL, UNIQUE, CHECK, DEFAULT — the database becomes a guardian of data quality.
📊 ER diagram with three boxes — Users, Orders, Products — and a junction table OrderItems linking Orders to Products (N:M). Label...

## Slide 190
ACID Properties — Concept Introduction
▸ ACID is the contract that makes RDBMS trustworthy for money, inventory, and identity
  ↳ Four guarantees that hold even when crashes, conflicts, or concurrency happen.
▸ A — Atomicity
  ↳ All operations in a transaction succeed together, or none of them do. No half-states.
▸ C — Consistency
  ↳ The database moves from one valid state to another; constraints are never violated.
▸ I — Isolation
  ↳ Concurrent transactions appear to run one at a time; intermediate states are hidden.
▸ D — Durability
  ↳ Once committed, data survives crashes, power loss, and reboots (written to disk/WAL).
📊 Four-quadrant graphic. Each quadrant shows a letter (A, C, I, D) with a small icon — a chain link, a checkmark, two parallel ar...

## Slide 191
ACID Deep Dive — The Bank Transfer Example
▸ Classic example: transfer $100 from Alice to Bob
  ↳ Two operations: debit Alice (-$100), credit Bob (+$100). Both must succeed.
▸ Atomicity in action
  ↳ If credit to Bob fails after debiting Alice, the debit is rolled back. No money lost.
▸ Consistency in action
  ↳ Total money in the system before and after the transfer is identical. Sum invariant preserved.
▸ Isolation in action
  ↳ A second transaction reading Alice's balance mid-transfer sees either the old or new value, never an in-between.
▸ Durability in action
  ↳ After the transfer commits and the bank's server crashes, the transfer is still recorded on restart.
📊 Four-panel comic. Panel 1: Alice $500, Bob $200. Panel 2: Atomicity (-100/+100 atomic). Panel 3: Crash icon. Panel 4: Reboot, A...

## Slide 192
When to Use RDBMS
▸ Structured data with stable schema
  ↳ User profiles, orders, financial records — entities that don't change shape weekly.
▸ Complex queries with joins and aggregations
  ↳ "Total revenue per region per month for top-10 products" — SQL excels here.
▸ Strong transactional guarantees needed
  ↳ Banking, e-commerce checkout, inventory, ticketing — anywhere correctness > scale.
▸ Reporting, analytics, and ad hoc queries
  ↳ SQL is the lingua franca of analysts and BI tools.
▸ Moderate scale (thousands to low millions of QPS with tuning)
  ↳ A well-tuned Postgres handles enormous workloads before you need to shard.
📊 Decision flowchart — "Need ACID transactions? -> Yes -> RDBMS. Schema stable? -> Yes -> RDBMS. Complex joins? -> Yes -> RDBMS."

## Slide 193
Indexes — Concept Introduction
▸ An index is an auxiliary data structure that accelerates lookups
  ↳ Like the index in the back of a book — find a topic without reading every page.
▸ Most common: B-tree index
  ↳ Balanced tree that keeps lookup, insert, and delete at O(log n).
▸ Without index: full table scan O(n)
  ↳ Database reads every row to find a match — fine for small tables, fatal at scale.
▸ With index: O(log n) lookup
  ↳ 1 billion rows? ~30 comparisons instead of 1 billion.
▸ Indexes are not free
  ↳ They consume disk, slow down writes, and need maintenance.
📊 Two diagrams side by side. Left: linear scan through 1B rows (red, slow). Right: B-tree with 4 levels reaching the same row (gr...

## Slide 194
B-Tree Index — How It Works
▸ Self-balancing tree with sorted keys
  ↳ Each node holds many keys (high fan-out), keeping the tree shallow even for billions of rows.
▸ Reads traverse from root to leaf in O(log n)
  ↳ 4–5 disk reads typically reach any row in a multi-billion-row table.
▸ Range queries are fast
  ↳ Leaves are linked in sorted order — "WHERE age BETWEEN 25 AND 35" walks adjacent leaves.
▸ Writes must update the index
  ↳ Every INSERT/UPDATE/DELETE rebalances the tree — extra cost on writes.
▸ Multiple indexes per table possible
  ↳ Each index is its own structure; more indexes = faster reads, slower writes, more disk.
📊 B-tree diagram. Root node with 3 keys, internal nodes branching out, leaf nodes at the bottom linked left-to-right with horizon...

## Slide 195
Indexes — Read vs Write Trade-off
▸ Reads: indexes turn O(n) into O(log n)
  ↳ Massive speedup for SELECT, especially with WHERE, JOIN, and ORDER BY.
▸ Writes: every modification updates every relevant index
  ↳ INSERT into a table with 5 indexes = 6 disk operations (1 table + 5 indexes).
▸ Storage cost
  ↳ Indexes can occupy 10–50% of table size; sometimes more than the data itself.
▸ Index only what you query
  ↳ Don't index every column "just in case" — measure first, then add.
▸ Composite indexes for multi-column queries
  ↳ INDEX(country, city) speeds up WHERE country='US' AND city='NYC' but not WHERE city alone.
📊 Seesaw diagram. One side labeled "Read speed" with a green up arrow, other side "Write speed" with a red down arrow. Indexes si...

## Slide 196
Query Optimization Basics
▸ The query planner translates SQL into an execution plan
  ↳ For each query, the database picks join order, index usage, and scan strategy.
▸ EXPLAIN reveals the plan
  ↳ `EXPLAIN ANALYZE SELECT ...` shows estimated and actual cost, rows, and operations.
▸ Watch for full table scans on large tables
  ↳ "Seq Scan" on millions of rows = missing index or non-sargable predicate.
▸ Avoid SELECT *
  ↳ Fetching unused columns wastes I/O, memory, and network.
▸ Statistics drive the planner
  ↳ Run ANALYZE periodically so the planner knows row counts and value distributions.
📊 Screenshot mockup of EXPLAIN output showing nodes — Hash Join, Index Scan, Seq Scan — with cost annotations. Highlight a "Seq S...

## Slide 197
RDBMS Examples in the Wild
▸ PostgreSQL — the Swiss Army knife
  ↳ Open source, ACID, JSON support, extensions (PostGIS, pg_trgm), strong concurrency (MVCC).
▸ MySQL — the web's workhorse
  ↳ Powers WordPress, half the internet's CMS layer; fast, simple, well-known.
▸ Oracle — the enterprise heavyweight
  ↳ Decades in banks, telecoms, governments; rich feature set, expensive licensing.
▸ SQL Server — the Microsoft stack pick
  ↳ Tight integration with .NET, Windows, and Azure; strong tooling.
▸ SQLite — the embedded champion
  ↳ Single-file database in your phone, browser, OS. Most-deployed database on Earth.
📊 Logo grid of the five databases with one-line descriptors under each.

## Slide 198
RDBMS Trade-offs
▸ Strong consistency, mature tooling, declarative SQL
  ↳ Decades of optimization, books, and battle-tested patterns.
▸ Rigid schema slows iteration
  ↳ Adding a column to a 1B-row table can lock the table for hours without care.
▸ Vertical scaling is the easy path
  ↳ Bigger CPU, more RAM, faster SSD — but there's a ceiling and it's expensive.
▸ Horizontal scaling (sharding) is hard
  ↳ Distributing joins and transactions across nodes is genuinely difficult.
▸ Best fit: structured, transactional, query-heavy systems
  ↳ Banking, ERP, CRM, e-commerce checkout, identity.
📊 Pros/Cons table — left column green check icons (ACID, SQL, joins, mature), right column red X icons (rigid schema, vertical sc...

## Slide 199
Part 2: NoSQL Databases — Types Deep Dive

## Slide 200
NoSQL — Concept Introduction
▸ "Not Only SQL" — a family, not a single technology
  ↳ Born from Web 2.0 needs: massive scale, flexible schemas, distributed by default.
▸ Four main types
  ↳ Key-Value, Document, Wide Column, Graph — each with different data models and use cases.
▸ Designed for horizontal scale
  ↳ Distribute data across many cheap machines instead of one expensive one.
▸ Trade strict ACID for flexibility and scale
  ↳ Most NoSQL systems offer BASE (eventual consistency) by default.
▸ Schema-less or schema-flexible
  ↳ No need to ALTER TABLE before adding a new field.
📊 Four-quadrant grid — top-left Key-Value (Redis), top-right Document (MongoDB), bottom-left Wide Column (Cassandra), bottom-righ...

## Slide 201
Key-Value Stores — Concept
▸ Simplest data model: a giant distributed hash map
  ↳ You give it a key, it gives you a value. That's it.
▸ Operations are O(1) average
  ↳ GET, SET, DELETE — predictable, blazing-fast latency (sub-millisecond).
▸ Values are opaque to the database
  ↳ Could be a string, JSON blob, image bytes — the store doesn't care.
▸ No queries, joins, or filtering on values
  ↳ You either know the key, or you don't find the data.
▸ Examples: Redis, Memcached, DynamoDB, Riak
  ↳ Used as caches, session stores, leaderboards, rate limiters.
📊 Hash table diagram — keys ("user:123", "session:abc", "cart:7") on the left, opaque values on the right, arrows connecting them.

## Slide 202
Key-Value Stores — Use Cases and Examples
▸ Caching layer in front of slower databases
  ↳ Redis caches hot user profiles; cache hit avoids hitting Postgres.
▸ Session storage for web apps
  ↳ Store login session by session ID; fast lookup on every request.
▸ Real-time leaderboards and counters
  ↳ Redis sorted sets rank millions of players in microseconds.
▸ Shopping cart and shopping-session state
  ↳ Per-user data, no relational joins needed.
▸ DynamoDB at Amazon scale
  ↳ Powers Amazon.com's catalog and orders pipeline; predictable single-digit-ms latency at any scale.
📊 Architecture diagram — App server -> Redis (cache) -> Postgres (source of truth). Show 95% of reads hitting Redis, 5% missing t...

## Slide 203
Document Stores — Concept
▸ Data stored as self-contained documents (typically JSON/BSON)
  ↳ Each document is a flexible, nested record — no fixed schema across documents.
▸ Documents grouped into collections
  ↳ Like tables, but documents in the same collection can have different fields.
▸ Rich queries on document fields
  ↳ Unlike key-value, you can query nested fields, arrays, and ranges.
▸ Indexes on any field
  ↳ Including nested paths like `address.city` or `tags.0`.
▸ Examples: MongoDB, CouchDB, Amazon DocumentDB, Firestore
  ↳ Ideal when entities are naturally hierarchical (a blog post with comments embedded).
📊 A JSON document for a "blog_post" with nested comments array and tags array. Show how this would map to 3 tables in RDBMS (Post...

## Slide 204
Document Stores — Use Cases and Examples
▸ Content management systems
  ↳ Articles with varying fields (image, video, gallery) fit naturally as documents.
▸ User profiles with evolving fields
  ↳ Adding "preferences.dark_mode" doesn't require a migration.
▸ Product catalogs with diverse attributes
  ↳ A shoe has size and color; a laptop has CPU and RAM — same collection, different fields.
▸ Event logging and IoT data
  ↳ Documents with timestamps and sensor readings, schema evolves as new sensors come online.
▸ MongoDB at scale
  ↳ Used by The New York Times, eBay, Cisco — millions of documents, sharded clusters.
📊 MongoDB collection illustration with three documents — a shoe, a laptop, a book — each with different fields, all in one "produ...

## Slide 205
Wide Column Stores — Concept
▸ Data stored as rows where each row can have a flexible set of columns
  ↳ Think "table" but each row picks its own columns; columns are sparse.
▸ Organized into column families
  ↳ A column family groups related columns physically together on disk.
▸ Optimized for massive write throughput and time-series data
  ↳ Append-friendly storage (LSM trees) — millions of writes per second per node.
▸ Queries by row key are fast; cross-row scans are slower
  ↳ Designed for predictable access patterns, not ad hoc joins.
▸ Examples: Apache Cassandra, HBase, ScyllaDB, Google Bigtable
  ↳ The backbone of many internet-scale services.
📊 Wide-column table illustration. Row keys on the left ("user:123"), then two column families (PersonalInfo: name, email) and (Ac...

## Slide 206
Column Families — Going Deeper
▸ A column family is a container for related columns
  ↳ Stored together on disk, accessed together — analogous to a "vertical partition".
▸ Each row may have any subset of columns within a family
  ↳ Sparse rows are normal — no NULL bloat for missing columns.
▸ Read/write paths are tuned per family
  ↳ Different compression, caching, and TTLs per family.
▸ Wide rows can have millions of columns
  ↳ Time-series: row = sensor_id, columns = timestamps -> readings.
▸ Cassandra's keyspace -> table -> partition -> row -> columns hierarchy
  ↳ Partition key determines which node owns the data.
📊 Diagram of a sensor wide row. Row key "sensor_42" with thousands of columns named by timestamp ("2026-04-28T10:00", "2026-04-28...

## Slide 207
Wide Column Stores — Use Cases and Examples
▸ Time-series data and IoT
  ↳ Sensor readings, metrics, logs — billions of writes, queried by time range.
▸ Messaging and activity feeds
  ↳ WhatsApp, Discord, Instagram store messages and events at massive scale.
▸ Recommendation systems' feature stores
  ↳ Pre-computed features per user, retrieved by user ID in microseconds.
▸ Cassandra at Netflix and Discord
  ↳ Discord migrated trillions of messages from MongoDB to Cassandra to ScyllaDB.
▸ HBase at Facebook (Messenger)
  ↳ Stores conversations and search indexes; pairs with Hadoop.
📊 Architecture diagram — IoT devices -> Kafka -> Cassandra cluster (5 nodes) -> dashboard reading recent metrics by time range.

## Slide 208
Graph Databases — Concept
▸ Data modeled as nodes (entities) and edges (relationships)
  ↳ Each node and edge can have properties (key-value pairs).
▸ Relationships are first-class citizens
  ↳ Traversing an edge is O(1) — no join cost regardless of graph size.
▸ Query language: Cypher (Neo4j), Gremlin, GQL
  ↳ "MATCH (a:Person)-[:FRIEND]->(b:Person) WHERE a.name='Alice' RETURN b"
▸ Excels at multi-hop relationship queries
  ↳ "Friends of friends who like jazz and live in Berlin" — a nightmare in SQL, trivial in graph.
▸ Examples: Neo4j, Amazon Neptune, JanusGraph, ArangoDB
  ↳ Used wherever connection patterns matter more than entities themselves.
📊 Graph illustration — circles for People, lines labeled "FRIEND", "LIKES", "LIVES_IN", connecting to Bands, Cities. Highlight a ...

## Slide 209
Graph Databases — Use Cases and Examples
▸ Social networks
  ↳ Friends-of-friends, mutual connections, network analysis (LinkedIn, Facebook).
▸ Recommendation engines
  ↳ "Customers who bought X also bought Y" — collaborative filtering as graph traversal.
▸ Fraud detection
  ↳ Detect rings of accounts sharing devices, addresses, or payment methods.
▸ Knowledge graphs
  ↳ Google Knowledge Graph, Wikidata — entities and relationships powering search.
▸ Network and IT operations
  ↳ Map dependencies between services, hosts, and incidents for root-cause analysis.
📊 Fraud-detection graph — multiple "Account" nodes connecting to a single "Device" node and "Address" node, highlighting suspicio...

## Slide 210
NoSQL Trade-offs Across Types
▸ Key-Value: ultimate speed, minimal querying
  ↳ You sacrifice query power for raw latency and throughput.
▸ Document: schema flexibility with rich queries
  ↳ Trade-off: harder to enforce cross-document consistency.
▸ Wide Column: massive write throughput
  ↳ Trade-off: must design tables around access patterns up front.
▸ Graph: relationship traversal is cheap
  ↳ Trade-off: not ideal for bulk analytics or simple key lookups.
▸ No NoSQL type does everything well
  ↳ Pick based on dominant access pattern, not hype.
📊 Radar chart with axes — Read Speed, Write Speed, Schema Flexibility, Query Power, Relationship Depth. Each NoSQL type drawn as ...

## Slide 211
Part 3: SQL vs NoSQL — When to Use Which

## Slide 212
SQL vs NoSQL — Concept Introduction
▸ Not a war, a toolkit
  ↳ Modern systems use both; the question is which fits a given workload.
▸ Five lenses to compare
  ↳ Schema, scale, consistency, query complexity, and ecosystem maturity.
▸ SQL's home turf: structured, transactional, complex queries
  ↳ Joins, aggregations, ACID — when correctness matters.
▸ NoSQL's home turf: massive scale, flexible schemas, simple access patterns
  ↳ Horizontal scaling, eventual consistency, document/graph shapes.
▸ The right answer is usually "it depends" — and often "both"
  ↳ Polyglot persistence is the modern default at scale.
📊 Two columns — "SQL strengths" (consistency, joins, mature tooling) vs "NoSQL strengths" (scale, schema flexibility, distributed...

## Slide 213
Schema Flexibility — SQL vs NoSQL
▸ SQL: schema-on-write
  ↳ Define columns and types up front; every row must match.
▸ Adding a column requires migration
  ↳ ALTER TABLE on a billion-row table can lock or take hours; tools like pt-online-schema-change help.
▸ NoSQL: schema-on-read (mostly)
  ↳ Documents/columns can vary; the application interprets the shape.
▸ NoSQL wins for evolving data
  ↳ Startups iterating on product ideas; user-generated content with unknown future fields.
▸ But schema-less is not free
  ↳ You still need discipline — otherwise you get inconsistent, undocumented data.
📊 Two database icons. SQL: locked box with rigid columns. NoSQL: open box with flexible documents of varying shapes.

## Slide 214
Scale — Vertical vs Horizontal
▸ SQL: vertical scaling first
  ↳ Bigger box (more CPU, RAM, SSD). Simple, but ceiling and cost grow non-linearly.
▸ SQL horizontal scaling: read replicas, then sharding
  ↳ Read replicas easy; sharding hard because of joins and cross-shard transactions.
▸ NoSQL: horizontal scaling by design
  ↳ Distribute data across many cheap nodes; scale by adding more.
▸ NoSQL handles billions of rows and millions of QPS
  ↳ Cassandra, DynamoDB, Bigtable run at petabyte scale routinely.
▸ Trade-off: distributed = more complexity (consistency, network failures)
  ↳ You inherit CAP theorem realities (covered earlier in the deck).
📊 Left side — one giant beefy server (vertical). Right side — many small servers in a row (horizontal). Cost/scale curves below, ...

## Slide 215
Consistency — ACID vs BASE
▸ SQL: ACID (Atomicity, Consistency, Isolation, Durability)
  ↳ Strong, immediate consistency — every read sees the latest committed write.
▸ NoSQL: BASE
  ↳ Basically Available, Soft state, Eventual consistency.
▸ BA — Basically Available
  ↳ The system always responds (maybe with stale data), preferring availability over correctness.
▸ S — Soft state
  ↳ Replica state may be in flux; the system doesn't guarantee instantaneous synchronization.
▸ E — Eventual consistency
  ↳ Given no new writes, all replicas converge to the same value eventually (milliseconds to seconds).
📊 Two boxes side by side. ACID box with a strict checkmark icon and "instant correctness". BASE box with three replica circles sl...

## Slide 216
Query Complexity — SQL Joins vs NoSQL Access Patterns
▸ SQL: declarative, optimizer-driven
  ↳ You say what you want; the planner figures out the best execution.
▸ Joins, aggregations, subqueries, window functions are first-class
  ↳ "Top 10 products by revenue per region this quarter" is a one-liner in SQL.
▸ NoSQL: model around access patterns
  ↳ You design the schema for the queries you'll run; ad hoc queries are painful.
▸ Most NoSQL stores have no joins
  ↳ You denormalize and embed, or join in application code.
▸ For analytics and BI: SQL still dominates
  ↳ Even NoSQL ecosystems rely on SQL layers (Presto, Athena, Spark SQL) for analysis.
📊 Two side-by-side queries. Left: SQL with INNER JOINs across 4 tables. Right: NoSQL — same result requires 4 separate fetches in...

## Slide 217
Real-World Hybrid — Twitter Uses Both
▸ Twitter (now X) is a textbook polyglot persistence example
  ↳ Different workloads have radically different requirements.
▸ MySQL for the social graph and metadata
  ↳ User accounts, follower relationships, settings — needs ACID and joins.
▸ Cassandra for the tweet timeline at massive scale
  ↳ Hundreds of thousands of writes per second; eventual consistency acceptable for feeds.
▸ Redis for caching hot timelines
  ↳ Sub-millisecond reads for active users' feeds, computed via fan-out-on-write.
▸ Manhattan (custom) for some real-time data
  ↳ Internal NoSQL store optimized for low-latency reads at scale.
📊 Twitter architecture diagram — User-service (MySQL) -> Timeline-service (Cassandra) -> Cache-layer (Redis) -> User. Annotate ea...

## Slide 218
SQL vs NoSQL — Decision Framework
▸ Default to SQL if you're uncertain
  ↳ Mature, well-understood, and Postgres scales further than most teams realize.
▸ Pick NoSQL when one of these is true
  ↳ You need horizontal scale beyond a single node, schema is genuinely fluid, or access pattern is simple key lookup at extreme QPS.
▸ Match the NoSQL type to the data shape
  ↳ Hierarchical -> document, time-series -> wide column, relationships -> graph, simple lookup -> key-value.
▸ Consider the team's expertise
  ↳ A perfectly fitted database your team can't operate is worse than a slightly imperfect one they know.
▸ Re-evaluate as scale grows
  ↳ Many systems start on Postgres and add specialized stores when bottlenecks appear.
📊 Decision tree starting at "Need ACID transactions?" branching to RDBMS or further questions about scale, schema, and access pat...

## Slide 219
SQL vs NoSQL — Trade-offs Summary
▸ SQL pros: ACID, joins, mature tooling, declarative queries
  ↳ Strong correctness guarantees and a battle-tested ecosystem.
▸ SQL cons: rigid schema, harder horizontal scaling
  ↳ Migrations and sharding are real pain points at scale.
▸ NoSQL pros: horizontal scale, schema flexibility, specialized models
  ↳ Designed for distributed environments from day one.
▸ NoSQL cons: weaker consistency, fewer joins, immature analytics tooling
  ↳ You trade developer convenience for raw scale.
▸ Conclusion: pick based on workload, not ideology
  ↳ The interview-perfect answer always weighs both sides explicitly.
📊 2x2 trade-off matrix. Rows: Pros / Cons. Columns: SQL / NoSQL. Each cell with 2-3 short bullets and a small icon.

## Slide 220
Part 4: Database Scaling Techniques

## Slide 221
Database Scaling — Concept Introduction
▸ A single database eventually hits a wall
  ↳ CPU saturated, disk full, locks contended, network bottlenecked.
▸ Six core techniques to scale databases
  ↳ Master-slave replication, master-master replication, federation, sharding, denormalization, SQL tuning.
▸ Each has different sweet spots
  ↳ Some help reads, some help writes, some help both — at different complexity costs.
▸ Combine techniques as scale grows
  ↳ Real systems use replication + sharding + caching + tuning together.
▸ Order matters: tune first, scale architecture last
  ↳ Index a missing column before you shard.
📊 Stair-step diagram. Step 1: SQL tuning (cheap). Step 2: Caching. Step 3: Read replicas. Step 4: Federation. Step 5: Sharding. S...

## Slide 222
Master-Slave Replication — Concept
▸ One master handles writes, one or more slaves replicate the data and serve reads
  ↳ Asynchronous replication is the common default.
▸ Reads scale horizontally
  ↳ Add more read replicas to handle more SELECT traffic.
▸ Writes still bottleneck on the master
  ↳ Replication helps reads, not writes.
▸ Replica lag is real
  ↳ A slave may be milliseconds-to-seconds behind master; reads can return stale data.
▸ Failover: a slave can be promoted to master if master fails
  ↳ HA tools (Patroni, MHA, RDS automatic failover) automate the dance.
📊 One master DB at the top, two arrows down to two slave DBs. App writes go to master; reads are load-balanced across slaves. Sho...

## Slide 223
Master-Slave Replication — Deep Dive and Use Cases
▸ Read-heavy workloads benefit massively
  ↳ Blogs, analytics dashboards, product catalogs — 95% reads, 5% writes.
▸ Geographic read replicas reduce latency
  ↳ Place replicas near users; writes still cross continents to reach master.
▸ Backup and analytics offload
  ↳ Run heavy reporting queries on a replica without harming production performance.
▸ Trade-off: replica lag breaks "read your writes"
  ↳ User updates profile, immediate read from replica may show old data — handle with sticky reads or read-from-master after write.
▸ Examples: MySQL replication, Postgres streaming replication, Aurora replicas
  ↳ All major RDBMS support this natively.
📊 World map with 1 master in US-East and 4 replicas in EU, APAC, US-West, and SA. Arrows show replication; users in each region r...

## Slide 224
Master-Master Replication — Concept
▸ Two (or more) masters each accept writes and replicate to each other
  ↳ Both nodes are read/write; useful for HA across regions.
▸ Helps write availability and geographic write distribution
  ↳ A failure of one master doesn't stop writes — the other keeps going.
▸ Conflict resolution is the hard part
  ↳ If both masters write to the same row simultaneously, who wins?
▸ Common strategies: last-writer-wins, application-level CRDTs, primary-region routing
  ↳ Each has correctness implications you must reason about explicitly.
▸ Examples: MySQL group replication, Postgres BDR, Galera Cluster
  ↳ Often replaced by NoSQL multi-master systems (Cassandra, DynamoDB) at scale.
📊 Two database icons connected by a bidirectional arrow labeled "replication". App writes flow to either master. Highlight a "con...

## Slide 225
Replication — Trade-offs
▸ Master-slave: simple, scales reads, doesn't scale writes
  ↳ The first scaling step; often sufficient for years.
▸ Master-master: scales writes regionally but adds conflict complexity
  ↳ Use when geographic write availability matters more than perfect consistency.
▸ Both add operational burden
  ↳ Monitoring lag, handling failover, ensuring replicas don't drift.
▸ Replication is not a backup
  ↳ A bad DELETE replicates instantly to all slaves — keep real backups separately.
▸ Synchronous vs asynchronous replication
  ↳ Sync = no data loss but slower writes; async = fast writes but possible loss on master crash.
📊 Comparison table — Master-Slave vs Master-Master. Rows: Read scaling, Write scaling, Complexity, Conflict handling. Mark with i...

## Slide 226
Federation — Concept Introduction
▸ Federation = functional partitioning by feature or domain
  ↳ Split one big database into several smaller databases, each owning a feature area.
▸ Example: separate databases for users, products, and forums
  ↳ Users-DB, Products-DB, Forums-DB — each independently scaled and operated.
▸ Each domain database is smaller and more focused
  ↳ Smaller working set fits in memory; less lock contention; team ownership clear.
▸ Aligns with microservices decomposition
  ↳ Each service owns its own database (database-per-service pattern).
▸ Trade-off: cross-domain joins now require application-level orchestration
  ↳ You can't `JOIN users.posts ON forums.threads` anymore.
📊 Single monolith DB on the left labeled "Before". Three smaller DBs on the right labeled Users, Products, Forums — each connecte...

## Slide 227
Federation — Deep Dive and Trade-offs
▸ Reduces read/write traffic per database
  ↳ Each box only handles one domain's load; capacity grows with each split.
▸ Smaller databases = simpler indexes, faster vacuum/maintenance
  ↳ Operational sanity improves dramatically.
▸ Independent scaling and tech choices
  ↳ Users on Postgres, Products on Postgres+ElasticSearch, Forums on MongoDB — all valid.
▸ Cross-domain queries become application logic
  ↳ Aggregating data from multiple DBs is your job, not the database's.
▸ Distributed transactions become hard
  ↳ Cross-DB writes need sagas, outbox patterns, or event-driven consistency.
📊 Microservice architecture — each service has its own DB icon, an event bus connects them for cross-domain workflows.

## Slide 228
Sharding — Concept Introduction
▸ Sharding = horizontal partitioning of a single dataset across many databases
  ↳ Split rows of one logical table across multiple physical databases (shards).
▸ Analogy: splitting a phone book by name
  ↳ Shard 1 holds names A–M, Shard 2 holds names N–Z. Lookup by name routes to the right shard.
▸ Each shard is an independent database with the same schema
  ↳ All shards together represent the full dataset.
▸ Scales reads AND writes
  ↳ Unlike replication, every shard handles its own write load.
▸ The hardest mainstream scaling technique
  ↳ Cross-shard joins, transactions, and rebalancing are non-trivial.
📊 A phone book split into two halves labeled "A–M" and "N–Z", each on its own database server. A "router" component on top decide...

## Slide 229
Sharding — Strategies
▸ Range-based sharding
  ↳ Partition by key range (user_id 1–1M on shard 1, 1M–2M on shard 2). Simple but prone to hotspots.
▸ Hash-based sharding
  ↳ Apply a hash function to the key; modulo over shard count distributes data evenly.
▸ Directory-based sharding
  ↳ A lookup service maps keys to shards; flexible but adds a hop.
▸ Geo-based sharding
  ↳ Shard by user region (EU users in EU shard); reduces latency, supports compliance (GDPR).
▸ Pick the shard key carefully
  ↳ The shard key drives routing, balance, and query patterns — bad keys cause endless pain.
📊 Four small diagrams in a 2x2 grid showing each strategy with arrows from a "key" to a "shard" using different routing logic.

## Slide 230
Consistent Hashing for Sharding
▸ Naive hash sharding: `shard = hash(key) % N`
  ↳ Works, but adding or removing a shard remaps almost every key (massive data movement).
▸ Consistent hashing: keys and nodes map onto a virtual ring
  ↳ Each key is owned by the next node clockwise on the ring.
▸ Adding a node only moves keys from the neighbor
  ↳ Roughly 1/N of data moves, instead of nearly everything.
▸ Virtual nodes (vnodes) smooth load distribution
  ↳ Each physical node represents many points on the ring, evening out hot spots.
▸ Used in DynamoDB, Cassandra, Riak, and many CDNs
  ↳ The same algorithm powers cache layers and load balancers too.
📊 Circular ring diagram with 4 nodes (N1, N2, N3, N4) placed around it and several keys mapped to the next clockwise node. Show w...

## Slide 231
Sharding — Trade-offs
▸ Pros: near-linear horizontal scaling for both reads and writes
  ↳ The path to internet scale.
▸ Cons: cross-shard joins are painful or impossible
  ↳ You denormalize, fan-out queries, or maintain materialized views.
▸ Cons: distributed transactions are hard
  ↳ Two-phase commit is slow and fragile; sagas are the modern alternative.
▸ Cons: re-sharding is operationally complex
  ↳ Splitting a hot shard while the system is live takes careful tooling.
▸ Hot shard problem: bad keys create skew
  ↳ One celebrity user's tweets all hit one shard — 10x the load.
📊 Pros/cons split panel. Bottom shows a "hot shard" warning — one shard glowing red while others are blue, illustrating skew.

## Slide 232
Denormalization — Concept
▸ Denormalization = intentionally duplicating data to speed up reads
  ↳ The opposite of normalization; trade write/storage cost for read simplicity.
▸ Joins are expensive at scale
  ↳ Pre-compute the join result and store it where it'll be read.
▸ Common in NoSQL and read-heavy SQL systems
  ↳ Cassandra schemas are designed denormalized from day one.
▸ Example: store user_name on every order row
  ↳ Avoid joining Orders to Users on every order list query.
▸ Trade-off: writes must update multiple places
  ↳ When the user renames themselves, you update many rows — eventual consistency in app logic.
📊 Two diagrams. Left: normalized — Orders joins Users. Right: denormalized — Orders has user_name embedded; arrow shows a write t...

## Slide 233
Denormalization — Use Cases and Trade-offs
▸ Activity feeds (fan-out-on-write)
  ↳ When someone tweets, copy the tweet into each follower's timeline at write time.
▸ Materialized views and read models in CQRS
  ↳ Pre-built read shapes that match what the UI needs.
▸ Aggregations cached as columns
  ↳ "post_count" on user row, updated on insert/delete, avoids COUNT(*) at read time.
▸ Trade-off: write amplification
  ↳ One logical write becomes many physical writes; storage and write throughput cost rise.
▸ Trade-off: data drift if updates miss a copy
  ↳ You need disciplined update paths or background reconciliation.
📊 Fan-out-on-write diagram. One tweet from a celebrity user fans out into N follower-timeline rows in parallel. Highlight the amp...

## Slide 234
SQL Tuning — Concept Introduction
▸ Tuning is the cheapest scaling technique
  ↳ Often a missing index gives 100x speedup; do this before any sharding talk.
▸ Three main levers
  ↳ Indexes, query rewriting, and schema design.
▸ Use EXPLAIN ANALYZE to find slow queries
  ↳ The plan shows what the database actually does, not what you think it does.
▸ Cache plans and parameters
  ↳ Prepared statements avoid replanning on each request.
▸ Monitor with slow query logs and APM
  ↳ You can't tune what you don't measure.
📊 Toolbox illustration containing labeled tools — "EXPLAIN", "ANALYZE", "Indexes", "Slow Query Log", "Prepared Statements".

## Slide 235
SQL Tuning — Practical Techniques
▸ Add indexes that match WHERE, JOIN, and ORDER BY clauses
  ↳ Composite indexes for multi-column predicates; covering indexes to avoid table lookups.
▸ Avoid N+1 queries from ORMs
  ↳ Eager-load relations; one well-formed JOIN beats 1000 tiny SELECTs.
▸ Rewrite non-sargable predicates
  ↳ `WHERE YEAR(created_at) = 2026` blocks index use; `WHERE created_at >= '2026-01-01' AND < '2027-01-01'` doesn't.
▸ Use LIMIT and pagination correctly
  ↳ Keyset pagination (WHERE id > last_id) beats OFFSET for deep pages.
▸ Vacuum, analyze, and update statistics regularly
  ↳ Stale stats lead the planner astray.
📊 Before/after EXPLAIN comparison. Before: Seq Scan, 1.2s. After: Index Scan, 8ms. Highlight the change in green.

## Slide 236
Database Scaling — Trade-offs Summary
▸ Replication: scales reads, simple to operate
  ↳ First step for most systems.
▸ Federation: cleaner ownership, smaller working sets
  ↳ Aligns with microservices; cross-domain queries get harder.
▸ Sharding: scales reads and writes
  ↳ Highest complexity, hardest to get right.
▸ Denormalization: fast reads at the cost of write complexity
  ↳ Default in NoSQL; selective in SQL.
▸ SQL tuning: highest ROI per hour of effort
  ↳ Always do this first; it often delays the need for harder steps.
📊 ROI vs Complexity scatter plot. SQL tuning: low complexity, high ROI. Replication: medium both. Sharding: high complexity, high...

## Slide 237
Section Wrap-Up

## Slide 238
Key Takeaways
▸ RDBMS = ACID, structured, joins, mature
  ↳ Default choice for most transactional workloads. Postgres scales further than people think.
▸ NoSQL is a family with four main types
  ↳ Key-Value (Redis), Document (MongoDB), Wide Column (Cassandra), Graph (Neo4j) — pick by data shape.
▸ ACID vs BASE is the consistency trade-off
  ↳ Strong consistency vs eventual consistency; pick what your business actually requires.
▸ Sharding = splitting data horizontally; federation = splitting by domain
  ↳ Different tools for different problems; both increase complexity.
▸ Real systems are polyglot
  ↳ Twitter, Netflix, Amazon use 5–10 different databases together by design.
📊 One-page cheat sheet — three columns: "Choose RDBMS when", "Choose NoSQL when", "Scale by". Each with 4 bullets.

## Slide 239
Interview Tips
▸ Always ask about scale, schema stability, and consistency before recommending a database
  ↳ "How many writes per second? How does the schema evolve? Is stale read OK?" wins points.
▸ Define ACID and BASE precisely if you mention them
  ↳ Especially Isolation and Eventual consistency — interviewers probe these.
▸ Mention specific examples: Postgres, MongoDB, Cassandra, Redis, Neo4j
  ↳ Concrete examples beat vague references.
▸ For sharding, explain the shard key and consistent hashing
  ↳ These are the most common follow-up questions.
▸ Discuss trade-offs explicitly — never claim one option is "best"
  ↳ "I'd start with Postgres; if writes exceed 50k/s I'd shard or move hot tables to Cassandra."
📊 Speech-bubble graphic — interviewer asks "Which database?", candidate replies with a structured framework: "Depends on (1) scal...

## Slide 240
Common Pitfalls
▸ Choosing NoSQL "for scale" before you have scale
  ↳ Most products fail from lack of users, not too many. Postgres is fine for most startups.
▸ Forgetting to define ACID precisely
  ↳ Mixing up Consistency (constraint integrity) with CAP-Consistency (linearizability) is a classic stumble.
▸ Ignoring replica lag in read-after-write scenarios
  ↳ "User updates profile, sees old data" is a top user-facing bug.
▸ Sharding too early or with a bad shard key
  ↳ Reshardings are expensive; pick a key with high cardinality and even access.
▸ Over-indexing tables
  ↳ Every index slows writes; benchmark before adding.
▸ Treating replication as a backup
  ↳ It isn't. Bad writes (DELETE without WHERE) replicate instantly. Keep point-in-time backups separately.
📊 "Pitfall warning" board with 6 stop-sign icons, each labeled with a pitfall in red text and a one-line corrective tip below in ...

## Slide 241
Section Closing — Mental Models
▸ "Pick the database that matches your access patterns"
  ↳ Not the trendiest, not the simplest, the one that fits your reads and writes.
▸ "Tune before you scale, scale before you shard"
  ↳ Cheapest fix first, most expensive last.
▸ "Polyglot persistence is normal at scale"
  ↳ Don't hunt for one database to rule them all — there isn't one.
▸ "Consistency is a spectrum, not a switch"
  ↳ From linearizable to eventual; pick the weakest level your business tolerates.
▸ Up next: Caching — the secret weapon that makes most databases survivable
  ↳ We'll cover Redis, Memcached, CDN caches, and cache invalidation strategies.
📊 Mountain summit graphic — climber at the top labeled "scale" with checkpoints below (tune, replicate, federate, shard, denormal...

## Slide 242
Section 7: Caching

## Slide 243
Section Overview — Caching
▸ Caching is the single highest-leverage performance technique in system design
  ↳ One well-placed cache can reduce latency by 10–100x and database load by 90%+
▸ We will cover what caching is, where to put caches, read/write strategies, invalidation, eviction, and distributed caching
  ↳ Each topic includes intuition, real-world examples, diagrams, and trade-offs
▸ Caching is everywhere: CPU registers, browsers, CDNs, app servers, databases, distributed systems
  ↳ Almost every "fast" system you use is fast because of layered caches
▸ Master caching and you master ~40% of system design interview problems
  ↳ Twitter timelines, YouTube videos, Amazon product pages, Facebook feeds — all cache-driven
▸ Core lesson: caching trades freshness for speed; the art is choosing the right trade-off
  ↳ Strong consistency + cache = hard problem; eventual consistency + cache = standard pattern
📊 Pyramid diagram showing latency hierarchy — CPU register (1ns) → L1 (1ns) → L2 (4ns) → RAM (100ns) → SSD (100µs) → Network (1ms...

## Slide 244
What is Caching?
▸ A cache is temporary, fast storage that holds the results of expensive computations or fetches
  ↳ "Expensive" can mean slow database query, network round-trip, CPU computation, or disk I/O
▸ Goal: serve future requests for the same data without redoing the work
  ↳ First request pays full cost; subsequent requests pay near-zero cost
▸ Caches exploit two fundamental properties of real workloads
  ↳ Temporal locality (recently used data is likely used again soon)
  ↳ Spatial locality (data near recently used data is likely used soon)
▸ The core trade-off: speed vs. freshness vs. memory cost
  ↳ Faster reads, but data may be stale; uses RAM (expensive) instead of disk (cheap)
▸ Caching is NOT a database — it is a derived, disposable view of authoritative data
  ↳ The source of truth always lives elsewhere; cache can be wiped without data loss
📊 Two-panel comparison: Left panel "Without Cache" — User → App → Database (slow, 50ms); Right panel "With Cache" — User → App → ...

## Slide 245
Why Caching? — The Business Case
▸ Reduces latency: serving from RAM is ~100x faster than disk and ~1000x faster than network
  ↳ Page load drops from 500ms to 5ms — measurably better user experience
▸ Reduces backend load: a 90% cache hit ratio means your database handles only 10% of traffic
  ↳ Lets you scale to 10x users on the same database hardware
▸ Reduces cost: cache hits are cheaper than database queries, API calls, or recomputation
  ↳ Cache a $0.01 LLM call once; serve 1M users from cache for the same penny
▸ Improves availability: cached data can serve users even when the origin is down
  ↳ Stale-while-revalidate keeps the site up during database outages
▸ Smooths traffic spikes: cache absorbs flash crowds before they hit the origin
  ↳ Black Friday, viral tweets, breaking news — cache is your shock absorber
📊 Bar chart comparing latencies on log scale — L1 cache (1ns), Memory (100ns), SSD (100µs), Network (1ms), Database query (10–100...

## Slide 246
Cache Hierarchy — From CPU to Network
▸ Modern computing is a stack of caches, each larger but slower than the one above
  ↳ Optimizing the hot path means keeping data as high in the hierarchy as possible
▸ CPU caches: L1 (~32KB, 1ns), L2 (~256KB, 4ns), L3 (~8MB, 12ns)
  ↳ Hardware-managed; invisible to your application but matters for performance-critical code
▸ Main memory (RAM): ~16–256GB, ~100ns access — where most application caches live
  ↳ Redis, Memcached, in-process LRU caches, JVM heap all live here
▸ Local disk / SSD: ~1TB, ~100µs — used for browser cache, OS page cache, large object cache
  ↳ CDN edge nodes use SSD-backed caches for warm assets
▸ Network and remote storage: ~1ms+ — origin servers, S3, primary databases
  ↳ This is what we are trying to avoid hitting on the hot path
📊 Inverted pyramid showing hierarchy with size growing downward and speed shrinking — CPU registers at top (bytes, picoseconds) t...

## Slide 247
Intuition — Cache as a Workshop Bench
▸ Imagine a carpenter with a workshop full of tools stored in a basement
  ↳ Walking to the basement for every tool would make any job impossibly slow
▸ The carpenter keeps frequently used tools (hammer, tape measure, pencil) on the workbench
  ↳ The workbench is small but right next to the work — instant access
▸ Less-used tools (specialty saws) sit on a nearby shelf — quick to grab but a step away
  ↳ Rarely used tools (annual jigs) stay in the basement
▸ Cache hierarchy works exactly the same way
  ↳ L1 = pocket, L2 = workbench, L3 = shelf, RAM = closet, disk = basement, network = warehouse across town
▸ The skill is predicting which tools you'll need next and pre-staging them
  ↳ This is exactly what cache eviction policies and prefetching algorithms do
📊 Cartoon of a carpenter at a workbench with tools labeled by access frequency, basement stairs leading down to "cold storage" la...

## Slide 248
Cache Hit vs. Cache Miss
▸ Cache hit: requested data is found in the cache — return immediately
  ↳ Cost = cache access time (~1ms for Redis, ~1ns for L1)
▸ Cache miss: requested data is not in the cache — must fetch from origin
  ↳ Cost = cache access + origin access + (usually) write-back to cache
▸ Three flavors of miss matter in practice
  ↳ Compulsory miss: first time data is requested (unavoidable cold start)
  ↳ Capacity miss: cache too small to hold working set (evicted before reuse)
  ↳ Conflict miss: hashing collisions in set-associative caches (rare in software caches)
▸ Miss penalty is the dominant performance variable in any cached system
  ↳ A 50ms miss vs 1ms hit means even small miss-rate changes drastically shift average latency
▸ Average latency formula: AvgLatency = HitRate × HitLatency + MissRate × MissLatency
  ↳ At 95% hit rate with 1ms hit / 50ms miss → avg = 3.45ms; at 80% → avg = 10.8ms (3x worse)
📊 Flowchart — Request arrives → Check cache → "Hit?" diamond → Yes (green path, return cached value) / No (red path, fetch from D...

## Slide 249
Cache Hit Ratio — The Most Important Metric
▸ Hit ratio = cache hits / total requests — measures how effective your cache is
  ↳ 90% means 9 out of 10 requests skip the database; 50% means cache is barely helping
▸ Why it matters more than raw cache size
  ↳ A 100GB cache with 30% hit rate is worse than a 10GB cache with 95% hit rate
▸ Target hit ratios depend on workload
  ↳ Web page caches: 95–99% (Cloudflare reports ~95% globally)
  ↳ Database query caches: 80–95% typical
  ↳ User session caches: ~99%
▸ Below 80% hit ratio, ask yourself
  ↳ Is the cache too small? Is TTL too short? Is the access pattern truly random?
▸ Hot keys often dominate the hit ratio (Pareto / Zipf distribution)
  ↳ Top 20% of keys often serve 80% of traffic — caching them gets you most of the win
📊 Line graph showing average latency on Y-axis vs. hit ratio on X-axis — exponential drop in latency as hit ratio crosses 90%, 95...

## Slide 250
When Caching Helps — and When It Hurts
▸ Caching helps when read traffic dominates write traffic
  ↳ Read-heavy workloads (1000:1 reads:writes) get massive benefit from caching
▸ Caching helps when the same data is requested repeatedly (high reuse)
  ↳ Trending tweets, popular product pages, common search results
▸ Caching helps when origin computation is expensive relative to cache lookup
  ↳ Complex SQL joins, ML inference, third-party API calls
▸ Caching HURTS when data changes faster than it is read
  ↳ Real-time stock prices, live game state — cache is stale before it is reused
▸ Caching HURTS when working set is larger than cache (low locality)
  ↳ Random scans over a 1TB table with 10GB cache → ~1% hit rate, just adds overhead
▸ Caching adds complexity: invalidation bugs, stale data, consistency edge cases
  ↳ Don't add a cache "just because" — measure first, cache the actual hot path
📊 Two columns — "Cache YES" with examples (user profiles, product catalog, news articles, autocomplete) vs "Cache NO" (real-time ...

## Slide 251
Caching Layers — The Big Picture
▸ A modern web request passes through 5–7 cache layers before hitting the origin
  ↳ Each layer captures a slice of traffic and forwards only the misses downstream
▸ Browser cache → CDN edge → reverse proxy → app cache → distributed cache → DB cache → disk
  ↳ Goal: maximize hits at the highest, cheapest layer
▸ Multi-layer caching is multiplicative — 50% hit at each of 4 layers = 6.25% reaches origin
  ↳ This is why CDN + Redis + DB query cache together can absorb millions of QPS
▸ Each layer has different TTLs, sizes, eviction policies, and invalidation semantics
  ↳ Static assets cached for a year at the edge; user data cached for seconds in app
▸ Design rule: cache as close to the user as possible, but as far back as correctness requires
  ↳ Personalized data → app/distributed cache; public assets → CDN; computed views → DB cache
📊 Horizontal layered diagram: Browser → CDN → Reverse Proxy → App Server (in-process cache) → Redis → Database (query cache + buf...

## Slide 252
Layer 1 — Client-Side Caching
▸ Browser HTTP cache stores responses based on Cache-Control, ETag, Last-Modified headers
  ↳ Cache-Control: max-age=31536000, immutable → cache for a year, never revalidate
▸ Service workers enable programmatic offline caches (PWAs)
  ↳ Gmail, Google Docs, Twitter use service workers for offline-first behavior
▸ localStorage / sessionStorage / IndexedDB store structured data locally
  ↳ User preferences, draft messages, recently viewed items — survive page refresh
▸ Pros: zero network cost, offline support, instant load on repeat visits
  ↳ 304 Not Modified responses save bandwidth even when revalidating
▸ Cons: no central control once cached — bad deploys can persist for hours/days
  ↳ Must use cache-busting URLs (style.abc123.css) for safe updates
📊 Browser window diagram showing layers — HTTP cache → Service Worker → IndexedDB → localStorage, with arrows showing fallback order

## Slide 253
Layer 2 — CDN Caching
▸ CDN = Content Delivery Network: geographically distributed edge servers caching origin content
  ↳ Cloudflare, Akamai, Fastly, AWS CloudFront, Google Cloud CDN
▸ Caches static assets (images, CSS, JS, video segments) at edge nodes near users
  ↳ Tokyo user fetches asset from Tokyo POP, not Virginia origin — 200ms → 5ms
▸ Modern CDNs cache dynamic content via edge functions and smart cache keys
  ↳ Cloudflare Workers, Fastly Compute@Edge let you cache personalized HTML
▸ Cache invalidation via purge APIs, surrogate keys (Fastly), or versioned URLs
  ↳ Netflix versions every asset; never invalidate, just deploy new URLs
▸ Real example: YouTube video streaming
  ↳ Hot videos cached at thousands of edge POPs; long-tail fetched from regional caches
▸ Pros: massive scale (Tbps of bandwidth), DDoS absorption, global low latency
  ↳ Cons: cost, cache key complexity for dynamic content, debugging hit/miss across POPs
📊 World map showing user requests routed to nearest CDN edge (colored dots on each continent) with origin server in one location;...

## Slide 254
Layer 3 — Reverse Proxy / Web Server Cache
▸ A reverse proxy sits between clients and app servers, caching HTTP responses
  ↳ Nginx, Varnish, HAProxy, Apache Traffic Server, Envoy
▸ Caches full HTML pages, API responses, even fragments (Edge Side Includes)
  ↳ One cached response can serve millions of identical requests
▸ Varnish is the gold standard for HTTP caching
  ↳ VCL (Varnish Configuration Language) lets you express complex cache rules
  ↳ Used by Wikipedia, NYT, Reddit to absorb traffic spikes
▸ Sits in your data center — different role than CDN (which sits globally)
  ↳ CDN handles geographic distribution; reverse proxy handles per-DC absorption
▸ Real example: Wikipedia serves ~20 billion pageviews/month with Varnish doing most of the work
  ↳ Database is rarely touched for anonymous reads of popular articles
📊 Diagram: Internet → Load Balancer → Varnish/Nginx (cache) → App Server cluster → Database; with cache hit returning at proxy le...

## Slide 255
Layer 4 — Application-Level (In-Memory) Caching
▸ Cache lives inside the application process — fastest possible access, no network hop
  ↳ Java: Caffeine, Guava Cache, Ehcache; Python: functools.lru_cache, cachetools; Go: bigcache, ristretto
▸ Sub-microsecond access (it's just a HashMap with eviction)
  ↳ Perfect for hot config, feature flags, computed lookup tables
▸ Limitation: each app instance has its own copy — N caches for N servers
  ↳ Memory waste, inconsistent values across instances, cold cache on every deploy
▸ Use when: data is small, mostly static, or per-instance state is acceptable
  ↳ Bad fit for user sessions (sticky sessions become required), good fit for currency conversion tables
▸ Real example: Caffeine in Twitter, Guava in many Google services
  ↳ Often used as L1 in front of Redis (L2) — local cache catches hot keys, distributed cache catches the rest
📊 Three app server boxes each with embedded "in-process cache" rectangle; arrows showing each independently caching, no synchroni...

## Slide 256
Layer 5 — Database Caching
▸ Databases have multiple internal caches you should understand
  ↳ Buffer pool / page cache: hot disk pages kept in RAM (Postgres shared_buffers, MySQL InnoDB buffer pool)
▸ Query result cache: caches result sets of identical queries
  ↳ MySQL's old query cache was deprecated due to mutex contention; modern systems use external caches
▸ Materialized views: pre-computed query results stored on disk, refreshed periodically
  ↳ Postgres MATERIALIZED VIEW; great for expensive aggregations (daily revenue, dashboards)
▸ Prepared statement cache: parsed/planned queries reused for performance
  ↳ Saves 1–10ms per query in OLTP workloads
▸ OS page cache sits below the database, caching disk blocks transparently
  ↳ Linux uses all free RAM for page cache; "free memory" is a meaningless metric
📊 Database internals diagram showing query → query cache → query planner → buffer pool → OS page cache → disk, with each layer la...

## Slide 257
Layer 6 — Distributed Caching
▸ Shared cache cluster accessible from all app servers — single source of cached truth
  ↳ Redis, Memcached, Hazelcast, Aerospike
▸ Solves the problem of inconsistent per-instance caches in app-level caching
  ↳ All servers see the same value; invalidation is centralized
▸ Adds a network hop (~0.5–1ms) but enables horizontal scaling
  ↳ Cache cluster scales independently of app servers
▸ Survives app server restarts — data persists in the cache layer
  ↳ Cold-start problem moves from "every deploy" to "rare cache failure"
▸ Real examples
  ↳ Twitter: Redis stores timelines, Memcached for objects (~100s of TB across thousands of nodes)
  ↳ Facebook: Memcached at planetary scale, originally invented McDipper, then TAO
📊 N app servers all connecting to a 3-node Redis cluster in the middle; database behind it as origin; arrows showing all reads hi...

## Slide 258
Caching Layers — Trade-offs Summary
▸ Browser cache: free, fastest for user, but uncontrollable once deployed
  ↳ Trade-off: speed vs. ability to push updates
▸ CDN: massive scale and global, but costs money and complicates dynamic content
  ↳ Trade-off: edge speed vs. invalidation complexity
▸ Reverse proxy: high throughput, full HTML caching, but per-DC only
  ↳ Trade-off: simplicity vs. geographic reach
▸ App-level cache: nanosecond access, but per-instance and inconsistent
  ↳ Trade-off: speed vs. consistency
▸ Distributed cache: shared and consistent, but adds network hop and operational burden
  ↳ Trade-off: consistency vs. latency and ops cost
▸ Database cache: closest to truth, but limited size and contention prone
  ↳ Trade-off: freshness vs. throughput
📊 Comparison matrix table — rows: Browser, CDN, Proxy, App, Distributed, DB; columns: Latency, Scale, Consistency, Ops cost, Use ...

## Slide 259
Caching Strategies — Read Patterns Overview
▸ Caching strategy = the protocol for how reads and writes interact with cache and origin
  ↳ Different strategies optimize for different consistency/latency/complexity trade-offs
▸ Five canonical strategies you must know cold for interviews
  ↳ Cache-aside, Read-through, Write-through, Write-behind, Refresh-ahead
▸ Two axes to think about
  ↳ Read path: who fills the cache (application vs cache itself)
  ↳ Write path: what gets updated and in what order (cache, DB, both, async)
▸ No strategy is universally best — each has a sweet spot
  ↳ Cache-aside is the default; others solve specific problems
▸ We'll cover each with mechanics, pros/cons, and a real-world example
  ↳ Memorize the diagrams, not just the names
📊 2x2 grid — axes "Read" (lazy/eager) and "Write" (sync/async) — with each strategy placed in its quadrant

## Slide 260
Strategy 1 — Cache-Aside (Lazy Loading)
▸ Application is responsible for both cache and DB; cache does not know about DB
  ↳ Read flow: check cache → on miss, query DB → write result to cache → return
▸ Most popular pattern; default choice for Redis/Memcached deployments
  ↳ Used by Facebook (Memcached + MySQL), most production stacks
▸ Pros
  ↳ Only caches what's actually read (no wasted space)
  ↳ Cache failure doesn't break the system (just slower)
  ↳ Easy to add to an existing application
▸ Cons
  ↳ First request always slow (cache miss penalty)
  ↳ Stale data risk if DB is updated without invalidating cache
  ↳ Two systems to coordinate — bugs in invalidation cause divergence
▸ Real example: Facebook's Memcached layer in front of MySQL
  ↳ Famous "Scaling Memcache at Facebook" paper — built the canonical cache-aside pattern at scale
📊 Sequence diagram — App → Cache (miss) → DB (read) → App writes back to Cache → returns to user; second request hits cache directly

## Slide 261
Cache-Aside — Pseudocode and Pitfalls
▸ Standard read implementation (Python-style)
  ↳ `value = cache.get(key); if not value: value = db.get(key); cache.set(key, value, ttl); return value`
▸ Standard write implementation
  ↳ `db.write(key, value); cache.delete(key) # next read repopulates`
▸ Pitfall 1: thundering herd on miss for hot keys
  ↳ 1000 concurrent readers all miss → 1000 DB queries; solved with mutex / single-flight
▸ Pitfall 2: race condition between read and write
  ↳ Reader sees old DB value, writer updates DB and invalidates cache, reader writes stale value back
  ↳ Solved via versioning, CAS, or "delete-after-write" with delay (Facebook's "leases")
▸ Pitfall 3: forgetting to invalidate on update → permanent stale cache
  ↳ Always pair every DB write with a cache invalidation in the same code path
▸ Default TTL is your safety net — even buggy invalidation eventually self-heals
  ↳ Pick TTL based on tolerance for staleness (seconds to hours)
📊 Code snippet on left showing read/write functions; race condition timeline on right showing how stale write can sneak in

## Slide 262
Strategy 2 — Read-Through Cache
▸ Cache itself knows how to load from the database on miss — application talks only to cache
  ↳ Read flow: app calls cache.get(key) → cache misses → cache calls DB loader → returns to app
▸ Cache acts as a smart proxy in front of the data store
  ↳ App code is simpler — no explicit DB call in the read path
▸ Pros
  ↳ Application code is clean — single API (`cache.get`)
  ↳ Cache logic centralized; consistent behavior across services
▸ Cons
  ↳ Cache must support pluggable loaders (Caffeine, Ehcache, AWS DAX do; raw Redis does not)
  ↳ First request still slow (same cold-start as cache-aside)
  ↳ Tighter coupling between cache and data store
▸ Real example: AWS DAX in front of DynamoDB; Caffeine's CacheLoader in JVM apps
  ↳ DAX gives DynamoDB sub-millisecond reads with zero application code change
📊 Sequence diagram — App → Cache → (cache internally fetches from DB on miss) → returns to App; cleaner single-arrow path from ap...

## Slide 263
Strategy 3 — Write-Through Cache
▸ Every write goes to BOTH cache and database synchronously, in the same operation
  ↳ Write flow: app writes → cache writes → DB writes → all complete before ack
▸ Cache is always consistent with database — no stale data possible
  ↳ Reads can hit cache safely, knowing it matches truth
▸ Pros
  ↳ Strong consistency between cache and DB
  ↳ No invalidation logic needed — cache always fresh
  ↳ Simple mental model
▸ Cons
  ↳ Every write pays double latency (cache write + DB write)
  ↳ Caches data even if it's never read again — wasted memory for write-once data
  ↳ Cache failure can fail the write (depending on implementation)
▸ Real example: DynamoDB DAX in write-through mode, some Hibernate L2 cache configs
  ↳ Best when read-after-write is required and write traffic is moderate
📊 Sequence diagram showing parallel/sequential write to Cache and DB, both acknowledging before app returns success

## Slide 264
Strategy 4 — Write-Behind (Write-Back) Cache
▸ Write goes to cache immediately; cache asynchronously flushes to DB later
  ↳ Write flow: app writes → cache acks immediately → background worker batches writes to DB
▸ Optimizes for write-heavy workloads at the cost of durability
  ↳ Multiple writes to the same key can coalesce, reducing DB load drastically
▸ Pros
  ↳ Very fast writes (cache speed, not DB speed)
  ↳ Batching reduces DB write amplification
  ↳ Smooths write spikes (cache absorbs bursts)
▸ Cons
  ↳ Risk of data loss if cache crashes before flush
  ↳ Eventual consistency — DB lags cache, complicates DR and analytics
  ↳ Complex failure recovery
▸ Real example: Linux page cache writing to disk; some metric/analytics pipelines (StatsD-like flushers)
  ↳ Use when losing the last few seconds of writes is acceptable (counters, metrics, view counts)
📊 Sequence diagram — write to cache returns instantly; dashed async arrow from cache to DB labeled "batched flush every N seconds"

## Slide 265
Strategy 5 — Refresh-Ahead Cache
▸ Proactively refresh cache entries BEFORE they expire, predicting next access
  ↳ On read, if entry is "close to expiring" (e.g., 80% of TTL), trigger async refresh
▸ Hides cache miss latency for hot data — readers always hit warm cache
  ↳ Particularly effective for predictable, frequently accessed keys
▸ Pros
  ↳ Eliminates miss penalty for hot keys
  ↳ Smooths out backend load (refreshes spread over time, not bursts at expiry)
▸ Cons
  ↳ May refresh entries that won't be read again (wasted DB call)
  ↳ Requires good prediction heuristic — naive implementations cause thrashing
  ↳ More complex than TTL-only eviction
▸ Real example: Caffeine's `refreshAfterWrite`, Guava's `LoadingCache.refresh()`
  ↳ Used heavily in feed/timeline systems where the same keys are read every second
📊 Timeline showing TTL bar — at 80% mark, async refresh fires while reads continue hitting old cached value, then new value seaml...

## Slide 266
Strategies — Decision Matrix
▸ Cache-aside: best general-purpose default for read-heavy workloads
  ↳ Use when: reads dominate, app can tolerate some staleness, you control DB writes
▸ Read-through: cleaner code than cache-aside, requires cache library support
  ↳ Use when: building on Caffeine, DAX, Hazelcast — get the benefit for free
▸ Write-through: when reads must always see latest write, write volume moderate
  ↳ Use when: user just wrote a comment and refreshes — must see their own write
▸ Write-behind: write-heavy, durability not critical, want batching
  ↳ Use when: counters, view counts, telemetry, leaderboard increments
▸ Refresh-ahead: hot keys with predictable access, latency-sensitive reads
  ↳ Use when: dashboards, feeds, autocomplete — same keys hit constantly
📊 Decision tree — "Read-heavy?" → cache-aside / read-through; "Write-heavy?" → write-behind; "Need consistency?" → write-through;...

## Slide 267
Strategies — Real-World Example: Twitter Timeline
▸ Timeline read uses cache-aside on Redis fronted by per-server Caffeine (L1+L2)
  ↳ User opens Twitter → app checks local cache → Redis → only on miss, recompute timeline
▸ Timeline write (new tweet) uses fanout-on-write into followers' Redis lists
  ↳ Resembles write-through into denormalized cache structures, not the source DB
▸ Hot accounts (Obama, Beyoncé) bypass fanout-on-write to avoid hot-key explosion
  ↳ Their tweets are fanned out lazily on read (fanout-on-read) — different strategy for different scale
▸ Counters (likes, retweets) use write-behind into Redis with periodic DB flush
  ↳ Tolerates losing last few seconds of likes during a Redis failover
▸ Multiple strategies coexist in one product because workloads differ per feature
  ↳ This is the real lesson: strategy is per-data-type, not per-system
📊 Twitter architecture sketch — User → App → L1 (Caffeine) → L2 (Redis fanout cache) → MySQL/Manhattan; with overlay showing diff...

## Slide 268
Cache Invalidation — Why It's Hard
▸ Phil Karlton: "There are only two hard things in computer science: cache invalidation and naming things"
  ↳ Quote is famous because invalidation breaks every "obvious" approach
▸ The fundamental problem: cache and source-of-truth can diverge silently
  ↳ You don't know your cache is wrong until a user complains
▸ Sources of invalidation difficulty
  ↳ Distributed writers updating DB without telling cache
  ↳ Race conditions between read-from-DB and write-to-cache
  ↳ Multi-region replication lag
  ↳ Caches at multiple layers all need to be invalidated coherently
▸ Trade-off triangle: freshness, performance, complexity — pick two
  ↳ Stronger freshness → either slower (synchronous invalidation) or more complex (event-driven)
▸ Invalidation bugs are the #1 cause of "weird" production issues with caches
  ↳ User updates email → still sees old email → support ticket → days of debugging
📊 Three-circle Venn diagram — "Fresh", "Fast", "Simple" — with caption "you can have any two"

## Slide 269
TTL-Based Expiry
▸ Every cache entry has a Time-To-Live; cache evicts/expires entries when TTL passes
  ↳ Simplest invalidation strategy: don't invalidate, just let entries die naturally
▸ Strengths
  ↳ Zero coordination — works without any write-side logic
  ↳ Self-healing — even if invalidation logic is buggy, staleness is bounded
  ↳ Predictable memory bounds
▸ Weaknesses
  ↳ Stale data window equal to TTL — users see old data for up to TTL seconds
  ↳ All-or-nothing per entry — can't be "kind of expired"
▸ Choosing a TTL
  ↳ Short TTL (seconds): low staleness, low hit ratio, high DB load
  ↳ Long TTL (hours/days): high hit ratio, high staleness risk
▸ Real example: DNS uses TTL exclusively (typical 300s for A records)
  ↳ DNS chose simplicity over freshness — propagation takes minutes globally
📊 Timeline showing entry lifecycle — write at t=0 with TTL=60s, reads hit cache, automatic eviction at t=60s, next read causes re...

## Slide 270
Event-Driven Invalidation
▸ On every write to source-of-truth, emit an event that invalidates affected cache keys
  ↳ Write to DB → publish "user:42 updated" → all caches receive event and evict user:42
▸ Implementations
  ↳ Synchronous: app deletes from cache after DB write (cache-aside default)
  ↳ Asynchronous: change-data-capture (Debezium reading MySQL binlog → Kafka → cache invalidator)
▸ Strengths
  ↳ Near-real-time freshness (milliseconds, not minutes)
  ↳ Targeted — only invalidates what changed, preserves cache for rest
▸ Weaknesses
  ↳ Coupling between writer and cache invalidator
  ↳ Lost events = permanent stale cache (need TTL as backstop)
  ↳ Hard to invalidate derived/aggregated keys (which list views contain user 42?)
▸ Real example: LinkedIn's Brooklin, Netflix's ev-cache invalidation via Kafka
  ↳ At scale, CDC pipelines are the standard for event-driven cache invalidation
📊 Diagram — DB write → CDC reader → Kafka topic → multiple cache invalidator workers → Redis cluster keys deleted

## Slide 271
Versioning and Stale-While-Revalidate
▸ Versioning approach: cache key includes a version, bumping the version invalidates instantly
  ↳ Old: `user:42` → New: `user:42:v17` — increment version, all readers fetch new key, old key expires naturally
▸ Avoids the race conditions of explicit deletes
  ↳ Atomic version bump = atomic invalidation; no "delete then write" window
▸ Stale-while-revalidate (SWR) pattern: serve stale data while refreshing in background
  ↳ HTTP `Cache-Control: max-age=60, stale-while-revalidate=600`
  ↳ For 60s, fresh; for next 600s, serve stale and refresh async; after that, must revalidate
▸ Combines best of TTL and refresh-ahead
  ↳ User never waits for refresh; cache is "soft expired" rather than "hard expired"
▸ Real example: Vercel/Next.js ISR (Incremental Static Regeneration), SWR React library
  ↳ Modern web frameworks bake SWR into their data-fetching primitives
📊 Two-bar timeline — Bar 1: "fresh window (60s)" green, Bar 2: "stale-while-revalidate window (600s)" yellow with async refresh a...

## Slide 272
Invalidation — Trade-offs Summary
▸ TTL: simplest, self-healing, but bounded staleness
  ↳ Use for: data with predictable update cadence, low write rates, tolerable staleness
▸ Event-driven (sync delete): fresh, but tight coupling, race-prone
  ↳ Use for: cache-aside in monoliths, write paths fully under your control
▸ Event-driven (async CDC): fresh, decoupled, scales to many caches
  ↳ Use for: distributed systems, multiple consumers of the same data
▸ Versioning: race-free, atomic, but key-management overhead
  ↳ Use for: user profiles, configurations, anywhere instant global flip is needed
▸ Stale-while-revalidate: fast and fresh-enough, but explicit staleness window
  ↳ Use for: dashboards, feeds, public content with eventual consistency
▸ Pragmatic rule: ALWAYS combine TTL with active invalidation as a safety net
  ↳ TTL bounds the bug — even if invalidation is broken, cache eventually self-corrects
📊 Comparison table — strategy / freshness / complexity / coupling / safety net

## Slide 273
Cache Eviction — Why We Need It
▸ Caches are bounded memory — when full, something must be removed to make room for new entries
  ↳ Eviction policy = the rule for choosing the victim
▸ Goal: evict the entry least likely to be requested again, keep entries most likely to be requested
  ↳ Different policies make different predictions about future access patterns
▸ Eviction is not invalidation
  ↳ Invalidation: entry is wrong, must remove
  ↳ Eviction: entry might still be valid, but we need the space
▸ A poor eviction policy can tank hit ratio even with plenty of memory
  ↳ A 100GB cache with random eviction may do worse than a 10GB cache with LRU
▸ Real workloads have skewed access patterns (Zipf-like) — exploit this in policy choice
  ↳ 80/20 rule: keep the 20% hottest keys, evict the long tail aggressively
📊 Cache visualized as a fixed-size box; new item arriving, "victim" item being pushed out via different doors labeled with policy...

## Slide 274
LRU — Least Recently Used
▸ Evict the entry whose last access is furthest in the past
  ↳ Assumption: data accessed recently is likely to be accessed again soon (temporal locality)
▸ Most popular eviction policy — sane default for almost all workloads
  ↳ Used by Redis (allkeys-lru), Memcached, OS page caches, CPU caches
▸ Implementation: doubly-linked list + hash map → O(1) get/set/evict
  ↳ Move accessed entry to front; evict from back
▸ Strengths
  ↳ Adapts to changing access patterns
  ↳ Simple, well-understood, O(1)
▸ Weaknesses
  ↳ One scan over a large dataset can pollute the cache (cache thrashing)
  ↳ Doesn't distinguish frequently used from one-time hot data
▸ Real example: Redis maxmemory-policy allkeys-lru — battle-tested default
  ↳ Variants like LRU-K, ARC, 2Q address scan pollution
📊 Linked list diagram — head (most recent) ← A ← B ← C ← D (least recent, eviction target); on access to C, it moves to head

## Slide 275
LFU — Least Frequently Used
▸ Evict the entry with the lowest access count
  ↳ Assumption: frequently accessed in the past = frequently accessed in the future
▸ Better than LRU for stable, skewed workloads (e.g., 20% of keys serve 80% of traffic)
  ↳ Hot keys accumulate count and stay; cold keys evicted regardless of recency
▸ Weakness: stale popularity — once-hot keys stay forever even after they cool down
  ↳ Solved by aging/decay schemes (TinyLFU, W-TinyLFU)
▸ Modern variants
  ↳ TinyLFU (used by Caffeine): tiny count-min sketch + window LRU; near-optimal hit ratios
  ↳ Caffeine often beats Guava by 10–20% hit rate on production workloads
▸ Implementation: requires frequency counters + min-heap or buckets
  ↳ More complex than LRU, but Caffeine has made it practical
▸ Use when: workload has stable hot keys (recommendation systems, popular content)
  ↳ Don't use for: workloads with shifting popularity (trending news, real-time feeds)
📊 Histogram of access frequencies — eviction arrow points at the lowest-frequency bar; aging shown as bars decaying over time

## Slide 276
FIFO and Random Eviction
▸ FIFO (First In First Out): evict the oldest entry by insertion time, ignore access pattern
  ↳ Simple queue; O(1); used in some hardware caches and simple buffers
▸ FIFO weakness: a hot entry inserted long ago gets evicted even if just accessed
  ↳ Generally underperforms LRU; rarely used in software caches today
▸ Random eviction: pick a random entry to evict
  ↳ Surprisingly competitive with LRU at scale (Redis allkeys-random)
▸ Random's strength: zero metadata overhead, cache-friendly, no contention
  ↳ Useful when memory tracking overhead would dwarf benefit
▸ Variants: random sample N, evict worst by some metric
  ↳ Redis's LRU is actually approximate — samples 5 keys, evicts oldest among them
▸ Use when: workload is uniform, or per-entry tracking is too expensive
  ↳ Reality: rarely the optimal choice but easy to implement and surprisingly OK
📊 Two queues side by side — FIFO showing insertion-order eviction; Random showing dart hitting a random entry

## Slide 277
Eviction Policy — Choosing the Right One
▸ LRU: default for general-purpose caches with temporal locality
  ↳ Web sessions, recently viewed items, query result caches
▸ LFU (or W-TinyLFU via Caffeine): when popularity is stable and skewed
  ↳ Recommendation engines, popular content caches, CDN edge caches
▸ FIFO: simple buffers, time-windowed data, when access pattern doesn't matter
  ↳ Recent log entries, audit trails (rarely a primary cache choice)
▸ Random: high-throughput caches where metadata cost matters
  ↳ Massive Memcached-style caches, hardware-constrained systems
▸ TTL-only: when freshness matters more than hit ratio
  ↳ DNS, configuration caches, anything with deterministic update windows
▸ Hybrid policies dominate modern systems
  ↳ Caffeine's W-TinyLFU = window LRU + frequency-aware admission filter; SOTA in JVM
📊 Decision flowchart — "Stable hot keys?" → LFU; "Recency matters?" → LRU; "Time-windowed?" → FIFO; "Tracking too expensive?" → R...

## Slide 278
Eviction — Real-World Examples
▸ Redis: configurable per-deployment via `maxmemory-policy`
  ↳ Options: noeviction, allkeys-lru, allkeys-lfu, allkeys-random, volatile-lru (only TTL keys), etc.
▸ Memcached: slab-allocator + LRU per slab class
  ↳ Each size class has its own LRU; avoids fragmentation but creates per-slab eviction pressure
▸ Linux page cache: 2Q (active + inactive lists) — approximate LRU with scan resistance
  ↳ Why a simple `cat huge_file` doesn't blow away your hot working set
▸ CDN edge nodes: typically LRU or LFU per POP
  ↳ Cloudflare uses Tiered Cache + LRU; Fastly uses similar approaches
▸ CPU caches: hardware pseudo-LRU (true LRU is too expensive in silicon)
  ↳ Tree-based bit-encoded approximation; gets within ~5% of true LRU
📊 Logos of Redis, Memcached, Linux, Cloudflare with their eviction policies labeled below

## Slide 279
Distributed Caching — Why Go Distributed?
▸ Single-node cache is limited by RAM, CPU, and network of one machine
  ↳ Single Redis node tops out around 100GB and ~100K ops/sec; need more for scale
▸ Distributed cache spreads data across multiple nodes
  ↳ 10 nodes × 100GB = 1TB working set; 10 × 100K = 1M ops/sec aggregate
▸ Solves three problems at once
  ↳ Capacity (more total memory than any single machine)
  ↳ Throughput (parallel ops across nodes)
  ↳ Availability (replication so single-node failure doesn't lose all cache)
▸ Adds new problems
  ↳ How to route a key to the correct node (sharding)
  ↳ How to handle node failures without invalidating all keys (consistent hashing)
  ↳ How to keep replicas consistent
▸ Two giants dominate the space: Redis and Memcached
  ↳ Modern alternatives: Hazelcast, Aerospike, Apache Ignite, KeyDB, DragonflyDB
📊 Single big-box cache labeled "doesn't scale" vs. cluster of N smaller boxes labeled with sharding/replication arrows

## Slide 280
Redis vs. Memcached — Feature Comparison
▸ Data types
  ↳ Memcached: strings only (max 1MB by default)
  ↳ Redis: strings, lists, sets, sorted sets, hashes, streams, hyperloglog, bitmaps, geo, JSON
▸ Persistence
  ↳ Memcached: in-memory only, lost on restart
  ↳ Redis: optional RDB snapshots + AOF append-only log; configurable durability
▸ Threading
  ↳ Memcached: multi-threaded (good per-node throughput)
  ↳ Redis: single-threaded core (Redis 6+ has I/O threads); simpler reasoning, less locking
▸ Replication and clustering
  ↳ Memcached: client-side sharding only
  ↳ Redis: built-in replication, Redis Cluster with hash slots, Sentinel for HA
▸ Use cases
  ↳ Memcached: simple object cache, session storage, ephemeral cache
  ↳ Redis: cache + queue + pub/sub + leaderboard + rate limiter — Swiss army knife
📊 Side-by-side table comparing Memcached and Redis across data types, persistence, threading, replication, ecosystem

## Slide 281
Redis vs. Memcached — When to Choose Which
▸ Choose Memcached when
  ↳ You need a pure cache, nothing else
  ↳ Object size is small and uniform
  ↳ You want simple horizontal scaling with client-side hashing
  ↳ Predictable performance under high concurrency
▸ Choose Redis when
  ↳ You need data structures (sorted sets for leaderboards, lists for queues)
  ↳ You want persistence as a safety net
  ↳ You need pub/sub, streams, scripting (Lua), or transactions
  ↳ You want an integrated solution rather than 5 separate systems
▸ Real-world deployments
  ↳ Facebook: massive Memcached fleet, custom enhancements (mcrouter)
  ↳ Twitter: Redis for timelines, Memcached for objects (different fits, same company)
  ↳ GitHub, Stack Overflow, Instagram: Redis
▸ Default modern choice: Redis (versatility wins for most teams)
  ↳ Memcached still excels for very-large simple object caches at extreme scale
📊 Two columns of company logos under "Memcached shops" (Facebook, Pinterest historically) vs "Redis shops" (Twitter, GitHub, Snap...

## Slide 282
Consistent Hashing — Sharding Across Nodes
▸ Problem: with N cache nodes, how do we route a key to the right one?
  ↳ Naive: `node = hash(key) % N` — but adding/removing a node remaps almost all keys
▸ Consistent hashing: hash both keys and nodes onto the same ring (e.g., 0–2^32)
  ↳ Each key is owned by the next node clockwise on the ring
▸ When a node is added/removed, only ~1/N of keys move
  ↳ Dramatic improvement over modulo hashing
▸ Virtual nodes (vnodes) smooth load distribution
  ↳ Each physical node owns 100–1000 vnodes around the ring → uniform key distribution
▸ Used in
  ↳ Memcached client libraries (libketama)
  ↳ Redis Cluster (hash slots — fixed 16384 slots, simpler variant of consistent hashing)
  ↳ DynamoDB, Cassandra, Riak (full database use, same idea)
📊 Circular ring with node markers (N1, N2, N3, N4) and key markers (K1, K2, K3) — each key drawn with arrow to next clockwise nod...

## Slide 283
Cache Stampede / Thundering Herd
▸ A hot key expires; thousands of concurrent readers all miss simultaneously
  ↳ All of them race to query the DB and rebuild the cache → DB collapses
▸ Famous failure mode — has caused outages at Facebook, Instagram, Reddit
  ↳ Worst when key is extremely popular and DB query is expensive
▸ Symptoms
  ↳ Sudden DB CPU spike at exact TTL boundaries
  ↳ Cascading latency spikes every TTL period
  ↳ Rare but catastrophic when it happens
▸ Three classic solutions
  ↳ Mutex / single-flight: only one request rebuilds, others wait
  ↳ Probabilistic early expiration: each reader independently decides "should I refresh now?"
  ↳ Stale-while-revalidate: serve stale, refresh in background
▸ Real example: Instagram's "promotional cache" pattern, Facebook's "leases" in Memcached
  ↳ Memcached leases (described in their scaling paper) coordinate which client repopulates
📊 Timeline showing TTL expiry; without mitigation: spike of 1000 concurrent DB queries; with mutex: one query, 999 waiters; with ...

## Slide 284
Stampede Solution — Mutex / Single-Flight
▸ On cache miss, acquire a lock for that key before querying DB
  ↳ First requester gets lock, queries DB, populates cache, releases lock
  ↳ Concurrent requesters either wait on the lock or retry the cache after a short sleep
▸ Implementation
  ↳ Redis: `SET key:lock value NX EX 10` — atomic acquire with TTL safety
  ↳ Go: golang.org/x/sync/singleflight — in-process coalescing
▸ Strengths: simple, prevents stampede, works for any read path
  ↳ Weakness: lock contention itself can become a bottleneck on extreme hot keys
▸ Distributed lock pitfalls
  ↳ Lock holder crashes → use TTL on lock to avoid permanent lockout
  ↳ Be aware of Redlock controversy (Martin Kleppmann critique) for stricter use cases
▸ Pattern works at any scale from in-process to global
  ↳ Cloudflare uses single-flight extensively at edge for backend protection
📊 Sequence diagram — Request 1 acquires lock, queries DB, fills cache, releases lock; Requests 2–1000 wait briefly, then read fre...

## Slide 285
Stampede Solution — Probabilistic Early Expiration
▸ Each reader independently decides whether to proactively refresh, weighted by closeness to TTL
  ↳ Probability of refresh increases as TTL approaches; far from expiry, almost zero chance
▸ XFetch algorithm (Vattani et al., 2015): mathematically optimal early refresh
  ↳ `if now - delta * beta * log(rand()) >= expiry: refresh()`
  ↳ Spreads refresh load smoothly over the last fraction of TTL
▸ Strengths
  ↳ No locking required — fully decentralized
  ↳ No synchronized expiry boundary, no thundering herd
▸ Weaknesses
  ↳ Some refreshes happen "early" — small wasted work
  ↳ Requires changing read path to know TTL/expiry timestamps
▸ Used in production by HashiCorp, Cloudflare, and others for hot-key caches
  ↳ Combines beautifully with stale-while-revalidate semantics
📊 Probability curve over TTL — flat at 0 for first 80%, rising sharply in last 20%, several reader dots triggering refresh at sta...

## Slide 286
Hot Key Problem
▸ One key receives massively disproportionate traffic, overwhelming a single cache node
  ↳ "Justin Bieber problem" — millions of fans, all hitting one timeline key
▸ Consistent hashing routes key X to node N; if X is super-hot, N is super-loaded
  ↳ Other nodes idle, N's CPU/network melts; classic load skew
▸ Solutions
  ↳ Local replica caching: app-level L1 in front of distributed L2 catches the hot key
  ↳ Key splitting: shard hot key into key:0..N variants, randomized read fanout
  ↳ Read replicas: replicate hot keys to multiple cache nodes; route reads round-robin
  ↳ Promotional caching: pre-emptively warm and pin known hot keys
▸ Detection
  ↳ Per-key counters at proxy/router (Twemproxy, Mcrouter)
  ↳ Sample-based heavy hitter detection (count-min sketch)
▸ Real example: Twitter's "celebrity" handling — separate cache tier for top accounts
  ↳ Hot keys are usually predictable (celebrities, breaking news, viral content)
📊 Bar chart showing one massive bar (hot key) dwarfing all others; mitigation diagram showing the hot key replicated across multi...

## Slide 287
Distributed Caching — Trade-offs Summary
▸ Centralized cache (single Redis node): simple, consistent, but limited capacity and SPOF
  ↳ Use for: small services, low-scale workloads
▸ Sharded cache (consistent hashing): scales linearly, but no replication = data loss on node failure
  ↳ Use for: pure caches where loss is acceptable, scale > durability
▸ Replicated cache (master + replicas): high availability, but eventual consistency between replicas
  ↳ Use for: read-heavy hot data, where reads can hit any replica
▸ Sharded + replicated (Redis Cluster): scale + HA, but complex ops and edge cases
  ↳ Use for: large production systems; the standard choice today
▸ Multi-region: cross-region replication for global apps, but huge consistency challenges
  ↳ Use for: global products willing to accept eventual cross-region staleness
📊 Spectrum diagram — left "Simple/Limited" (single node) → right "Complex/Scalable" (sharded+replicated+multi-region) with exampl...

## Slide 288
Caching — Key Takeaways
▸ Caching is the cheapest performance lever in system design
  ↳ One Redis layer can 10x your throughput without touching the database
▸ Cache hit ratio is the metric — track it, alert on it, optimize for it
  ↳ Below 80%, your cache is barely earning its keep
▸ Cache-aside is the default strategy; learn the others for the workloads where they fit
  ↳ Match write-through, write-behind, refresh-ahead to specific data shapes
▸ Invalidation is hard — combine TTL (safety net) with active invalidation (freshness)
  ↳ Versioned keys and stale-while-revalidate are powerful tools
▸ Distributed caching adds capacity/availability but requires consistent hashing, stampede protection, hot-key handling
  ↳ Redis vs. Memcached: choose Redis unless you have a reason not to
▸ Cache as close to the user as correctness allows; layered caches multiply your effective hit ratio
  ↳ Browser → CDN → proxy → app → distributed → DB — each layer matters
📊 Top-5 list with bold callouts for each takeaway; Twitter/Facebook/YouTube logos as supporting evidence

## Slide 289
Caching — Interview Tips
▸ When asked about latency or throughput, propose caching FIRST — it's the lowest-cost win
  ↳ "Before scaling the database, I'd add a cache layer to absorb read traffic"
▸ Always state your strategy explicitly: "I'd use cache-aside with Redis, 5-minute TTL, LRU eviction"
  ↳ Vague answers ("I'd add caching") get probed; specific answers get nods
▸ Be ready to discuss invalidation — interviewers will press here
  ↳ Have a default answer: "TTL as safety net + active invalidation on write + versioned keys for instant flips"
▸ Mention real systems to anchor your design
  ↳ "Like Twitter's Caffeine + Redis layered cache" or "Like Facebook's Memcached architecture"
▸ Address consistency explicitly — name the trade-off, don't dodge it
  ↳ "This gives eventual consistency; for read-after-write, I'd use write-through for that path"
▸ Discuss failure modes proactively (cold start, stampede, hot keys)
  ↳ Showing you've thought about edge cases is a senior-level signal
▸ Know the numbers: RAM ~100ns, network ~1ms, disk ~10ms, cross-region ~100ms
  ↳ Latency budgeting is a frequent follow-up
📊 Interview cheat sheet — numbered tips with example phrases in italics

## Slide 290
Caching — Common Pitfalls
▸ Caching everything indiscriminately
  ↳ Pitfall: low-locality data wastes memory; measure access patterns first
▸ Forgetting to invalidate on writes
  ↳ Pitfall: silent staleness, hard to debug; pair every write with invalidation in same code path
▸ No TTL as a backstop
  ↳ Pitfall: a single missed invalidation persists forever; always set a sane TTL
▸ Ignoring cache stampede
  ↳ Pitfall: works fine until the hot key expires; add mutex / SWR / probabilistic refresh
▸ Over-trusting the cache for source of truth
  ↳ Pitfall: cache is disposable; never write data only to cache (unless write-behind with durable backing)
▸ Massive cache key cardinality
  ↳ Pitfall: caching unique queries with no reuse → 0% hit rate, just adds latency
▸ Not monitoring hit ratio
  ↳ Pitfall: you can't fix what you don't measure; alert when hit ratio drops
▸ Mixing TTLs across related keys (cache aliasing)
  ↳ Pitfall: user object expires at t=60, user's posts at t=120 → inconsistent view
▸ Using local cache for personalized data without sticky sessions
  ↳ Pitfall: user's request hits a different server with stale local cache; use distributed cache instead
▸ Premature caching as a substitute for fixing the real bottleneck
  ↳ Pitfall: caching a slow query is a band-aid; fix the query, then cache it
📊 "Cache landmines" infographic — each pitfall as a labeled mine icon with a brief mitigation note next to it

## Slide 291
Caching — Mental Model Recap
▸ Cache = a small, fast layer that remembers expensive answers
  ↳ Trade memory for time, trade freshness for speed
▸ Three questions to answer for every cache you design
  ↳ WHERE: which layer (browser / CDN / proxy / app / distributed / DB)?
  ↳ HOW: which strategy (cache-aside / read-through / write-through / write-behind / refresh-ahead)?
  ↳ WHEN: invalidation (TTL / event-driven / versioned / SWR) and eviction (LRU / LFU / FIFO / random)?
▸ Caching is multi-layered by default in modern systems
  ↳ Each layer absorbs a slice; misses cascade downward
▸ Distributed caching turns one fast box into many; consistent hashing makes it scale
  ↳ Mind the stampede, mind the hot key, mind the network hop
▸ Master caching and you understand 40% of system design
  ↳ Every "fast" system you admire is fast because someone put a cache in the right place
📊 One-page mental model — three concentric questions (WHERE / HOW / WHEN) with strategy options branching from each

## Slide 292
Section 7 Wrap-Up
▸ We covered: definition, hierarchy, hit ratio, layers, strategies, invalidation, eviction, distributed caching
  ↳ Each topic with intuition, examples, diagrams, and trade-offs
▸ Caching is the single most-tested topic in system design interviews
  ↳ Expect questions about it in 80%+ of design rounds
▸ Always anchor caching choices in concrete trade-offs
  ↳ "I'd choose X because it optimizes for Y, accepting cost Z"
▸ Up next: Section 8 — Databases, where caching meets persistence
  ↳ Buffer pools, query caches, materialized views — caching shows up there too
▸ Remember: a well-placed cache is the closest thing to free performance
  ↳ But every cache is a deal with the consistency devil — choose your terms wisely
📊 Section-7 summary card with all 10 sub-topics as a checklist, transitioning into Section 8 preview

## Slide 293
Section 8: Asynchronism and Message Queues

## Slide 294
Section Overview — Why Asynchronism Matters
▸ Modern systems must stay responsive even when work is slow
  ↳ Users expect sub-second responses; backend work (email, ML, billing) often takes seconds to minutes
▸ Async lets us decouple "accepting work" from "doing work"
  ↳ The web tier acknowledges quickly, while heavy lifting happens elsewhere
▸ Message queues are the connective tissue of distributed systems
  ↳ They smooth out traffic spikes, isolate failures, and enable horizontal scaling
▸ This section covers queues, task systems, streaming, backpressure, and orchestration
  ↳ From SQS-style queues to Kafka-scale streaming to Temporal-style workflows
📊 Split-screen — left: synchronous "user waits 30s for email confirmation"; right: asynchronous "user sees instant 'Order placed'...

## Slide 295
Synchronous vs Asynchronous — Concept Introduction
▸ Synchronous = caller blocks until the callee returns a response
  ↳ Like phoning someone and staying on the line until they answer your question
▸ Asynchronous = caller hands off work and continues immediately
  ↳ Like dropping a letter in a mailbox; you don't wait for the recipient to read it
▸ Sync is simpler to reason about; async is more scalable under load
  ↳ Sync ties up threads/connections; async frees them to serve more requests
▸ The choice is per-operation, not per-system
  ↳ A single API can do sync DB reads but async email sending
📊 Two timelines — "Sync: Request → [wait] → Response" vs "Async: Request → Ack ↓ ... Worker processes later"

## Slide 296
Synchronous Processing — Deep Explanation
▸ Caller thread is blocked end-to-end
  ↳ HTTP connection, DB connection, memory, and CPU are all held hostage
▸ Failures cascade immediately to the user
  ↳ If the payment gateway is down, the user sees a 500 right now
▸ Latency = sum of all downstream latencies
  ↳ p99 of your API ≥ p99 of every dependency you call serially
▸ Easier to debug: stack traces show the full call path
  ↳ Great for CRUD APIs, simple reads, and operations under ~200ms
▸ Bad fit for slow, flaky, or expensive operations
  ↳ Email, video transcoding, third-party APIs, ML inference
📊 Stack of bars showing "API latency = auth (50ms) + DB (100ms) + payment (2s) + email (3s) = 5.15s response time"

## Slide 297
Asynchronous Processing — Deep Explanation
▸ Producer enqueues a task and returns to the caller
  ↳ Caller sees a 202 Accepted with a tracking ID, not a 200 OK with the final result
▸ A separate worker pool consumes and processes tasks
  ↳ Workers scale independently from web servers based on queue depth
▸ Status is tracked out-of-band
  ↳ Polling, webhooks, WebSockets, or push notifications inform the user when done
▸ Improves availability: producer survives consumer outages
  ↳ If the email service dies, orders still complete; emails go out when it recovers
▸ Adds complexity: eventual consistency, retries, idempotency, dead letters
  ↳ You trade a simple call stack for a distributed state machine
📊 Diagram — User → API (returns 202 + jobId) → Queue → Worker → DB/Notification, with dotted "status check" line from User to API

## Slide 298
Async Example — Uber Ride Request
▸ Rider taps "Request Ride" — must feel instant
  ↳ Sync work: validate user, check payment method, create ride record (~100ms)
▸ Async work fanned out to queues
  ↳ Driver matching, ETA calculation, surge pricing logging, fraud scoring, push notifications
▸ Each downstream system scales independently
  ↳ Matching service runs on GPU-backed workers; logging runs on cheap commodity boxes
▸ If notification service is down, the ride still happens
  ↳ The push is retried from the queue when notifications recover
📊 Uber app screen "Finding driver..." with branching arrows to 5 background services, each with its own queue

## Slide 299
Sync vs Async — Trade-offs
▸ Sync wins on: simplicity, immediate feedback, strong consistency
  ↳ One request, one response, one transaction — easy mental model
▸ Async wins on: throughput, resilience, decoupling, smoothing spikes
  ↳ Producers don't care if consumers are slow, scaling, or briefly down
▸ Async costs: operational complexity, harder debugging, eventual consistency
  ↳ You now own a queue, retry logic, DLQs, idempotency keys, and observability
▸ Rule of thumb: async anything that is slow (>1s), flaky, or non-critical-path
  ↳ Email, analytics, search indexing, thumbnails, webhooks
📊 Comparison table with rows Latency / Throughput / Complexity / Failure Isolation / Consistency, columns Sync / Async

## Slide 300
Message Queues — Concept Introduction
▸ A message queue is a buffer between producers and consumers
  ↳ Producers write messages; consumers read messages; the queue durably holds them in between
▸ Analogy: a post office mailbox
  ↳ Senders drop letters anytime; recipients pick up when ready; the box holds mail safely in between
▸ Messages are typically small payloads (JSON, Protobuf, Avro)
  ↳ Often a reference + metadata, not the full data — e.g., "process file s3://bucket/key"
▸ Decouples in time, space, and rate
  ↳ Producer and consumer don't need to be online together, on the same host, or running at the same speed
📊 Three boxes — Producer(s) → [Queue: ▢▢▢▢▢] → Consumer(s), with arrows showing one-way message flow

## Slide 301
Message Queues — Core Benefits
▸ Decoupling: services evolve independently
  ↳ Add new consumers without touching producers; swap implementations behind the queue
▸ Buffering: absorbs traffic spikes
  ↳ Black Friday surge fills the queue; consumers drain it at their own pace instead of crashing
▸ Reliability: messages persist through restarts and failures
  ↳ Durable queues replicate to disk; in-flight work isn't lost when a worker dies
▸ Retry & redelivery: built-in fault tolerance
  ↳ Failed messages reappear after a visibility timeout, no custom retry code needed
▸ Fan-out: one event, many consumers
  ↳ "OrderPlaced" can simultaneously trigger billing, shipping, analytics, and email services
📊 Funnel diagram — many spiky producer arrows on top → flat queue line → smooth consumer arrows on bottom (rate smoothing)

## Slide 302
Dead Letter Queues (DLQ) — Deep Explanation
▸ A DLQ is a secondary queue for messages that repeatedly fail
  ↳ After N retries (typically 3–10), the broker moves the message to the DLQ instead of redelivering forever
▸ Prevents poison messages from blocking the queue
  ↳ One malformed JSON shouldn't stall thousands of healthy orders behind it
▸ DLQ contents are inspected by humans or replay tools
  ↳ Common causes: bad data, schema drift, downstream bugs, missing dependencies
▸ Always set DLQs in production
  ↳ Without one, retries pile up forever, queue grows unbounded, and observability becomes a nightmare
▸ Monitor DLQ depth as a critical alert
  ↳ DLQ growth = silent business failures; treat it like a P1 page
📊 Main queue → consumer (red X failure 3x) → arrow to DLQ box; separate "Ops Engineer" inspecting DLQ

## Slide 303
Delivery Semantics — At-most/At-least/Exactly-once
▸ At-most-once: message delivered 0 or 1 times
  ↳ Fast and simple, but messages can be lost; OK for metrics, not for payments
▸ At-least-once: message delivered 1 or more times (duplicates possible)
  ↳ The default for most queues (SQS, RabbitMQ); requires idempotent consumers
▸ Exactly-once: message processed exactly 1 time end-to-end
  ↳ The "holy grail"; truly hard in distributed systems; usually approximated via idempotency + dedup IDs
▸ Kafka offers "exactly-once semantics" within Kafka transactions
  ↳ Real exactly-once across external systems (e.g., DB + email) needs idempotency keys
▸ Practical advice: design consumers to be idempotent
  ↳ Use unique message IDs, upserts, and dedup tables; assume at-least-once
📊 Three timelines showing same message — at-most-once (lost), at-least-once (delivered twice), exactly-once (delivered once)

## Slide 304
Message Ordering Guarantees
▸ FIFO queues preserve order within a partition/group
  ↳ SQS FIFO, Kafka per-partition, RabbitMQ per-queue: messages exit in the same order they entered
▸ Standard (non-FIFO) queues maximize throughput, no ordering guarantee
  ↳ SQS Standard can deliver out-of-order; trade strict order for massive scale
▸ Global ordering across partitions is usually impossible at scale
  ↳ You can have order OR parallelism; pick one per use case
▸ Use a partition key to keep related messages ordered together
  ↳ e.g., partition by userId so all events for one user are processed in order
▸ Many systems don't actually need strict order
  ↳ Use timestamps + idempotency to handle out-of-order events gracefully
📊 Two queues side-by-side — FIFO (1,2,3,4 in/out) vs Standard (1,2,3,4 in / 2,1,4,3 out)

## Slide 305
Message Queue Examples — Real Systems
▸ RabbitMQ: mature, AMQP-based, flexible routing
  ↳ Strong for complex routing topologies (direct, topic, fanout exchanges); used by Reddit, Instagram early days
▸ Amazon SQS: fully managed, infinite scale, pay-per-message
  ↳ Used internally across Amazon for decoupling services; FIFO and Standard variants
▸ ActiveMQ / Artemis: JMS-compliant, Java ecosystem staple
  ↳ Common in enterprise Java systems; supports topics and queues
▸ Redis Streams / Lists: lightweight queueing inside Redis
  ↳ Good for moderate scale; simple ops if you already run Redis
▸ NATS / NATS JetStream: high-perf, cloud-native
  ↳ Sub-millisecond latency; popular in service mesh and IoT scenarios
📊 Logos grid (RabbitMQ, SQS, ActiveMQ, Redis, NATS) with one-line descriptors and "best for" tags

## Slide 306
Message Queue Diagram — Order Processing Flow
▸ Producer: checkout service writes "OrderPlaced" message
  ↳ Includes orderId, userId, items, amount, timestamp
▸ Queue: durable, replicated, partitioned by orderId
  ↳ Persists message even if all consumers are down
▸ Consumers: billing, inventory, notification workers
  ↳ Each consumer group processes independently and at its own rate
▸ ACK / NACK feedback loop
  ↳ Successful processing → ACK removes message; failure → NACK triggers retry, eventually DLQ
📊 Flow — Checkout Service → "OrderPlaced" → [Queue with 3 messages] → 3 parallel consumer groups (Billing/Inventory/Email), each ...

## Slide 307
Message Queues — Trade-offs
▸ Pro: massive decoupling, resilience, elastic scaling
  ↳ Producers and consumers evolve, fail, and scale independently
▸ Con: eventual consistency
  ↳ Data is "in flight" — readers may see stale state until consumers catch up
▸ Con: operational overhead
  ↳ Monitoring, DLQs, replay tooling, schema management, on-call rotations
▸ Con: harder debugging
  ↳ Distributed traces across queue boundaries require correlation IDs and tracing tools (OpenTelemetry, Jaeger)
▸ Watch for: queue depth growth, consumer lag, redelivery rate, DLQ size
  ↳ These are your golden signals for queue-based systems
📊 Pros/Cons split with green checkmarks (decoupling, scaling) and red warnings (consistency, ops cost)

## Slide 308
Task / Job Queues — Concept Introduction
▸ Task queues are message queues specialized for "units of work"
  ↳ The message represents a function to call, not just an event that happened
▸ Difference from generic message queues
  ↳ Task queue knows about retries, scheduling, priorities, results, and worker pools out of the box
▸ Workers pull tasks and execute code
  ↳ "Send email to bob@x.com" → worker invokes send_email() with those args
▸ Often paired with a result backend
  ↳ Stores task status (PENDING, STARTED, SUCCESS, FAILURE) and return value for later lookup
📊 Code snippet showing `send_email.delay(user_id=123)` on left, worker process on right pulling and executing the function

## Slide 309
Task Queues — Common Use Cases
▸ Image / video processing
  ↳ Resize, transcode, watermark; CPU/GPU-heavy work offloaded from web servers
▸ Email & SMS delivery
  ↳ Third-party APIs are slow and flaky; never block a request on Mailgun/Twilio
▸ Report & PDF generation
  ↳ 30-second SQL queries and PDF rendering happen async; user gets an email when ready
▸ ML inference & training jobs
  ↳ Long-running model runs queued and dispatched to GPU workers
▸ Periodic / scheduled tasks
  ↳ Nightly cleanup, weekly digests, hourly reindexing handled by the same workers
📊 Icon grid — camera (image), envelope (email), document (report), brain (ML), clock (scheduled)

## Slide 310
Task Queue Workers — Pull-Based Processing
▸ Workers poll the queue for tasks
  ↳ "Anything for me?" — pull model gives natural backpressure
▸ Concurrency tuned per worker
  ↳ N processes × M threads/coroutines per process = total parallelism
▸ Acknowledge after success, requeue or DLQ on failure
  ↳ Tasks that crash mid-flight are re-delivered to another worker
▸ Workers are stateless and horizontally scalable
  ↳ Add more workers when the queue backs up; remove them when idle
▸ Long-running tasks need heartbeats
  ↳ Otherwise the broker thinks the worker died and re-delivers, causing duplicates
📊 Queue at top, 4 worker boxes pulling down arrows; one worker shows "heartbeat ❤" while processing a long task

## Slide 311
Priority Queues
▸ Not all tasks are equal — some need to jump the line
  ↳ Paid-tier customer reports vs free-tier batch jobs
▸ Implementation 1: separate queues per priority
  ↳ Workers always check `high` before `medium` before `low`; simple and effective
▸ Implementation 2: priority field on messages
  ↳ Broker (e.g., RabbitMQ priority queues) reorders internally; can starve low-priority tasks
▸ Watch out for starvation
  ↳ High-priority floods can permanently block low-priority work; use weighted fair scheduling
▸ Use case: real-time vs batch
  ↳ Interactive ML inference high-priority, nightly retraining low-priority on the same workers
📊 Three lanes labeled HIGH / MED / LOW feeding into shared worker pool, with worker checking lanes top-down

## Slide 312
Task Queue Examples — Celery, Sidekiq, Bull
▸ Celery (Python): the de-facto Python task queue
  ↳ Used by Instagram, Mozilla; supports RabbitMQ/Redis brokers, scheduled tasks, chains, groups, chords
▸ Sidekiq (Ruby): Redis-backed, high-performance
  ↳ Default in Rails apps; Shopify processes billions of jobs/day on Sidekiq
▸ Bull / BullMQ (Node.js): Redis-backed, modern API
  ↳ Used by NestJS apps; supports priorities, rate limiting, repeatable jobs
▸ Resque (Ruby), RQ (Python), Hangfire (.NET)
  ↳ Each ecosystem has its own; pick the one with the best community in your language
▸ Cloud-native: AWS Step Functions + Lambda, GCP Cloud Tasks
  ↳ Managed task execution without running your own workers
📊 Logo grid by language ecosystem — Python (Celery), Ruby (Sidekiq), Node (BullMQ), .NET (Hangfire)

## Slide 313
Task Queue Example — Email Delivery at Scale
▸ User signs up → sync code creates account, returns 200
  ↳ Total sync latency: ~80ms
▸ Async: `send_welcome_email.delay(user_id)` enqueued in Redis
  ↳ Returns instantly; web server moves on
▸ Email worker picks up task, calls SendGrid API
  ↳ Takes 800ms–3s; if SendGrid is slow, only the worker waits, not the user
▸ On failure: exponential backoff retries (1m, 5m, 30m, 2h)
  ↳ Transient SendGrid 5xx errors recover automatically
▸ After max retries: task → DLQ, ops alerted
  ↳ User experience never degraded, even during a 4-hour SendGrid outage
📊 Sequence diagram — User → API (200 OK in 80ms), API → Redis Queue, Worker → SendGrid (with retry loop)

## Slide 314
Task Queues — Trade-offs
▸ Pro: massively improves perceived latency
  ↳ User-facing requests stay fast even when downstream is slow
▸ Pro: built-in retry, scheduling, monitoring
  ↳ Saves writing custom orchestration code per use case
▸ Con: idempotency burden on the developer
  ↳ Tasks may run twice; "send email" running twice = bad user experience
▸ Con: state visibility — "did it run?"
  ↳ Need result backends, dashboards (Flower for Celery, Sidekiq Web UI), alerting
▸ Con: version skew between producers and workers
  ↳ Deploying new task signatures while old workers run = pickle/serialization errors
📊 Two-column trade-off table with concrete examples in each cell

## Slide 315
Pub/Sub & Event Streaming — Concept Introduction
▸ Point-to-point queue: one message, one consumer (load balancing)
  ↳ Each task processed by exactly one worker
▸ Pub/Sub: one message, many subscribers (broadcast)
  ↳ Producer publishes once; every subscribed consumer gets its own copy
▸ Event streaming: durable, replayable log of events
  ↳ Consumers can rewind to any point in history; events are facts, not commands
▸ Mental shift: events vs commands
  ↳ Command "ChargeCustomer" → one handler. Event "OrderPlaced" → many independent reactions
📊 Two diagrams — left "Queue: 1 msg → 1 of N consumers", right "Pub/Sub: 1 msg → all N subscribers"

## Slide 316
Event Sourcing — The Concept
▸ Store every state change as an immutable event
  ↳ Instead of `account.balance = 100`, store `Deposited(amount=100)` and `Withdrew(amount=20)`
▸ Current state = replay of all past events
  ↳ Audit trail, time travel, and debugging come for free
▸ Pairs naturally with Kafka-style event logs
  ↳ The log IS the source of truth; databases become materialized views
▸ Enables CQRS (Command Query Responsibility Segregation)
  ↳ Write side appends events; read side projects events into query-optimized views
▸ Real example: banking ledgers, Git, blockchain
  ↳ All are append-only event logs by design
📊 Bank account view — left "Events: +100, -20, +50" / right "Materialized State: balance=130"

## Slide 317
Apache Kafka — Architecture Deep Dive
▸ Topic: a named stream of events (e.g., `orders`, `clicks`, `page_views`)
  ↳ Logical category; producers write to topics, consumers read from topics
▸ Partition: a topic split into ordered, append-only logs
  ↳ Each partition is a separate file on disk; partitions = unit of parallelism
▸ Offset: monotonically increasing ID per partition
  ↳ Consumers track their own offset; "I've read up to message 4,521"
▸ Consumer group: a set of consumers sharing the work
  ↳ Kafka assigns partitions to consumers in the group; one partition → one consumer in a group
▸ Brokers + replication: distributed, fault-tolerant
  ↳ Each partition replicated across N brokers (typically 3); leader handles writes, followers stay in sync
📊 Topic "orders" with 3 partitions, each showing ordered messages with offset numbers, and 3 consumers in a group each reading a ...

## Slide 318
Why Kafka is Durable and Replayable
▸ Append-only commit log on disk
  ↳ Sequential writes are fast; old messages aren't deleted on consume
▸ Configurable retention (time or size)
  ↳ "Keep 7 days" or "keep 1TB"; consumers can re-read anytime within retention
▸ Replication for fault tolerance
  ↳ Replication factor 3 means any 2 broker failures are survivable
▸ Consumers track their own offsets (in `__consumer_offsets` topic)
  ↳ Reset to earliest, latest, or arbitrary timestamp — replay last hour of events for free
▸ This is why Kafka unlocks new architectures
  ↳ Event sourcing, change data capture, stream processing, log aggregation all ride on these properties
📊 Disk-shaped commit log with messages 0–9, replicated across 3 brokers; consumer arrow pointing to offset 6 with note "can reset...

## Slide 319
Kafka Use Cases — Real Examples
▸ LinkedIn: Kafka was born here for activity feeds & metrics
  ↳ Now handles 7+ trillion messages/day; powers feed, search indexing, monitoring
▸ Netflix: real-time analytics, recommendation pipelines
  ↳ 10+ trillion events/day flow through Kafka into Flink and Spark jobs
▸ Uber: trip events, dynamic pricing, fraud detection
  ↳ Surge pricing runs on Kafka streams of recent ride requests
▸ Change Data Capture (CDC) with Debezium
  ↳ Stream every DB change into Kafka; downstream services build their own views
▸ Log aggregation (replacing Scribe/Flume)
  ↳ All app logs flow through Kafka into Elasticsearch / S3 / Snowflake
📊 World map / company logos showing Kafka deployments at scale, with throughput numbers

## Slide 320
Pub/Sub Alternatives — Pulsar, Kinesis, Google Pub/Sub
▸ Apache Pulsar: tiered storage, multi-tenancy, geo-replication
  ↳ Separates compute (brokers) from storage (BookKeeper); good for very long retention
▸ AWS Kinesis Data Streams: managed, Kafka-like
  ↳ Tightly integrated with AWS (Lambda triggers, Firehose to S3); per-shard pricing
▸ Google Cloud Pub/Sub: globally-distributed, push or pull
  ↳ Scales to millions of msg/s; supports push to HTTP endpoints
▸ AWS SNS: pure pub/sub (no durable log)
  ↳ Fan-out to SQS, Lambda, HTTP, email; not for replay
▸ Azure Event Hubs: Microsoft's Kafka equivalent
  ↳ Kafka-protocol-compatible; integrates with Azure Stream Analytics
📊 Comparison matrix — features (durability, retention, throughput, managed) across Kafka / Pulsar / Kinesis / Pub/Sub

## Slide 321
Pub/Sub Diagram — News Feed Fan-Out
▸ Producer: a user posts a tweet
  ↳ Single write to `tweets` topic with userId, content, timestamp
▸ Topic: durable, partitioned by userId
  ↳ One partition per user "shard"; ordered per user
▸ Consumers (independent groups)
  ↳ Search indexer, ML moderation, follower fan-out, analytics — each at its own pace
▸ No coupling between subscribers
  ↳ Adding "fraud detection" later = new consumer group, no producer change
📊 Central Kafka topic, 1 producer arrow in, 4 consumer group arrows out, each labeled with its purpose

## Slide 322
Pub/Sub & Streaming — Trade-offs
▸ Pro: ultimate decoupling and replayability
  ↳ Add new consumers years later; rebuild views from scratch using historical events
▸ Pro: handles massive scale (millions of msg/s)
  ↳ Partitioning is the secret sauce
▸ Con: operational complexity
  ↳ ZooKeeper/KRaft, brokers, partitions, ISR, rebalancing — Kafka has a real learning curve
▸ Con: ordering only within a partition
  ↳ Need careful partition key choice to maintain useful ordering
▸ Con: schema evolution is critical
  ↳ Use Avro/Protobuf with a Schema Registry; breaking changes cascade to all consumers
📊 Iceberg metaphor — visible "easy producer/consumer API" above water, hidden "ops, partitioning, schemas" below

## Slide 323
Backpressure — Concept Introduction
▸ Backpressure = a slow consumer signaling "stop sending so fast"
  ↳ When work arrives faster than it can be processed, something must give
▸ Without backpressure, queues grow unbounded
  ↳ Memory blows up, latency spikes, eventually the whole system crashes
▸ The danger: cascading failures
  ↳ Producer hammers a slow consumer → consumer dies → producer's queue fills → producer dies
▸ Goal: graceful degradation, not collapse
  ↳ Better to drop or delay some work than to fail completely
📊 Water analogy — fire hose (producer) into a small drain (consumer); without overflow valve, everything floods

## Slide 324
Backpressure — Solutions
▸ Bounded queues with rejection
  ↳ Queue full → reject new messages with 503; producer must back off
▸ Rate limiting at the producer
  ↳ Token bucket or leaky bucket caps requests/second per client
▸ Load shedding: drop non-critical work
  ↳ Under stress, skip analytics events; keep payments flowing
▸ Circuit breakers: fail fast when downstream is unhealthy
  ↳ Trip after N failures, return cached/default response, retry after cooldown (Hystrix, resilience4j)
▸ Adaptive concurrency: dynamically adjust parallelism
  ↳ Use latency / error signals to scale workers up or down (Netflix concurrency-limits)
▸ Pull-based consumption naturally provides backpressure
  ↳ Consumers pull only what they can handle; producer queue absorbs the rest
📊 Five icons — bounded queue, rate limiter, load shedder, circuit breaker, autoscaler — feeding into a "stable system" core

## Slide 325
Backpressure Example — Stripe Webhooks
▸ Stripe sends webhooks for every payment event
  ↳ Spikes during sales: thousands of events/second hitting your endpoint
▸ Naive: process inline → endpoint timeouts → Stripe retries → makes it worse
  ↳ Classic positive feedback loop into total failure
▸ Better: webhook handler does only "verify + enqueue"
  ↳ Returns 200 in <100ms; heavy work happens async
▸ Best: bounded internal queue + alert when nearing capacity
  ↳ If queue >80%, scale workers up; if >95%, return 429 to Stripe (which retries with backoff)
▸ The queue acts as a shock absorber for traffic spikes
  ↳ 10x burst becomes a 30-minute drain instead of an outage
📊 Time-series graph of webhook arrivals (spiky) vs queue drain (smooth), with "auto-scale" annotation at threshold

## Slide 326
Backpressure — Trade-offs
▸ Pro: prevents catastrophic cascading failures
  ↳ The single biggest stability win in distributed systems
▸ Pro: makes capacity planning explicit
  ↳ You know your limits because you defined them
▸ Con: requires choosing what to drop
  ↳ Business decision: which work is sheddable vs critical?
▸ Con: clients must handle 429s and retries
  ↳ Not all clients are well-behaved; mobile apps especially
▸ Without it, autoscaling alone won't save you
  ↳ You can't scale faster than failures propagate; backpressure is the brake pedal
📊 Two timelines — "no backpressure: gradual slowdown → cliff" vs "with backpressure: gentle plateau"

## Slide 327
Workflow Orchestration — When Queues Aren't Enough
▸ Simple async fits "fire and forget" or single-step jobs
  ↳ Send email, resize image, charge card
▸ Multi-step workflows need orchestration
  ↳ "Place order → reserve inventory → charge card → ship → email confirmation → handle returns"
▸ Each step may fail, retry, or compensate
  ↳ If charge succeeds but inventory reservation fails, you must refund (saga pattern)
▸ Long-running, stateful processes
  ↳ Hours, days, or months between steps (e.g., subscription renewals, multi-day approval flows)
▸ Visibility & auditability requirements
  ↳ "Where is this order?" needs a single answer, not 5 logs across 5 services
📊 DAG diagram — order workflow with branching, retries, and compensation arrows, contrasted with a flat queue

## Slide 328
Workflow Orchestration Tools
▸ AWS Step Functions: managed state machines (JSON / ASL)
  ↳ Tight AWS integration; visual workflow editor; great for serverless workflows
▸ Apache Airflow: Python DAGs, batch / data pipelines
  ↳ Originally Airbnb; the standard for ETL & data engineering
▸ Temporal: code-as-workflow, durable execution
  ↳ Write workflows like normal code; Temporal handles retries, state, history; used by Uber, Snap, Datadog
▸ Cadence (Uber's predecessor to Temporal): similar model
  ↳ Same authors; Temporal is the actively-developed fork
▸ Argo Workflows: Kubernetes-native, container per step
  ↳ Strong fit for ML pipelines and Kubernetes-heavy shops
📊 5-tile gallery with tool logo, language, sweet spot — Step Functions / Airflow / Temporal / Argo / Prefect

## Slide 329
Orchestration Example — Uber Trip Lifecycle
▸ Workflow steps: request → match → pickup → ride → drop-off → fare → receipt → rating
  ↳ Spans 30+ minutes; each step is its own service
▸ Built on Temporal/Cadence at Uber
  ↳ Workflow code resembles a normal program; durability and retries handled by the platform
▸ Failure handling: retry transient errors, compensate on permanent failures
  ↳ Driver cancels mid-ride? Refund partial fare, rematch rider, notify both parties
▸ Single source of truth for trip state
  ↳ Customer support and analytics query one workflow, not 8 services
📊 Linear timeline of trip steps with retry loops, branching for cancellation, and a "Temporal" badge orchestrating it all

## Slide 330
Section Key Takeaways
▸ Async = decouple "accepting work" from "doing work"
  ↳ The single biggest tool for building responsive, resilient systems
▸ Message queues add buffering, retries, and fault isolation
  ↳ DLQs, idempotency, and ordering choices are non-negotiable in production
▸ Task queues specialize for application work units
  ↳ Celery, Sidekiq, Bull bring batteries-included retries, scheduling, priorities
▸ Streaming (Kafka) unlocks pub/sub, event sourcing, and replay
  ↳ Topics + partitions + offsets are the foundational vocabulary
▸ Backpressure prevents cascading failures
  ↳ Bounded queues, rate limits, circuit breakers, load shedding
▸ Orchestration handles multi-step durable workflows
  ↳ Reach for Temporal/Step Functions/Airflow when queues alone aren't enough
📊 6-icon summary grid mapping each takeaway to a pictogram

## Slide 331
Interview Tips — Async & Queues
▸ Default to async for any operation >1s or with external dependencies
  ↳ "I'd send the email via a Celery/SQS task so we return 202 immediately"
▸ Always mention idempotency when discussing at-least-once delivery
  ↳ "Consumer will be idempotent using a dedup table on messageId"
▸ Pick the right tool for the job
  ↳ SQS for simple work queues, Kafka for streaming/replay, Temporal for multi-step workflows
▸ Show you understand failure modes
  ↳ DLQs, poison messages, consumer lag, replication factor, partition rebalancing
▸ Talk through partitioning strategy in streaming questions
  ↳ "Partition by userId so all events for one user stay ordered on one partition"
▸ Mention observability: queue depth, consumer lag, redelivery rate, DLQ size
  ↳ These are the SRE-level signals that show maturity
📊 Interview "cheat sheet" panel with 6 bullet headers, each with a 1-line answer template

## Slide 332
Common Pitfalls
▸ Treating queues as databases
  ↳ Queues are for in-flight work; long-term state belongs in a DB
▸ Forgetting idempotency
  ↳ At-least-once delivery means duplicates; "send email twice" or "charge card twice" = real bugs
▸ No DLQ → infinite retries
  ↳ Poison messages block the queue forever; producers stop, alerts fire, weekend ruined
▸ Ignoring consumer lag
  ↳ Lag silently grows for hours, then SLOs are violated; monitor it as a top-tier signal
▸ Picking Kafka when SQS would do (or vice versa)
  ↳ Kafka is heavy operationally; don't run it for 100 messages/day. Don't use SQS where you need replay.
▸ Synchronous-feeling APIs over async backends
  ↳ Polling forever for a job result instead of using webhooks/WebSockets degrades UX
▸ Schema changes that break consumers
  ↳ Always use a Schema Registry + backward-compatible evolution (Avro, Protobuf)
▸ Not testing failure paths
  ↳ Worker crashes mid-task, broker restarts, network partitions — chaos test these in staging
📊 "Warning signs" themed slide — 8 red caution-tape strips, each with a one-line pitfall

## Slide 333
Section 9: Communication Protocols

## Slide 334
Why Communication Protocols Matter
▸ Distributed systems are conversations between machines
  ↳ Every request, every database query, every cache hit is a network call governed by some protocol
▸ Protocol choice dictates latency, throughput, and reliability
  ↳ Picking TCP vs UDP, REST vs gRPC, polling vs WebSockets can swing performance by 10x or more
▸ Protocols define the contract between services
  ↳ They encode assumptions about ordering, delivery guarantees, encoding, and error handling
▸ System design interviews probe protocol fluency constantly
  ↳ "How would you push live scores to 10M users?" is fundamentally a protocol question
▸ One layer's strength is another's weakness
  ↳ Reliability costs latency; flexibility costs structure; choosing well requires understanding the trade space
📊 Layered diagram showing client -> protocol -> network -> protocol -> server, with annotations for "where latency hides" at each...

## Slide 335
OSI Model - Concept Introduction
▸ The OSI (Open Systems Interconnection) model is a 7-layer conceptual framework for network communication
  ↳ Created by ISO in 1984 as a vendor-neutral way to reason about networking
▸ Each layer has a single responsibility and talks only to layers directly above and below
  ↳ This separation lets you swap implementations (e.g., Ethernet for Wi-Fi at L2) without rewriting upper layers
▸ Real-world stacks (TCP/IP) don't strictly match OSI but borrow its vocabulary
  ↳ "L4 load balancer" or "L7 proxy" comes directly from OSI terminology
▸ It exists to give engineers a shared mental model
  ↳ When someone says "the problem is at Layer 3," every network engineer knows they mean routing
▸ Foundational because system design constantly references L4 vs L7 distinctions
  ↳ Understanding the model unlocks discussions about load balancers, firewalls, and proxies
📊 Vertical 7-layer stack with icons (cable for L1, MAC address for L2, IP for L3, TCP/UDP for L4, etc.)

## Slide 336
OSI Model - The 7 Layers Deep Dive
▸ Layer 1 - Physical: bits over wire/fiber/radio
  ↳ Cables, voltages, Wi-Fi signals; deals with raw 0s and 1s
▸ Layer 2 - Data Link: frames between adjacent nodes (Ethernet, MAC addresses)
  ↳ Handles collisions and local addressing on the same network segment
▸ Layer 3 - Network: packets across networks (IP, routing)
  ↳ Routes data between different networks using IP addresses
▸ Layer 4 - Transport: end-to-end delivery (TCP, UDP)
  ↳ Manages reliability, ordering, flow control between processes on different hosts
▸ Layer 5-6-7 - Session, Presentation, Application: conversations, encoding (TLS, JSON), and the actual app (HTTP, SMTP)
  ↳ In practice these three are often blurred together; HTTP, gRPC, and DNS all live "at L7"
📊 7 layers with example data unit at each (bit -> frame -> packet -> segment -> data) and a representative protocol

## Slide 337
OSI Model - L4 vs L7 in System Design
▸ L4 load balancers route on IP and port without inspecting payload
  ↳ Fast, protocol-agnostic; AWS NLB, HAProxy in TCP mode, IPVS
▸ L7 load balancers understand HTTP, can route on URL, headers, cookies
  ↳ Smarter routing (e.g., /api/v2 to new cluster); Nginx, Envoy, AWS ALB
▸ L4 is cheaper and faster but blind to application semantics
  ↳ Can't do path-based routing, header rewrites, or content-based caching
▸ L7 enables advanced features at higher CPU cost
  ↳ TLS termination, A/B testing, canary deployments, sticky sessions by user ID
▸ Choose L4 when you need raw throughput; L7 when you need application-aware routing
  ↳ Modern systems often layer both: L4 in front of L7 for tiered scaling
📊 Side-by-side comparison - L4 LB looking at "envelope" only vs L7 LB reading the "letter inside"

## Slide 338
OSI vs TCP/IP Model Comparison
▸ TCP/IP model is the practical 4-layer model the internet actually uses
  ↳ Link -> Internet -> Transport -> Application; collapses OSI's L1+L2 and L5+L6+L7
▸ OSI is the textbook reference; TCP/IP is the engineering reality
  ↳ You'll see TCP/IP terms in RFCs and documentation, OSI terms in interviews
▸ Mapping: OSI L1+L2 = TCP/IP Link; L3 = Internet; L4 = Transport; L5+L6+L7 = Application
  ↳ Functionality is the same, granularity differs
▸ Why this matters: when you read "the application layer" in TCP/IP, it includes encoding and session management
  ↳ HTTPS bundles HTTP (L7), TLS (L5/6), and runs on TCP (L4) over IP (L3)
▸ Both models exist because abstraction is the only way to manage networking complexity
  ↳ You don't write code that thinks about voltage levels when calling fetch()
📊 Two stacks side-by-side with arrows mapping OSI 7 layers to TCP/IP 4 layers

## Slide 339
TCP - Concept Introduction
▸ TCP (Transmission Control Protocol) is connection-oriented and reliable
  ↳ Sender and receiver establish a session, exchange data with guaranteed delivery, then tear down
▸ Guarantees: in-order delivery, no duplicates, no losses (or you get an error)
  ↳ The OS retransmits lost packets, reorders out-of-order ones, and deduplicates
▸ Trades latency and overhead for reliability
  ↳ Every packet is acknowledged; lost packets trigger retransmission; congestion control throttles speed
▸ TCP is the workhorse of the internet
  ↳ HTTP/1.1, HTTP/2, SSH, SMTP, FTP, database connections - virtually all "important" data uses TCP
▸ Exists because applications need reliable byte streams without writing their own retry logic
  ↳ Before TCP, every app reinvented retry, ordering, and flow control - TCP standardized it
📊 Two stick figures passing numbered envelopes back and forth with checkmarks for ACKs

## Slide 340
TCP - 3-Way Handshake Deep Dive
▸ Step 1 - SYN: client sends synchronize packet with initial sequence number
  ↳ "Hi, I want to talk; my numbering starts at X"
▸ Step 2 - SYN-ACK: server replies with its own SYN and acknowledges client's SYN
  ↳ "Got it, I'll number my data starting at Y, and I confirm I saw your X"
▸ Step 3 - ACK: client acknowledges server's SYN, connection established
  ↳ "Confirmed, let's go"; takes 1.5 round-trips before any real data flows
▸ Connection teardown uses a 4-way handshake (FIN, ACK, FIN, ACK)
  ↳ Each side closes its half independently; this is why "TIME_WAIT" sockets accumulate
▸ Handshake overhead is why TCP feels slow on high-latency networks
  ↳ On a 100ms RTT link, you've burned 150ms before sending a single byte of data
📊 Sequence diagram with client and server lifelines showing SYN, SYN-ACK, ACK arrows with timestamps

## Slide 341
UDP - Concept Introduction
▸ UDP (User Datagram Protocol) is connectionless and unreliable
  ↳ Send a packet and hope it arrives; no handshake, no acknowledgments, no retransmission
▸ "Fire and forget" semantics with minimal overhead
  ↳ 8-byte header vs TCP's 20+ bytes; no connection state on either side
▸ No ordering, no deduplication, no congestion control by default
  ↳ Application is responsible for handling lost or out-of-order packets if it cares
▸ Faster and lighter than TCP, ideal when latency matters more than reliability
  ↳ Real-time use cases tolerate occasional loss but cannot tolerate buffering delays
▸ Exists for cases where retransmission is worse than loss
  ↳ In a video call, a 200ms-old frame is useless; better to skip it than wait for it
📊 Stick figure throwing paper airplanes - some fly, some crash, sender doesn't look back

## Slide 342
TCP vs UDP - Trade-offs and When to Choose
▸ Choose TCP when correctness > speed
  ↳ Banking transactions, file downloads, web pages, emails, database queries
▸ Choose UDP when speed > perfect delivery
  ↳ Live video, online gaming, VoIP, DNS lookups, real-time telemetry, multicast
▸ TCP is slower because of retransmissions, ACKs, congestion control, and head-of-line blocking
  ↳ One lost packet stalls everything behind it until it's recovered
▸ UDP forces you to build reliability yourself if you need it
  ↳ QUIC (used by HTTP/3) does exactly this: UDP + custom reliability layer
▸ Real examples: Netflix uses TCP for control plane and UDP-based protocols for video chunks
  ↳ Google Meet, Zoom, Discord voice all run RTP-over-UDP for audio/video streams
📊 Decision tree - "Is loss tolerable?" branching to UDP, "Need reliability?" branching to TCP, with example apps at leaves

## Slide 343
TCP vs UDP - Real Product Examples
▸ HTTP, HTTPS, SSH, SFTP, SMTP -> TCP
  ↳ Loading this slide deck, pulling git repos, sending emails all rely on TCP guarantees
▸ DNS queries -> primarily UDP (with TCP fallback for large responses)
  ↳ DNS is small and idempotent; retry on timeout is fine
▸ Online games (Fortnite, CS:GO, Valorant) -> UDP for game state, TCP for chat/lobby
  ↳ Position updates that arrive 50ms late are useless; chat messages need reliability
▸ Streaming (YouTube live, Twitch, Zoom) -> UDP-based RTP for media, TCP for control
  ↳ Video frames can be dropped gracefully; "join meeting" command must succeed
▸ WhatsApp/Signal voice calls -> SRTP over UDP for audio, TCP for messaging
  ↳ Voice tolerates loss; "read receipts" need exact-once delivery
📊 Product logos in two columns - TCP column (Gmail, GitHub, Stripe) and UDP column (Zoom audio, Fortnite, DNS)

## Slide 344
TCP/UDP Diagram - Packet Flow Comparison
▸ TCP flow: connect -> data -> ACK -> data -> ACK -> close (lots of bookkeeping)
  ↳ Each segment carries sequence numbers, ACK numbers, window size, flags
▸ UDP flow: send packet, send packet, send packet (no return trips)
  ↳ Each datagram is independent with just source/dest port and length
▸ TCP retransmission scenario: packet 5 lost -> receiver buffers 6, 7, 8 -> sender resends 5 -> deliver 5,6,7,8 in order
  ↳ This buffering causes head-of-line blocking
▸ UDP loss scenario: packet 5 lost -> receiver gets 6, 7, 8 -> application decides what to do
  ↳ Game engine interpolates missing position; voice codec masks dropped frame
▸ Visualizing the difference clarifies why protocol choice matters
  ↳ The "shape" of the conversation determines latency floor and reliability ceiling
📊 Two timelines side-by-side - TCP showing handshake, ordered delivery with ACKs; UDP showing simple unidirectional packet stream...

## Slide 345
HTTP Protocol - Concept Introduction
▸ HTTP (HyperText Transfer Protocol) is the request-response protocol of the web
  ↳ Client sends a request (method + URL + headers + optional body), server sends a response (status + headers + body)
▸ Stateless by design: each request is independent
  ↳ Server doesn't remember previous requests; state lives in cookies, tokens, or databases
▸ Text-based and human-readable in HTTP/1.x; binary in HTTP/2 and HTTP/3
  ↳ You can literally telnet to port 80 and type GET / HTTP/1.1 in HTTP/1.1
▸ Built on TCP (HTTP/1.1, HTTP/2) or QUIC/UDP (HTTP/3)
  ↳ Transport choice fundamentally changes performance characteristics
▸ Exists to standardize document and resource transfer
  ↳ Before HTTP, every system had a custom protocol; HTTP made the web possible
📊 Browser sending GET /index.html request with headers shown, server responding with 200 OK and HTML body

## Slide 346
HTTP/1.1 Deep Dive
▸ Text-based protocol with one request per connection (originally)
  ↳ Each request opens a TCP connection, sends, receives, closes - extremely wasteful
▸ Keep-alive (persistent connections) reuses TCP connection for multiple requests
  ↳ Default in HTTP/1.1; saves the handshake cost on subsequent requests
▸ Pipelining allows multiple requests without waiting for responses
  ↳ Rarely used in practice due to head-of-line blocking and proxy bugs
▸ Head-of-line blocking: response 1 must complete before response 2 starts
  ↳ One slow image blocks all subsequent assets on the same connection
▸ Browsers work around this by opening 6 parallel connections per origin
  ↳ This is why "domain sharding" was a popular HTTP/1.1 optimization
📊 Timeline showing 6 parallel TCP connections, each fetching assets sequentially with idle gaps

## Slide 347
HTTP/2 Deep Dive
▸ Binary framing layer replaces text parsing
  ↳ Frames are typed (HEADERS, DATA, SETTINGS, etc.); efficient and unambiguous
▸ Multiplexing: many requests/responses interleaved on one TCP connection
  ↳ Solves application-layer head-of-line blocking; one connection serves the whole page
▸ HPACK header compression reduces redundant header bytes
  ↳ Cookies, User-Agent, Accept headers are sent once and referenced by index thereafter
▸ Server push allows server to preemptively send resources
  ↳ "You asked for index.html; here's style.css too because I know you'll need it"
▸ Still suffers from TCP-level head-of-line blocking
  ↳ One lost TCP packet stalls all multiplexed streams until retransmission completes
📊 Single TCP connection with multiple colored streams (HTML, CSS, JS, images) interleaved as frames

## Slide 348
HTTP/3 and QUIC Deep Dive
▸ HTTP/3 runs over QUIC, which runs over UDP instead of TCP
  ↳ Google built QUIC in user space for faster iteration than kernel-level TCP changes
▸ Eliminates TCP head-of-line blocking by giving each stream its own loss recovery
  ↳ A lost packet for stream 1 doesn't stall streams 2, 3, 4
▸ Faster connection setup with 0-RTT and 1-RTT handshakes
  ↳ Reconnecting clients can send data with the very first packet
▸ TLS 1.3 baked in; encryption is mandatory at the transport level
  ↳ No more "speak HTTP first then upgrade to TLS" round trips
▸ Better mobile performance with connection migration
  ↳ Switch Wi-Fi to cellular and your QUIC connection survives via connection IDs
📊 HTTP/3 stack diagram - HTTP/3 -> QUIC -> UDP -> IP, with TLS 1.3 inside QUIC, contrasted with HTTP/2 -> TLS -> TCP -> IP

## Slide 349
HTTP Methods Deep Dive
▸ GET: retrieve a resource; safe and idempotent
  ↳ Should never modify server state; cacheable; parameters in URL
▸ POST: create a resource or trigger a non-idempotent action
  ↳ Two POSTs to /orders create two orders; not safe to retry blindly
▸ PUT: replace a resource entirely; idempotent
  ↳ PUT /users/42 with full user object; same call twice yields same result
▸ PATCH: partial update; usually idempotent but not guaranteed
  ↳ PATCH /users/42 with {"email": "x@y.com"} only changes email
▸ DELETE: remove a resource; idempotent
  ↳ HEAD: like GET but no body (check existence/headers); OPTIONS: discover allowed methods (CORS preflight)
📊 Method matrix with columns Safe, Idempotent, Cacheable, Has-Body and rows for each method with checkmarks

## Slide 350
HTTP Status Codes Deep Dive
▸ 2xx Success: 200 OK, 201 Created, 204 No Content
  ↳ 201 means resource created (use after POST); 204 means success but no body to return
▸ 3xx Redirection: 301 Moved Permanently, 302 Found, 304 Not Modified
  ↳ 301 is cacheable forever; 304 enables conditional GETs with ETag/If-Modified-Since
▸ 4xx Client Error: 400 Bad Request, 401 Unauthorized, 403 Forbidden, 404 Not Found, 429 Too Many Requests
  ↳ 401 means "who are you?"; 403 means "I know you, you can't do this"; 429 signals rate limiting
▸ 5xx Server Error: 500 Internal Server Error, 502 Bad Gateway, 503 Service Unavailable, 504 Gateway Timeout
  ↳ 502/504 typically indicate problems behind your load balancer; 503 means deliberately unavailable
▸ Picking the right code matters for caching, retries, and observability
  ↳ Returning 200 with an error body breaks every middlebox that relies on status codes
📊 Color-coded grid - green 2xx, yellow 3xx, orange 4xx, red 5xx with key codes and one-line descriptions

## Slide 351
HTTP Headers, Cookies, and Sessions
▸ Headers carry metadata: Content-Type, Authorization, Cache-Control, User-Agent
  ↳ Custom headers (X-Request-ID, X-Forwarded-For) propagate trace IDs and client IPs through proxies
▸ Cookies are key-value pairs the server sets and the browser sends back automatically
  ↳ Set-Cookie response header; Cookie request header; scoped by domain and path
▸ Sessions are server-side state keyed by a cookie (often a session ID)
  ↳ Alternative: stateless JWTs that encode user info in the cookie itself
▸ Critical security flags: HttpOnly (no JS access), Secure (HTTPS only), SameSite (CSRF protection)
  ↳ Missing these flags is how XSS attacks steal session tokens
▸ Cache-Control headers govern CDN and browser caching
  ↳ max-age, no-store, private, immutable, stale-while-revalidate each have specific meanings
📊 HTTP request/response with headers highlighted, showing cookie flow and a session token round trip

## Slide 352
HTTP Comparison and Real Examples
▸ HTTP/1.1: still ubiquitous, simple to debug, fine for small APIs
  ↳ curl, postman, server logs all show readable HTTP/1.1 traffic
▸ HTTP/2: most production websites in 2020+; great for multi-asset pages
  ↳ Cloudflare, Google, Facebook serve HTTP/2 by default
▸ HTTP/3: rolling out at scale; Google, Cloudflare, Meta, Akamai have 30%+ traffic on HTTP/3
  ↳ Especially beneficial for mobile users on flaky networks
▸ Migration is mostly transparent: same URLs, same APIs, faster transport
  ↳ The browser and server negotiate the highest version both support via ALPN
▸ Choose based on infrastructure: HTTP/3 needs UDP-friendly networks (some corporate firewalls block it)
  ↳ Most CDNs auto-upgrade and fall back gracefully
📊 Bar chart showing page load time for 1.1 vs 2 vs 3 on a 100-asset page, plus a globe with major adopters

## Slide 353
REST API - Concept Introduction
▸ REST (Representational State Transfer) is an architectural style for HTTP APIs
  ↳ Coined by Roy Fielding in 2000; not a protocol, just a set of conventions
▸ Core principles: client-server, stateless, cacheable, uniform interface, layered, code-on-demand (optional)
  ↳ Statelessness means each request contains everything the server needs to process it
▸ Resource-oriented: every "thing" gets a URL; verbs are HTTP methods
  ↳ /users, /users/42, /users/42/orders are nouns; GET/POST/PUT/DELETE are verbs
▸ Exists to standardize CRUD APIs and leverage HTTP's existing semantics
  ↳ You get caching, content negotiation, status codes, and tooling for free
▸ Dominates web APIs because it's simple, debuggable, and composable
  ↳ Stripe, GitHub, Twitter, Slack all expose REST-ish APIs as their primary interface
📊 URL anatomy - /api/v1/users/42/orders?status=pending broken into resource path components

## Slide 354
REST URL Design and Conventions
▸ Use plural nouns for collections: /users, /orders, /products
  ↳ Singular for top-level when it makes sense: /me, /health
▸ Use IDs for specific resources: /users/42 not /user/42 or /getUser?id=42
  ↳ Hierarchy reflects relationships: /users/42/orders/100/items
▸ Filter, sort, paginate via query parameters: ?status=active&sort=-created_at&page=2
  ↳ Don't put filters in the path; that's a different resource
▸ Avoid verbs in URLs; the HTTP method IS the verb
  ↳ Bad: POST /createUser; Good: POST /users
▸ For non-CRUD actions, use sub-resources or be pragmatic: POST /orders/42/cancel
  ↳ Pure REST purists hate this; everyone does it anyway
📊 Two columns - "Bad URL" vs "Good URL" with examples like /getUser?id=42 -> GET /users/42

## Slide 355
REST Idempotency Deep Dive
▸ Idempotent: calling N times has the same effect as calling once
  ↳ GET, PUT, DELETE, HEAD, OPTIONS are idempotent by spec
▸ POST is NOT idempotent: each call creates a new resource
  ↳ POST /orders twice creates two orders; this is why double-clicking "Submit" is dangerous
▸ Idempotency enables safe retries on network failures
  ↳ Client doesn't know if request succeeded -> retry it -> server handles duplicate gracefully
▸ For non-idempotent operations, use idempotency keys (Stripe-style)
  ↳ Client generates a UUID, server stores it for 24h, returns cached response on duplicate
▸ Idempotency is the foundation of reliable distributed systems
  ↳ Without it, every retry risks double-charging customers or duplicating orders
📊 Network failure scenario - client times out, retries, server recognizes idempotency key and returns same response

## Slide 356
REST vs SOAP Comparison
▸ REST: lightweight, JSON, HTTP-native, easy to debug, mobile-friendly
  ↳ Build a REST API in 10 minutes; debug it with curl
▸ SOAP: heavyweight, XML, protocol-agnostic, strong contracts via WSDL
  ↳ Verbose envelopes, built-in security (WS-Security), formal schemas
▸ REST won for public web APIs; SOAP persists in enterprise/legacy
  ↳ Banks, payment processors, government systems still ship SOAP endpoints
▸ SOAP advantages: built-in transactions, formal contracts, language-agnostic codegen
  ↳ When you need ACID across services or strict typing, SOAP/WSDL still has merit
▸ REST advantages: simpler, cacheable, lower bandwidth, better tooling, ubiquitous
  ↳ For 95% of new APIs in 2020+, REST (or gRPC, or GraphQL) wins
📊 Side-by-side request - REST showing tiny JSON, SOAP showing 50-line XML envelope for the same operation

## Slide 357
REST Pagination, Filtering, and Versioning
▸ Pagination strategies: offset (?page=2&size=20), cursor (?cursor=eyJpZCI6MTAwfQ), keyset (?after_id=100)
  ↳ Cursor and keyset are stable under inserts; offset breaks when data shifts
▸ Filtering: query params for simple cases (?status=active), JSON body for complex queries
  ↳ GraphQL solves complex querying entirely; REST gets awkward past 4-5 filter dimensions
▸ Versioning: URL (/v1/users), header (Accept: application/vnd.api+json;version=1), query (?v=1)
  ↳ URL versioning is most common because it's visible and easy to route
▸ Backward compatibility matters: never break v1 while v2 exists
  ↳ Add fields freely; renaming or removing fields breaks clients
▸ Deprecation strategy: announce, dual-run, sunset with clear timelines
  ↳ Stripe gives 1+ year notice and pins API versions per account for stability
📊 Pagination comparison showing offset-based "page 2 of 10" vs cursor-based "next: abc123"

## Slide 358
REST API - Real Product Examples
▸ Stripe API: gold standard REST design with idempotency keys, versioning, deep filtering
  ↳ GET /v1/charges?limit=10&customer=cus_123; uses cursor pagination via starting_after
▸ GitHub API v3: classic REST with hypermedia links and rate limit headers
  ↳ GET /repos/{owner}/{repo}/issues; includes Link headers for pagination
▸ Twilio, Twitter v1.1, Slack Web API: similar RESTful patterns
  ↳ Resource URLs, HTTP methods, JSON payloads, OAuth tokens
▸ Common patterns: API keys in Authorization header, JSON request/response, rate limit headers
  ↳ X-RateLimit-Remaining and Retry-After are de facto standards
▸ These APIs demonstrate REST's strengths: discoverability, cacheability, ecosystem support
  ↳ Every language has a great HTTP client; Postman/Insomnia work out of the box
📊 Logos of Stripe, GitHub, Twilio, Slack with example endpoints listed below each

## Slide 359
REST Diagram - Request/Response Lifecycle
▸ Client -> DNS lookup -> TCP/TLS handshake -> HTTP request -> server
  ↳ Modern clients reuse connections; first request pays handshake cost, subsequent ones don't
▸ Server -> auth middleware -> rate limiter -> router -> controller -> database -> response builder
  ↳ Each layer can short-circuit (401 from auth, 429 from rate limiter)
▸ Response flows back: HTTP response -> CDN cache check -> client
  ↳ Cacheable responses get stored at edge; subsequent requests skip the origin
▸ Status code, headers, body all carry information for the client
  ↳ Client parses JSON, reads pagination links, updates UI
▸ Understanding this lifecycle helps debug latency: where is the time going?
  ↳ DNS? TLS? Server-side? Database? Network? Different fixes for different bottlenecks
📊 Sequence diagram from browser to CDN to LB to app server to DB and back, with latency annotations

## Slide 360
RPC - Concept Introduction
▸ RPC (Remote Procedure Call) lets you call a function on another machine like it's local
  ↳ clientStub.getUser(42) feels like a local call but executes on a remote server
▸ Hides network details behind a function call abstraction
  ↳ Marshaling, network I/O, error handling all wrapped by generated stub code
▸ Older than HTTP: ONC RPC (Sun, 1984), CORBA, Java RMI all predate REST
  ↳ The idea is fundamental; modern incarnations (gRPC, Thrift) refined the execution
▸ Exists because thinking in functions is more natural than thinking in resources
  ↳ For service-to-service calls, "createOrder(customer, items)" feels right; REST forces noun-shaping
▸ The illusion is leaky: networks fail, latency exists, partial failures happen
  ↳ Fallacies of distributed computing - treating remote calls as local is the original sin
📊 Two boxes labeled "Client" and "Server" with a function call arrow that conceptually crosses both

## Slide 361
gRPC Deep Dive
▸ gRPC = Google RPC: HTTP/2 transport, Protocol Buffers serialization, multi-language codegen
  ↳ Open-sourced by Google in 2015; built on internal Stubby system
▸ Protobuf .proto files define services and messages; tooling generates clients and servers
  ↳ One source of truth; generated code is type-safe in Go, Java, Python, C++, etc.
▸ Four streaming modes: unary, server-streaming, client-streaming, bidirectional
  ↳ Replaces REST + WebSockets + polling with a single protocol
▸ HTTP/2 multiplexing means one connection handles many concurrent calls
  ↳ Header compression and binary framing cut overhead vs JSON over HTTP/1.1
▸ Built-in deadlines, cancellation, retries, load balancing primitives
  ↳ Production-grade out of the box; cloud providers offer managed gRPC routing
📊 .proto schema -> code generator -> client stub + server skeleton in 4 different languages

## Slide 362
gRPC vs REST - When to Use Each
▸ gRPC: internal microservice-to-microservice communication
  ↳ Strong typing, low latency, streaming, polyglot teams; Netflix, Square, Uber use it heavily
▸ REST: public APIs, browser clients, simple CRUD
  ↳ Universal tooling, debuggable with curl, no special client libraries
▸ gRPC needs HTTP/2; some networks/proxies still struggle (improving fast)
  ↳ gRPC-Web bridges browsers but adds a proxy hop
▸ REST is easier to evolve loosely; gRPC enforces stricter contracts
  ↳ Trade-off: REST flexibility vs gRPC safety
▸ Many companies run both: REST at the edge for clients, gRPC internally between services
  ↳ GraphQL is sometimes the third option for complex client queries
📊 Architecture diagram - mobile/browser -> REST gateway -> gRPC mesh of microservices -> databases

## Slide 363
Protobuf vs JSON
▸ Protobuf is a binary, schema-first serialization format
  ↳ Fields tagged by integer; no field names on the wire; schema required to decode
▸ JSON is text, schema-less, self-describing
  ↳ Human-readable; works without any external definition; ubiquitous tooling
▸ Size: Protobuf typically 30-70% smaller than equivalent JSON
  ↳ No quotes, no field names, integers packed efficiently, repeated fields delta-encoded
▸ Speed: Protobuf parses 5-10x faster than JSON in most languages
  ↳ Generated parsers walk fixed offsets; JSON parsers tokenize and allocate strings
▸ Trade-off: JSON debuggable in any browser/curl; Protobuf needs schema and tools to inspect
  ↳ Use Protobuf when bandwidth/CPU matter; JSON when human inspection matters
📊 Same User object shown as 200-byte JSON next to 80-byte Protobuf hex dump, with parse-time benchmark bars

## Slide 364
gRPC Diagram - Streaming Modes
▸ Unary: one request, one response (like REST GET)
  ↳ getUser(id) -> User
▸ Server streaming: one request, stream of responses
  ↳ listEvents(filter) -> stream of Event messages; great for log tailing, news feeds
▸ Client streaming: stream of requests, one response
  ↳ uploadChunks(stream of Chunk) -> UploadResult; useful for file uploads, batch ingestion
▸ Bidirectional streaming: both sides stream independently
  ↳ chat(stream of Message) -> stream of Message; perfect for real-time collaboration
▸ All four modes share one HTTP/2 connection and contract
  ↳ Replaces multiple protocols with a unified streaming model
📊 2x2 grid showing four streaming modes with arrows representing message flow direction

## Slide 365
RPC Real Examples and Trade-offs
▸ Google internal: Stubby (gRPC's predecessor) for thousands of microservices
  ↳ Every internal API call is RPC; REST is rare internally
▸ Kubernetes: gRPC for kubelet <-> API server, etcd <-> peers
  ↳ High-frequency control plane traffic benefits from binary efficiency
▸ Etsy, Square, Lyft: gRPC for service mesh; REST/GraphQL at the edge
  ↳ Internal latency drops 30-50% vs JSON-over-HTTP/1.1
▸ Trade-offs: harder to debug (need grpcurl or BloomRPC), browser support requires gRPC-Web
  ↳ Tooling has matured but still less ubiquitous than HTTP/JSON
▸ Choose RPC for service mesh; REST for public APIs; both for hybrid architectures
  ↳ The right answer is rarely one protocol everywhere
📊 Real-world stack - mobile app -> REST -> API gateway -> gRPC -> 50 microservices

## Slide 366
WebSockets - Concept Introduction
▸ WebSocket is a full-duplex, persistent connection over a single TCP socket
  ↳ After an HTTP-based handshake (Upgrade: websocket), the connection becomes bidirectional
▸ Both sides can send messages anytime without waiting for a request
  ↳ Server pushes events to client; client sends commands to server; symmetric
▸ Designed for real-time, low-latency communication
  ↳ Avoids the cost of repeatedly opening HTTP connections or polling
▸ Works through most firewalls because it starts as HTTP
  ↳ Standard ports 80/443; survives most corporate proxies (with WSS for TLS)
▸ Exists because HTTP's request-response model is wrong for real-time apps
  ↳ Before WebSockets, "real-time" meant ugly hacks like long polling or Comet
📊 HTTP handshake transitioning into a persistent bidirectional pipe with messages flowing both ways

## Slide 367
WebSockets vs Polling vs SSE
▸ Short polling: client requests every N seconds; simple but wasteful
  ↳ 60 requests/min for sub-second freshness; horrendous server load and battery drain
▸ Long polling: client request hangs until server has data, then immediately reconnects
  ↳ Lower waste than short polling but still HTTP overhead per message; complex on server
▸ SSE (Server-Sent Events): one-way server-to-client over HTTP
  ↳ Simpler than WebSockets; built-in reconnection; client cannot push (uses separate HTTP for that)
▸ WebSocket: full-duplex, lowest latency, persistent connection
  ↳ Best for chat, collaborative editing, multiplayer games
▸ Choose based on traffic pattern: SSE for read-heavy feeds, WebSocket for interactive
  ↳ Stock tickers and news feeds work great with SSE; chat needs WebSockets
📊 Four timelines comparing short polling, long polling, SSE, and WebSocket - showing message latency and connection count

## Slide 368
WebSockets - Real Product Examples
▸ Discord: WebSocket for voice channel signaling, presence, chat
  ↳ Millions of concurrent connections; uses Erlang/Elixir for connection-heavy workloads
▸ Slack: WebSocket (RTM API) for real-time message delivery
  ↳ Now mostly Events API + WebSocket fallback; chat updates feel instant
▸ Trading platforms (Robinhood, Coinbase): WebSocket for market data streams
  ↳ Sub-millisecond price updates require persistent push connections
▸ Collaborative editors (Google Docs, Figma, Notion): WebSocket for OT/CRDT sync
  ↳ Every keystroke flows over WebSocket so other users see edits in real time
▸ Multiplayer games (Agar.io, browser games): WebSocket for game state
  ↳ When UDP isn't available (browsers), WebSocket is the lowest-latency option
📊 Product logos with their use case - Discord (voice signaling), Figma (cursor sync), Robinhood (price updates)

## Slide 369
WebSocket Trade-offs and Scaling
▸ Stateful connections complicate horizontal scaling
  ↳ Load balancers need sticky sessions or pub/sub backplane (Redis, Kafka) to broadcast
▸ Memory and file descriptors per connection
  ↳ 1M connections = 1M sockets in kernel + app memory; tune ulimits and use efficient runtimes
▸ Reconnection logic is your problem: networks drop, mobile switches Wi-Fi/cellular
  ↳ Implement exponential backoff, resume tokens, deduplication
▸ No built-in caching, batching, or rate limiting like HTTP
  ↳ You build the application protocol on top - message types, ack semantics, heartbeats
▸ Choose only when you actually need real-time bidirectional comms
  ↳ For "every minute" updates, polling or SSE is simpler and cheaper
📊 WebSocket scaling architecture - clients -> sticky LB -> WebSocket servers -> Redis pub/sub -> backend

## Slide 370
WebSocket Diagram - Connection Lifecycle
▸ Step 1: Client sends HTTP request with Upgrade: websocket and Sec-WebSocket-Key headers
  ↳ Looks like normal HTTP, traverses any HTTP-aware infrastructure
▸ Step 2: Server responds 101 Switching Protocols; TCP connection now speaks WebSocket
  ↳ Transition is irreversible; same socket carries WS frames
▸ Step 3: Both sides exchange framed messages (text or binary) anytime
  ↳ Frames have small headers; messages can be fragmented across frames
▸ Step 4: Heartbeats (ping/pong) keep connection alive through NAT timeouts
  ↳ Without them, idle connections die silently after a few minutes
▸ Step 5: Either side sends close frame; TCP socket teardown follows
  ↳ Graceful close codes communicate intent (1000 normal, 1001 going away, 1006 abnormal)
📊 Sequence diagram - HTTP upgrade handshake, then bidirectional message flow, then close handshake

## Slide 371
GraphQL - Concept Introduction
▸ GraphQL is a query language and runtime for APIs, developed by Facebook (2012, open-sourced 2015)
  ↳ Client specifies exactly what fields it needs; server returns exactly that
▸ Single endpoint (typically /graphql); one POST per query regardless of resources fetched
  ↳ Replaces dozens of REST endpoints with one schema-driven entry point
▸ Strongly typed schema defines all queries, mutations, subscriptions
  ↳ Schema is the contract; tools (GraphiQL, codegen) leverage it for great DX
▸ Solves over-fetching and under-fetching problems in REST
  ↳ REST: one endpoint returns 50 fields when you need 3 (over-fetching) or you call 5 endpoints to assemble a screen (under-fetching)
▸ Exists because mobile clients have varied data needs and bandwidth constraints
  ↳ Facebook's mobile teams built it to ship features without backend coupling
📊 GraphQL query alongside its precise JSON response, contrasted with REST returning a bloated payload

## Slide 372
GraphQL vs REST - Trade-offs
▸ GraphQL flexibility: client-driven queries, no versioning needed (deprecate fields, add new ones)
  ↳ Mobile teams can iterate without waiting for backend endpoint changes
▸ REST simplicity: HTTP caching just works; CDN-friendly; debuggable
  ↳ GraphQL needs custom caching (Apollo, Relay) since all queries POST to one URL
▸ GraphQL complexity costs: N+1 query problem, complex authorization, harder to rate limit
  ↳ DataLoader pattern, query depth limits, persisted queries help but add overhead
▸ REST excels for cacheable resource-oriented APIs; GraphQL excels for complex client UIs
  ↳ Facebook, Shopify, GitHub (v4) ship GraphQL; Stripe, AWS still REST-first
▸ Choose GraphQL when client data needs vary widely; REST when resources are stable and cacheable
  ↳ Hybrid is common: REST for public API, GraphQL for internal app backend
📊 Decision matrix - "Many clients with different needs?" GraphQL; "Public API with caching?" REST

## Slide 373
GraphQL Real Examples and When to Use
▸ GitHub API v4: full GraphQL replacement for REST v3
  ↳ One query fetches repo + issues + PRs + comments in a single round trip
▸ Shopify Storefront API: GraphQL for theme/storefront customization
  ↳ Frontend devs assemble exactly the product data they need
▸ Facebook, Instagram, Twitter (partially): GraphQL powers mobile apps
  ↳ Bandwidth-constrained mobile clients benefit most from precise queries
▸ Use GraphQL when: many client types, evolving UIs, complex relationships, mobile bandwidth concerns
  ↳ Avoid when: simple CRUD, public API needing HTTP caching, small team without GraphQL experience
▸ Subscriptions provide real-time updates over WebSocket
  ↳ GraphQL becomes a unified query/mutation/streaming layer
📊 GitHub GraphQL example - one query fetching repo metadata, last 10 issues, and authors' avatars

## Slide 374
GraphQL Diagram - Query Resolution Flow
▸ Client sends POST /graphql with query string and variables
  ↳ Single endpoint; query body describes the desired shape of the response
▸ Server parses query, validates against schema, generates execution plan
  ↳ Type-checks every field, argument, fragment before any resolver runs
▸ Resolvers fetch each field, often in parallel; DataLoader batches DB calls to avoid N+1
  ↳ getUser resolver triggers, getOrders resolver runs in parallel, etc.
▸ Server assembles result tree matching query shape; returns JSON
  ↳ Errors are partial: you can get 200 OK with some fields populated and some null with errors[]
▸ Client merges into normalized cache (Apollo/Relay) for fast subsequent renders
  ↳ Cache invalidation is fine-grained per object/field, not per URL
📊 Flow chart - query -> parse -> validate -> plan -> resolvers (parallel) -> assemble -> JSON

## Slide 375
Section Key Takeaways
▸ Protocol choice is a system design lever, not a default
  ↳ TCP for reliability, UDP for speed, HTTP/2 or 3 for web, gRPC for microservices, WebSocket for real-time, GraphQL for flexible queries
▸ Understand L4 vs L7 - it shapes load balancers, proxies, and security tooling
  ↳ "Where do I terminate TLS?" and "Can I route by URL?" both hinge on this
▸ Idempotency is non-negotiable for reliable distributed systems
  ↳ GET/PUT/DELETE safe to retry; POST needs idempotency keys
▸ HTTP versions matter: each generation removed a class of latency problem
  ↳ 1.1 -> 2 (multiplexing) -> 3 (no TCP HoL blocking)
▸ Real-time apps need persistent connections (WebSocket/SSE) - not polling
  ↳ Polling worked in 2005; in 2026 it's a code smell unless data is genuinely low-frequency
📊 One-page cheat sheet with protocol -> use case mapping

## Slide 376
Section Interview Tips
▸ Always justify protocol choice with concrete trade-offs
  ↳ "I'd use UDP because frame loss is acceptable but 50ms latency is not" beats "UDP is faster"
▸ Mention HTTP/2 or HTTP/3 when discussing modern web architecture
  ↳ Shows you're current; especially relevant for high-throughput services
▸ For real-time features, walk the polling -> long polling -> SSE -> WebSocket evolution
  ↳ Demonstrates depth; lets you choose the simplest option that meets the requirements
▸ Discuss idempotency and retries when designing payment, order, or messaging systems
  ↳ Interviewers love hearing "idempotency key in the request" for POST endpoints
▸ Know when to NOT use a protocol: GraphQL for simple CRUD, gRPC for browser, WebSocket for low-frequency updates
  ↳ Showing where things break is as valuable as knowing where they shine
📊 Interview script template - "Requirement -> Constraint -> Protocol -> Trade-off acknowledged"

## Slide 377
Section Common Pitfalls
▸ Defaulting to REST for everything ignoring streaming or low-latency needs
  ↳ "We just polled the API every 500ms" - now your server is melting
▸ Ignoring TCP head-of-line blocking when discussing HTTP/2 performance
  ↳ HTTP/2 doesn't fully solve HoL; HTTP/3 does (interview gotcha)
▸ Treating remote calls as local (RPC fallacy)
  ↳ Network failures, partial failures, timeouts must be designed for explicitly
▸ Using WebSockets when SSE or long polling would suffice
  ↳ Persistent bidirectional connections are expensive; use them when you actually need bidi
▸ Forgetting authentication, rate limiting, and observability at the protocol layer
  ↳ Every protocol needs auth (Bearer tokens, mTLS), throttling (429s, leaky buckets), and tracing (X-Request-ID)
▸ Not versioning APIs from day one
  ↳ "We'll add /v1 later" usually means breaking every existing client when "later" arrives
📊 "Avoid these traps" warning signs with each pitfall and its consequence

## Slide 378
Section 10: Security

## Slide 379
Section 11: Advanced Topics and Interview Framework

## Slide 380
Topic 1: Security Fundamentals

## Slide 381
Security Fundamentals - Concept Introduction
▸ Security is not a feature, it is a property of the entire system
  ↳ Every component, layer, and human interaction can be an attack surface
▸ Three foundational pillars: principles, mechanisms, and defenses
  ↳ Principles guide design, mechanisms enforce policy, defenses respond to attacks
▸ Goal: protect data, users, and infrastructure from unauthorized access or harm
  ↳ While maintaining usability and performance for legitimate users
▸ Security is continuous, not one-time
  ↳ Threats evolve; defenses must evolve with them
▸ Real example: Equifax 2017 breach exposed 147M records due to one unpatched library
  ↳ A single weak link compromised the entire fortress
📊 Concentric castle walls labeled "Network → Host → Application → Data" with arrows showing attacks bouncing off multiple layers

## Slide 382
Defense in Depth - Deep Explanation
▸ Defense in depth means layered security controls so no single failure is catastrophic
  ↳ If one layer fails, others still protect the asset
▸ Layers typically include: perimeter (firewall, WAF), network (VPC, segmentation), host (OS hardening), application (input validation, authz), data (encryption)
  ↳ Each layer is independent and uses different mechanisms
▸ Assume breach: design as if attackers will get past the outer wall
  ↳ Internal services should still authenticate, authorize, and log
▸ Redundant controls: multiple firewalls, multiple authentication factors, multiple logging systems
  ↳ Attacker must defeat every layer to succeed
▸ Real example: AWS uses VPC + Security Groups + NACLs + IAM + KMS as overlapping layers
  ↳ Compromising one does not grant access to data
📊 Onion diagram with layers labeled outer-to-inner: WAF, Firewall, IDS, Auth, Encryption, Audit Logs

## Slide 383
CIA Triad - The Three Pillars
▸ Confidentiality: only authorized parties can read data
  ↳ Achieved via encryption, access control, authentication
▸ Integrity: data is not tampered with in transit or at rest
  ↳ Achieved via hashing, digital signatures, checksums, version control
▸ Availability: legitimate users can access the system when needed
  ↳ Achieved via redundancy, DDoS protection, rate limiting, failover
▸ Trade-offs exist between the three pillars
  ↳ Heavy encryption can hurt availability; aggressive rate limiting can hurt availability for legitimate users
▸ Real example: Banking app must keep balance secret (C), unalterable (I), and accessible 24/7 (A)
  ↳ Failure in any one pillar destroys trust
📊 Equilateral triangle with vertices labeled Confidentiality, Integrity, Availability; center labeled "Security"

## Slide 384
Authentication vs Authorization - Example/Intuition
▸ Authentication (AuthN) answers: who are you?
  ↳ Verifies identity using passwords, tokens, biometrics, certificates
▸ Authorization (AuthZ) answers: what are you allowed to do?
  ↳ Determines permissions, roles, scopes, resource access
▸ Order matters: authenticate first, then authorize
  ↳ Cannot grant permissions without knowing the identity
▸ Common mistake: conflating the two leads to security holes
  ↳ A logged-in user is not automatically allowed to access every resource
▸ Real example: Boarding a plane - showing your ID is authentication, your ticket class is authorization
  ↳ ID gets you in the airport; ticket determines which seat
📊 Two-step gate diagram. Gate 1: "Who are you?" with ID check. Gate 2: "What can you do?" with permission badge check

## Slide 385
Principle of Least Privilege - Diagram
▸ Grant the minimum permissions needed to perform a task, nothing more
  ↳ Reduces blast radius if credentials are compromised
▸ Apply to users, services, processes, and database accounts
  ↳ Microservice X should not have DROP TABLE privilege if it only reads
▸ Time-bound access: temporary elevation when needed, revoked after
  ↳ JIT (just-in-time) access for production debugging
▸ Role-based access control (RBAC) and attribute-based access control (ABAC) operationalize this principle
  ↳ Roles bundle permissions; attributes add context (time, location, resource tag)
▸ Real example: AWS IAM roles for EC2 instances scoped to specific S3 buckets and actions
  ↳ A compromised instance cannot enumerate or delete unrelated buckets
📊 Org chart where each role has a small key icon labeled with only the specific permissions it holds; CEO does NOT have all keys

## Slide 386
Security Fundamentals - Trade-offs
▸ Security vs Usability: stronger controls add friction
  ↳ 2FA improves security but slows login; balance per risk level
▸ Security vs Performance: encryption and validation cost CPU
  ↳ TLS termination at edge; selective encryption of sensitive fields
▸ Security vs Cost: dedicated security teams, audits, tooling are expensive
  ↳ Match investment to threat model and data sensitivity
▸ Security vs Developer Velocity: strict review gates slow shipping
  ↳ Automate scans (SAST, DAST, dependency scanning) into CI/CD
▸ Real example: Google BeyondCorp replaced VPN with continuous device + user verification
  ↳ Higher security with better UX, but multi-year investment
📊 Four-quadrant chart with security on Y-axis and usability/performance/cost/velocity on X-axis showing balance points

## Slide 387
Topic 2: Encryption

## Slide 388
Encryption - Concept Introduction
▸ Encryption transforms readable data (plaintext) into unreadable ciphertext using a key
  ↳ Only those with the right key can reverse it
▸ Two main families: symmetric (one shared key) and asymmetric (key pair)
  ↳ Each has different strengths, costs, and use cases
▸ Encryption protects confidentiality; signing protects integrity and authenticity
  ↳ Often combined in real protocols
▸ Encryption is mathematics, not obscurity
  ↳ Algorithms are public; security depends on key secrecy
▸ Real example: WhatsApp E2EE uses Signal Protocol so even WhatsApp servers cannot read messages
  ↳ Encryption shifts trust from servers to math
📊 "HELLO" + key icon → AES box → "8x#2K9z" with locked padlock icon

## Slide 389
Symmetric Encryption (AES) - Deep Explanation
▸ Same key encrypts and decrypts; both parties must share it secretly
  ↳ Fast, suitable for bulk data
▸ AES (Advanced Encryption Standard) is the modern default
  ↳ 128-bit and 256-bit key sizes; hardware-accelerated on modern CPUs
▸ Modes matter: AES-GCM provides authenticated encryption (confidentiality + integrity)
  ↳ Avoid ECB; use GCM or CBC with HMAC
▸ Key distribution is the hard problem
  ↳ How do two parties agree on a shared key without anyone intercepting it?
▸ Real example: AWS S3 server-side encryption uses AES-256-GCM at rest
  ↳ Throughput is gigabytes per second per core
📊 Alice and Bob each holding identical key icons, both encrypting/decrypting a shared lockbox

## Slide 390
Asymmetric Encryption (RSA) - Deep Explanation
▸ Two mathematically linked keys: public (share freely) and private (keep secret)
  ↳ Encrypt with public, decrypt with private; or sign with private, verify with public
▸ RSA, ECC (Elliptic Curve), Ed25519 are common asymmetric algorithms
  ↳ ECC offers same security with smaller keys (256-bit ECC ≈ 3072-bit RSA)
▸ 100-1000x slower than symmetric; used for key exchange and signatures, not bulk data
  ↳ Encrypt a symmetric session key with RSA, then use AES for the conversation
▸ Solves key distribution: anyone can send you encrypted data using your public key
  ↳ Foundation of TLS, SSH, signed software updates
▸ Real example: GitHub SSH keys use Ed25519/RSA so you authenticate without sharing a password
  ↳ Your private key never leaves your laptop
📊 Alice has lock + private key. Bob downloads Alice's open lock (public key), uses it to lock a box, sends it. Only Alice's priva...

## Slide 391
TLS Handshake - Example/Intuition
▸ TLS combines asymmetric (for key exchange) and symmetric (for data) encryption
  ↳ Best of both worlds: secure setup, fast bulk transfer
▸ Steps: ClientHello → ServerHello + certificate → key exchange (ECDHE) → Finished → encrypted application data
  ↳ Modern TLS 1.3 reduces this to 1 round trip (1-RTT) or even 0-RTT for resumed sessions
▸ Server presents an X.509 certificate signed by a Certificate Authority (CA)
  ↳ Browser validates the chain back to a trusted root CA
▸ Result: a shared symmetric session key both sides can use
  ↳ Forward secrecy ensures past sessions stay safe even if long-term keys leak
▸ Real example: Browsing https://google.com triggers a full TLS 1.3 handshake in <100ms
  ↳ Padlock icon means handshake succeeded and traffic is encrypted
📊 Sequence diagram: Client ↔ Server with arrows labeled ClientHello, ServerHello+Cert, KeyExchange, Finished, EncryptedData

## Slide 392
End-to-End Encryption (E2EE) - Deep Explanation
▸ Only the communicating endpoints can read the data
  ↳ Servers in the middle see only ciphertext
▸ Compare to transport encryption (TLS): server can decrypt and re-encrypt
  ↳ With E2EE, even the service provider cannot read content
▸ Key management is the hard part: how do users verify each other's keys?
  ↳ Safety numbers, QR code verification, key transparency logs
▸ Trade-offs: lose server-side features (search, content moderation, multi-device sync becomes complex)
  ↳ Many features must move to client side
▸ Real example: Signal, WhatsApp, iMessage use E2EE; Gmail does not
  ↳ Your iMessage cannot be subpoenaed from Apple's servers in readable form
📊 Alice → Server (lock icon, server cannot read) → Bob; vs TLS where server has a key icon and can read

## Slide 393
At-Rest vs In-Transit Encryption - Diagram
▸ In-transit: protects data moving over networks
  ↳ TLS for HTTP, SSH, database connections, service-to-service mTLS
▸ At-rest: protects data stored on disk, in databases, in backups
  ↳ Disk encryption, database TDE, S3 SSE, encrypted backups
▸ In-use (emerging): protects data while being processed
  ↳ Confidential computing with Intel SGX, AWS Nitro Enclaves
▸ Both are required; encrypting only one leaves the other exposed
  ↳ HTTPS without disk encryption: stolen drive reveals everything
▸ Real example: HIPAA and PCI-DSS require both at-rest and in-transit encryption for sensitive data
  ↳ Auditors check key rotation, algorithm, and scope
📊 Three-state diagram: Disk (lock) → Network pipe (lock) → Memory/CPU (lock with question mark for in-use)

## Slide 394
Encryption - Trade-offs
▸ Symmetric: fast but key distribution is hard
  ↳ Use for bulk data after key is established
▸ Asymmetric: solves distribution but slow
  ↳ Use for key exchange, signatures, certificates
▸ Stronger keys (256 vs 128) cost more CPU; usually negligible on modern hardware
  ↳ Choose 256-bit for long-lived sensitive data
▸ Key rotation: needed but operationally complex
  ↳ Use envelope encryption: data keys encrypted by master keys (KMS pattern)
▸ Real example: AWS KMS, Google Cloud KMS, HashiCorp Vault provide managed key rotation and audit
  ↳ Avoid rolling your own crypto; use vetted libraries (libsodium, BoringSSL)
📊 Comparison table - Symmetric vs Asymmetric across columns: Speed, Key Distribution, Use Case, Example Algorithm

## Slide 395
Topic 3: Authentication Mechanisms

## Slide 396
Password Storage - Concept Introduction
▸ Never store plaintext passwords
  ↳ A breach exposes every user account immediately
▸ Hash passwords with a slow, salted, adaptive function
  ↳ bcrypt, scrypt, Argon2, PBKDF2 are designed to be slow on purpose
▸ Salt: random per-user value mixed into the hash
  ↳ Prevents rainbow table attacks; identical passwords produce different hashes
▸ Pepper: server-side secret added to all hashes (extra defense)
  ↳ Stored separately from the database
▸ Real example: LinkedIn 2012 breach leaked 117M unsalted SHA-1 password hashes; cracked within days
  ↳ Modern bcrypt with cost factor 12 would have made this far harder
📊 Password "hunter2" + salt "x9k2" → bcrypt(cost=12) → "$2b$12$abc...xyz"; arrow to database row

## Slide 397
Password Hashing - Deep Explanation
▸ bcrypt: Blowfish-based, configurable cost factor (work parameter)
  ↳ Cost 12-14 typical in 2026; double work each time CPUs get faster
▸ Argon2: winner of Password Hashing Competition; memory-hard
  ↳ Resists GPU/ASIC cracking better than bcrypt
▸ Time complexity: each password verification should take ~100-500ms
  ↳ Slow enough to deter brute force, fast enough for UX
▸ Never use MD5, SHA-1, or fast hashes for passwords
  ↳ GPUs can crack billions of fast hashes per second
▸ Real example: Dropbox uses bcrypt + AES wrapper; 1Password uses PBKDF2 with high iteration count
  ↳ Defense layers compound
📊 Comparison bar chart - MD5 (1B/sec crack rate, RED), SHA-256 (100M/sec, ORANGE), bcrypt (10K/sec, YELLOW), Argon2 (1K/sec, GREEN)

## Slide 398
JWT (JSON Web Tokens) - Deep Explanation
▸ Self-contained token: header.payload.signature, base64url encoded
  ↳ Server signs; clients send back; server verifies signature
▸ Stateless authentication: no server-side session lookup needed
  ↳ Scales horizontally; any server can validate
▸ Payload contains claims: sub (user id), exp (expiry), iat, custom roles
  ↳ Visible to anyone who has the token; do not put secrets there
▸ Algorithms: HS256 (shared secret), RS256 (asymmetric, public verification)
  ↳ Use RS256 when verifiers (microservices) should not be able to forge tokens
▸ Real example: Auth0, Firebase Auth, AWS Cognito issue JWTs for API access
  ↳ Short expiry (15 min) + refresh token pattern is standard
📊 Three colored boxes - Header (red) . Payload (purple) . Signature (cyan) - with decoded JSON beneath each

## Slide 399
OAuth 2.0 / OpenID Connect - Example/Intuition
▸ OAuth 2.0: authorization framework for delegated access
  ↳ "Let App X access my Google Drive without giving X my Google password"
▸ OpenID Connect (OIDC): authentication layer on top of OAuth 2.0
  ↳ Adds ID token (JWT) so apps can verify who the user is
▸ Common flows: Authorization Code (web apps), Authorization Code + PKCE (mobile/SPA), Client Credentials (service-to-service)
  ↳ Implicit flow is deprecated; do not use
▸ Tokens: access token (short-lived, used in API calls), refresh token (long-lived, used to get new access tokens)
  ↳ Refresh tokens require secure storage
▸ Real example: "Sign in with Google" on a third-party site uses OIDC + Authorization Code flow
  ↳ You log into Google; site receives ID token + access token
📊 Sequence diagram - User → App → Auth Server → Resource Server with redirect arrows and token exchange

## Slide 400
API Keys vs Session Tokens vs JWT - Diagram
▸ API Keys: long-lived, identify a client/app, often no user context
  ↳ Best for server-to-server; rotate regularly; never expose in client code
▸ Session tokens: opaque random IDs stored server-side (Redis, DB)
  ↳ Easy to revoke (delete the row); requires lookup per request
▸ JWT: signed self-contained tokens, stateless verification
  ↳ Hard to revoke before expiry without a denylist
▸ Choose based on revocation needs, scale, and trust model
  ↳ Session for sensitive apps with logout; JWT for high-scale stateless APIs
▸ Real example: Stripe uses API keys; banking apps use sessions; modern SaaS uses JWT + refresh
  ↳ Hybrid: short JWT for API calls + opaque refresh token in HttpOnly cookie
📊 3-column comparison table - API Key, Session Token, JWT - rows: Storage, Revocation, Stateless?, Use Case

## Slide 401
Authentication - Trade-offs
▸ Stateless (JWT) vs Stateful (sessions)
  ↳ Stateless scales easier; stateful revokes easier
▸ Short expiry vs UX friction
  ↳ 15-min access tokens require refresh logic; 24-hour tokens are riskier if stolen
▸ Single sign-on (SSO) vs independent auth per app
  ↳ SSO simpler for users, single point of failure for security
▸ MFA strength: SMS (weakest, SIM swap risk) → TOTP apps → Hardware keys (FIDO2/WebAuthn, strongest)
  ↳ Hardware keys phishing-resistant by design
▸ Real example: GitHub now requires hardware-backed 2FA for contributors to popular repos
  ↳ Phishing-resistant MFA mitigates the most common attack vector
📊 2x2 matrix - Security strength vs User friction, with MFA methods plotted (SMS, TOTP, Push, Hardware Key)

## Slide 402
Topic 4: Common Vulnerabilities (OWASP Top 10)

## Slide 403
OWASP Top 10 - Concept Introduction
▸ OWASP Top 10: industry-standard list of most critical web vulnerabilities
  ↳ Updated every 3-4 years based on real breach data
▸ Categories include: Broken Access Control, Cryptographic Failures, Injection, Insecure Design, Security Misconfiguration
  ↳ Most breaches map to one of these classes
▸ Defenses are well-known; problem is consistent application across teams and code
  ↳ Automation (SAST, DAST, dependency scanning) catches most common issues
▸ Awareness is step one; secure-by-default frameworks are step two
  ↳ Modern frameworks prevent many vulnerabilities if used as intended
▸ Real example: Capital One 2019 breach (100M records) was Broken Access Control via SSRF
  ↳ One misconfigured WAF rule cascaded into a massive breach
📊 Top 10 list as a leaderboard with attack icons next to each, colored red-to-yellow by severity

## Slide 404
SQL Injection - Deep Explanation
▸ Attacker injects SQL through user input that is concatenated into queries
  ↳ Classic: ' OR '1'='1 in a login form bypasses authentication
▸ Defense: parameterized queries (prepared statements)
  ↳ Database treats input as data, never as code
▸ ORMs and query builders use parameterization by default
  ↳ Avoid raw query construction with string concatenation
▸ Defense in depth: input validation, least-privilege DB accounts, WAF, query allowlists
  ↳ Read-only service should not have write DB credentials
▸ Real example: 2008 Heartland Payment Systems breach (130M cards) started with SQL injection
  ↳ Parameterized queries would have prevented it entirely
📊 Two code snippets side-by-side - Bad (string concat with red X) vs Good (prepared statement with green check)

## Slide 405
Cross-Site Scripting (XSS) - Deep Explanation
▸ Attacker injects malicious JavaScript into pages viewed by other users
  ↳ Steals cookies, session tokens, performs actions as victim
▸ Three types: Stored (in DB), Reflected (in URL), DOM-based (client-side rendering)
  ↳ All exploit insufficient output encoding
▸ Defense: contextual output encoding (HTML, JS, URL contexts each need different escaping)
  ↳ Modern frameworks (React, Vue) escape by default; danger lies in dangerouslySetInnerHTML
▸ Content Security Policy (CSP) headers: restrict what scripts can run and where
  ↳ Defense in depth even if encoding fails
▸ Real example: 2010 Twitter onMouseOver worm spread by self-retweeting via stored XSS
  ↳ Took down Twitter for hours; CSP would have blocked it
📊 Attacker → injects <script> into comment → victim views page → script sends victim cookie to attacker server

## Slide 406
CSRF - Deep Explanation
▸ Cross-Site Request Forgery: tricks an authenticated user's browser into making unwanted requests
  ↳ Attacker site embeds <img src="https://bank.com/transfer?to=attacker&amount=1000"> while user is logged in
▸ Defense: CSRF tokens (random per-session value required in form submissions)
  ↳ Server rejects requests missing the token
▸ Defense: SameSite cookies (Lax or Strict) prevent cross-origin cookie sending
  ↳ Modern browsers default to Lax
▸ Defense: check Origin / Referer headers for state-changing requests
  ↳ Defense in depth alongside CSRF tokens
▸ Real example: 2008 Gmail CSRF allowed attackers to add email forwarding rules silently
  ↳ Now all major frameworks ship with CSRF protection by default
📊 Attacker site with hidden form auto-submits to bank.com using victim's logged-in session cookie

## Slide 407
DDoS and MITM - Example/Intuition
▸ DDoS (Distributed Denial of Service): overwhelm capacity with traffic from many sources
  ↳ Volumetric (bandwidth), protocol (SYN floods), application-layer (HTTP floods)
▸ DDoS defense: CDN absorption (Cloudflare, Akamai), rate limiting, scrubbing centers, anycast routing
  ↳ Distribute and absorb at the edge before reaching origin
▸ MITM (Man-in-the-Middle): attacker intercepts/modifies traffic
  ↳ Public WiFi, compromised routers, rogue CAs
▸ MITM defense: HTTPS everywhere, HSTS headers, certificate pinning for mobile apps
  ↳ HSTS forces browsers to use HTTPS; pinning prevents rogue CA attacks
▸ Real example: Cloudflare absorbed 26M req/sec DDoS in 2022; GitHub absorbed 1.35 Tbps in 2018
  ↳ Largest attacks now exceed terabits per second
📊 Left - thousands of bots → CDN edge (shield icon) → small filtered traffic → origin. Right - Alice → MITM attacker (eye icon) →...

## Slide 408
Vulnerabilities - Trade-offs
▸ WAF rules: too strict blocks legitimate users; too loose lets attacks through
  ↳ Tune over time using blocked-request analysis
▸ Rate limiting: too aggressive impacts power users; too lenient allows abuse
  ↳ Tiered limits per user class
▸ CSP: strict policy requires refactoring inline scripts/styles
  ↳ Start in report-only mode; tighten incrementally
▸ Input sanitization vs output encoding: encode at output (context-aware) is safer
  ↳ Sanitization can miss edge cases; encoding is provably safe per context
▸ Real example: Stripe's WAF was tuned over years using ML on legitimate traffic patterns
  ↳ Continuous tuning is more important than initial config
📊 Risk-vs-friction chart for each defense, plotted as dots

## Slide 409
Topic 5: Rate Limiting

## Slide 410
Rate Limiting - Concept Introduction
▸ Cap the number of requests a client can make in a time window
  ↳ Protects against abuse, brute force, accidental DoS, runaway scripts
▸ Without it: a single buggy client can take down your service
  ↳ Or attackers can scrape, enumerate, or exhaust resources
▸ Apply at multiple layers: edge (CDN, WAF), API gateway, service, database
  ↳ Earlier layers are cheaper; later layers are more granular
▸ Returns HTTP 429 Too Many Requests with Retry-After header
  ↳ Well-behaved clients back off
▸ Real example: GitHub API: 5000 req/hour authenticated, 60 req/hour unauthenticated
  ↳ Twitter API rate limits forced developers to design with backoff from day one
📊 Funnel - many requests at top → rate limiter (filter icon) → smaller stream of allowed requests, with rejected ones bouncing off

## Slide 411
Token Bucket Algorithm - Deep Explanation
▸ Bucket holds N tokens; each request consumes 1 token
  ↳ Tokens refill at rate R per second up to bucket capacity
▸ Allows bursts up to bucket size, then sustained rate R
  ↳ Friendly to bursty traffic patterns (e.g., page load with many assets)
▸ Stateless to implement with Redis: store {token_count, last_refill_timestamp}
  ↳ On request: refill based on elapsed time, decrement, accept or reject
▸ Pros: simple, supports bursts, well-understood
  ↳ Cons: can allow short bursts that overwhelm downstream
▸ Real example: AWS API Gateway uses token bucket per API key
  ↳ Stripe API uses token bucket with burst + steady-state limits
📊 Bucket icon with falling drops (tokens) at rate R, requests on the right scooping tokens to enter the system

## Slide 412
Leaky Bucket Algorithm - Deep Explanation
▸ Requests enter a queue (bucket); processed at constant rate R (drain rate)
  ↳ If bucket overflows, new requests are dropped or rejected
▸ Smooths bursts into a steady stream
  ↳ Output rate is always constant regardless of input pattern
▸ Stricter than token bucket: no burst allowance
  ↳ Better for downstream systems that cannot tolerate spikes
▸ Trade-off: legitimate burst users (page loads, batch ops) get throttled
  ↳ Less friendly to UX
▸ Real example: Network routers use leaky bucket for QoS shaping
  ↳ Cellular carriers use leaky bucket variants for fair usage
📊 Bucket with hole at bottom, water dripping out at constant rate R, top inflow showing variable bursts that overflow when bucket...

## Slide 413
Fixed Window vs Sliding Window - Example/Intuition
▸ Fixed window: count requests in [00:00-00:59], reset at top of each minute
  ↳ Simple but allows 2x burst at window boundary (59 reqs at 00:59 + 60 at 01:00)
▸ Sliding window log: track timestamp of each request, count in last 60 seconds
  ↳ Accurate but expensive (memory grows with request volume)
▸ Sliding window counter: weighted blend of current and previous fixed windows
  ↳ Approximates sliding log with constant memory
▸ Choose based on accuracy vs memory: fixed (cheapest), sliding counter (balanced), sliding log (most accurate)
  ↳ Most APIs use sliding counter
▸ Real example: Cloudflare uses sliding window counters across global edge
  ↳ Redis sorted sets implement sliding window log easily
📊 Three timeline bars - Fixed (clear minute boundaries), Sliding Log (every dot tracked), Sliding Counter (smooth gradient)

## Slide 414
Rate Limiting - Where to Apply
▸ API gateway / reverse proxy: protect all backend services uniformly
  ↳ Kong, Envoy, Nginx, AWS API Gateway, Cloudflare
▸ CDN edge: absorb global traffic before it reaches origin
  ↳ Cheapest place to drop bad traffic
▸ Application layer: per-endpoint rules (e.g., login is stricter than search)
  ↳ Per-feature granularity
▸ Distributed store: Redis with atomic INCR + EXPIRE for shared counters across nodes
  ↳ Or local in-memory + gossip for low latency
▸ Real example: GitHub layers - Cloudflare → HAProxy → Rails app, each with different limits
  ↳ Login endpoint: 10/min/IP; API: 5000/hour/token; webhooks: 1000/min
📊 Layered architecture - User → CDN (limit A) → Gateway (limit B) → Service (limit C) → DB

## Slide 415
Per-User vs Per-IP vs Per-Endpoint - Diagram
▸ Per-IP: blocks abusive networks; problem with NAT, mobile carriers, corporate proxies
  ↳ Many legitimate users behind one IP
▸ Per-user (authenticated): fair allocation per identity
  ↳ Requires authentication; does not protect login itself
▸ Per-endpoint: tighter limits on sensitive ops (login, password reset, payment)
  ↳ Defends against credential stuffing
▸ Per-API-key: B2B fairness across customers
  ↳ Combine with quota for billing tiers
▸ Real example: Login endpoint - 5/min/IP + 10/hour/account combined
  ↳ Password reset - 3/hour/account to prevent enumeration
📊 Multi-dimensional table with rows IP/User/Endpoint/Key and columns showing example limits and use cases

## Slide 416
Rate Limiting - Trade-offs
▸ Strict limits: better protection, worse UX for power users
  ↳ Provide tiered limits (free, paid, enterprise)
▸ Distributed counters (Redis) add latency vs local counters that are inconsistent
  ↳ Approximate algorithms (count-min sketch) for high-scale eventual consistency
▸ Hard reject (429) vs queueing
  ↳ Queue for short bursts; reject when sustained
▸ Synchronous vs asynchronous tracking
  ↳ Async (post-request log + tally) faster but allows brief overage
▸ Real example: Discord uses Redis-backed sliding window with per-route limits and bucket sharing
  ↳ Returns rate limit headers (X-RateLimit-Remaining, X-RateLimit-Reset) so clients self-throttle
📊 Trade-off scale - Accuracy vs Latency vs Cost with each algorithm placed

## Slide 417
Section 10 Wrap-Up

## Slide 418
Security - Key Takeaways
▸ Defense in depth: layer controls so no single failure is catastrophic
  ↳ Perimeter, network, host, application, data
▸ CIA triad guides every security decision
  ↳ Confidentiality, Integrity, Availability
▸ Authentication ≠ Authorization: verify identity, then check permissions
  ↳ Apply least privilege everywhere
▸ Use vetted crypto: AES-GCM for symmetric, RSA/Ed25519 for asymmetric, bcrypt/Argon2 for passwords
  ↳ Never roll your own
▸ Rate limiting protects against abuse, brute force, and accidental overload
  ↳ Apply at multiple layers with appropriate algorithms
📊 One-page cheat sheet with 5 quadrants - Principles, Encryption, Auth, Vulnerabilities, Rate Limiting

## Slide 419
Security - Interview Tips
▸ Always ask: who can access this data? What if their credentials leak?
  ↳ Threat modeling shows senior thinking
▸ Mention defense in depth even when asked about a single layer
  ↳ "I would also add..." demonstrates breadth
▸ For auth questions, contrast JWT vs sessions explicitly with trade-offs
  ↳ Revocation, scale, complexity
▸ For password storage, never accept "we hash with SHA-256"
  ↳ Push for bcrypt/Argon2 with appropriate cost factor
▸ Real example to drop: "Like the Capital One breach, SSRF + over-permissive IAM can cascade"
  ↳ Anchors abstract advice in real consequences
📊 Interview Q&A flowchart - "How would you store passwords?" → answer + follow-up branches

## Slide 420
Security - Common Pitfalls
▸ Storing JWTs in localStorage where XSS can steal them
  ↳ Use HttpOnly cookies for sensitive tokens
▸ Forgetting to revoke refresh tokens on logout or password change
  ↳ Maintain a revocation list keyed on jti
▸ Treating TLS as sufficient and skipping at-rest encryption
  ↳ Both are required for sensitive data
▸ Logging passwords, tokens, or PII in plaintext
  ↳ Redact before logging; review log pipelines for sensitive fields
▸ Hardcoding secrets in source code or config files
  ↳ Use secret managers (Vault, AWS Secrets Manager) with rotation
📊 "Wall of shame" - 5 anti-patterns crossed out with red X marks, correct pattern next to each

## Slide 421
Topic 6: Consistent Hashing

## Slide 422
Consistent Hashing - Concept Introduction
▸ A hashing scheme where adding/removing nodes only remaps a small fraction of keys
  ↳ Traditional hash(key) % N remaps almost all keys when N changes
▸ Maps both keys and nodes onto a circular hash ring (0 to 2^32-1)
  ↳ Each key is owned by the next node clockwise on the ring
▸ Solves the rebalancing problem in distributed systems
  ↳ When a node fails or scales out, only neighboring keys move
▸ Foundation for distributed caches, sharded databases, CDN routing
  ↳ Critical for elastic scale without massive data movement
▸ Real example: Amazon DynamoDB partitions data using consistent hashing across thousands of nodes
  ↳ Adding a node moves ~1/N of keys, not all of them
📊 Circle ring with 5 node icons placed around it; colored arcs showing the keyspace each node owns

## Slide 423
Consistent Hashing - Deep Explanation
▸ Hash function maps both nodes (by IP/ID) and keys to points on the ring
  ↳ Same hash function for both
▸ Each key is assigned to the first node found going clockwise from the key's position
  ↳ O(log N) lookup using a sorted structure (TreeMap, skip list)
▸ When node N is added: only keys between previous node and N are remapped
  ↳ Average 1/N of keys move
▸ When node N is removed: its keys redistribute to the next clockwise node
  ↳ Hot spot risk if removed node had a large arc
▸ Real example: Memcached clients (ketama hashing) use consistent hashing across servers
  ↳ Client-side decision; no server coordination needed
📊 Before/after ring diagrams. Before: 3 nodes with arcs A, B, C. After adding node D: only part of arc B is reassigned to D

## Slide 424
Virtual Nodes (vnodes) - Example/Intuition
▸ Problem with naive consistent hashing: uneven distribution due to hash randomness
  ↳ One node may own a much larger arc than others
▸ Solution: each physical node is represented by many virtual nodes (e.g., 100-200 per physical)
  ↳ Each vnode is hashed independently to a position on the ring
▸ Result: arcs average out, distribution becomes near-uniform
  ↳ Adding/removing a node spreads keys across many vnode boundaries
▸ Heterogeneous nodes: powerful nodes get more vnodes, weak nodes fewer
  ↳ Weight by capacity
▸ Real example: Cassandra defaults to 256 vnodes per physical node
  ↳ DynamoDB, Riak, ScyllaDB all use vnodes
📊 Two rings - Left: 3 nodes with uneven arcs (red highlights). Right: 3 nodes with 100 vnodes each, evenly distributed dots

## Slide 425
Consistent Hashing - Diagram
▸ Ring layout with hash space 0 to 2^32-1
  ↳ Wraps around; max value connects to 0
▸ Nodes placed at hash(node_id) positions
  ↳ Clients compute hash(key) and walk clockwise to find owner
▸ Replication: store on next K nodes clockwise for fault tolerance
  ↳ Quorum reads/writes across replicas
▸ Lookup data structure: sorted map of node positions
  ↳ findCeiling(hash(key)) returns owning node
▸ Real example: CDN edge selection - hash(URL) → walk ring → nearest healthy edge
  ↳ Removing a failed edge only affects its neighbors
📊 Detailed ring with hash positions labeled, key arrows pointing clockwise to their owning nodes, replication arrows to next 2 nodes

## Slide 426
Consistent Hashing - Trade-offs
▸ vs Modulo hashing: minimal remapping when nodes change (huge win)
  ↳ Modulo remaps ~all keys when N changes
▸ vs Range partitioning: better load balance for random keys
  ↳ Range better for ordered scans
▸ Lookup is O(log N), slightly more expensive than O(1) modulo
  ↳ Negligible at typical N
▸ Hot keys still possible: if one key gets 10x traffic, its node burns
  ↳ Pair with caching or hot-key replication
▸ Real example: DynamoDB uses consistent hashing + adaptive capacity to handle hot partitions
  ↳ Splits hot partitions automatically
📊 3-column table - Modulo, Consistent Hashing, Consistent Hashing+vnodes - rows: Remap %, Distribution, Complexity

## Slide 427
Topic 7: Bloom Filters

## Slide 428
Bloom Filters - Concept Introduction
▸ Probabilistic data structure for set membership testing
  ↳ "Is X in this set?" with very small memory footprint
▸ No false negatives (if it says no, it really is not there)
  ↳ Possible false positives (it may say yes when it is not)
▸ Trade space for certainty: ~10 bits per element for ~1% false positive rate
  ↳ Compare to a hash set storing full elements (8 bytes each + overhead)
▸ Cannot enumerate elements or delete from a standard Bloom filter
  ↳ Use Counting Bloom Filter for deletes
▸ Real example: Google Bigtable, Cassandra, RocksDB use Bloom filters to skip disk lookups
  ↳ Saves expensive disk seeks for keys that definitely do not exist
📊 Bit array with hash functions H1, H2, H3 each setting bits; query "is X in set?" checking same bits

## Slide 429
Bloom Filters - Deep Explanation
▸ Bit array of m bits + k independent hash functions
  ↳ Insert: hash element with each function, set those k bit positions to 1
▸ Query: hash element, check all k positions
  ↳ All 1 → "probably in set"; any 0 → "definitely not in set"
▸ False positive rate ≈ (1 - e^(-kn/m))^k
  ↳ Optimize k = (m/n) * ln(2) for given m, n
▸ Tunable: choose m and k based on expected n and acceptable FP rate
  ↳ 1% FP rate ≈ 9.6 bits per element with 7 hash functions
▸ Real example: Google Chrome's safe browsing uses Bloom filter of malicious URLs
  ↳ 1MB filter checks billions of URLs locally before contacting Google
📊 Math formulas + bit array with 3 hashes mapping to positions, showing both insert and query

## Slide 430
Bloom Filters - Use Cases
▸ Cache filters: "Is this URL cached?" before doing expensive lookup
  ↳ Avoid wasted cache miss round trips
▸ Database read optimization: skip SSTable disk reads for absent keys
  ↳ LevelDB, RocksDB, Cassandra, HBase
▸ Username/email availability check: fast pre-check before authoritative DB query
  ↳ Filter rejects most negatives instantly
▸ Distributed systems: gossiping set membership without sending full sets
  ↳ DHT, peer-to-peer networks
▸ Real example: Bitcoin SPV nodes use Bloom filters to ask peers for relevant transactions
  ↳ Keeps wallet privacy reasonable while reducing bandwidth
📊 4-quadrant grid with use cases as icons - Cache, Database, Username, P2P

## Slide 431
Bloom Filters - Example/Intuition
▸ Imagine a small library with 1M books and a "do we have this book?" desk
  ↳ A naive search of the catalog takes seconds
▸ Bloom filter is a compact summary: a 1.2 MB bit array answers in microseconds
  ↳ "Definitely not in library" → save the user a wasted catalog search
  ↳ "Probably in library" → check catalog to confirm
▸ ~1% of "yes" answers are wrong, but no "no" answer is ever wrong
  ↳ Acceptable when false positive cost is low (an extra DB call)
▸ Memory savings: 1M book titles × 100 bytes ≈ 100MB; Bloom filter ≈ 1.2MB
  ↳ 80x reduction
▸ Real example: Akamai uses Bloom filters at edge to filter "one-hit-wonder" URLs from cache
  ↳ Only cache items requested 2+ times; saves cache space dramatically
📊 Library counter - "yes" stamp (green with small "1% FP" footnote), "no" stamp (red, 100% accurate)

## Slide 432
Bloom Filters - Trade-offs
▸ Pros: tiny memory, fast O(k) operations, no full element storage
  ↳ Excellent for negative lookups
▸ Cons: false positives, no deletion, fixed size at creation
  ↳ Cannot enumerate elements
▸ Variants: Counting Bloom Filter (deletes via counters), Scalable Bloom Filter (grows dynamically)
  ↳ Cuckoo filter offers similar features with deletion support
▸ Sizing matters: too small → high FP rate; too large → wastes memory
  ↳ Plan for target n carefully
▸ Real example: Cassandra rebuilds Bloom filters per SSTable on compaction
  ↳ Tuned per-table based on workload
📊 Comparison bar - Hash Set vs Bloom Filter vs Cuckoo Filter on memory, lookup speed, supports delete

## Slide 433
Topic 8: Circuit Breaker Pattern

## Slide 434
Circuit Breaker - Concept Introduction
▸ Protects a service from repeatedly calling a failing downstream dependency
  ↳ Inspired by electrical circuit breakers that trip on overload
▸ Without it: failed dependency causes thread pool exhaustion, cascading failures, total outage
  ↳ One slow service brings down the entire system
▸ Tracks failure rate; "trips open" when threshold exceeded
  ↳ Subsequent calls fail fast, freeing resources
▸ Periodically allows test calls to detect recovery
  ↳ Self-healing without manual intervention
▸ Real example: Netflix Hystrix protected video streaming during downstream API failures
  ↳ One failing recommendation service did not block playback start
📊 Electrical breaker icon next to a microservice diagram, with breaker tripping when failure rate spikes

## Slide 435
Circuit Breaker States - Deep Explanation
▸ Closed (normal): all calls go through; failures counted
  ↳ If failures exceed threshold (e.g., 50% over 20 calls), trip to Open
▸ Open (tripped): all calls fail immediately without contacting downstream
  ↳ Returns cached value, default response, or error - fast fail
  ↳ After cooldown period (e.g., 30s), transition to Half-Open
▸ Half-Open (testing): allow limited number of test calls through
  ↳ If they succeed, go back to Closed; if they fail, return to Open
▸ Metrics tracked: failure rate, latency, slow call rate
  ↳ Slow calls counted as failures (otherwise hangs cascade)
▸ Real example: Resilience4j tracks rolling window of last N calls for failure rate
  ↳ Configurable thresholds per dependency
📊 State machine diagram - Closed (green) → Open (red) → Half-Open (yellow) with arrows labeled "threshold exceeded", "cooldown el...

## Slide 436
Circuit Breaker - Example/Intuition
▸ Service A calls Service B for user preferences
  ↳ B starts timing out (DB issue downstream)
▸ Without circuit breaker: A's threads pile up waiting on B
  ↳ A's thread pool exhausts; A starts failing all requests, including unrelated ones
▸ With circuit breaker: A detects 60% B-call failures, trips breaker
  ↳ A immediately returns cached preferences or default values
  ↳ A's thread pool stays healthy; other features work fine
▸ After 30 seconds, breaker tries one call to B
  ↳ If success → close breaker; if failure → wait another 30s
▸ Real example: Amazon Prime Video uses circuit breakers between recommendation, billing, and playback services
  ↳ User can still watch even if recommendations fail
📊 Two scenarios side-by-side - Without breaker (cascading red across all services) vs With breaker (failure isolated to one)

## Slide 437
Circuit Breaker + Retry + Timeout - Diagram
▸ Three patterns work together: timeout, retry, circuit breaker
  ↳ Timeout: per-call deadline (e.g., 1s)
  ↳ Retry: a few retries with exponential backoff and jitter
  ↳ Circuit breaker: gives up entirely when system is clearly down
▸ Without timeout: retries hang forever; circuit breaker cannot detect failures fast
  ↳ Always set tight, sensible timeouts first
▸ Without retry: transient blips cause unnecessary breaker trips
  ↳ Retry handles momentary glitches; breaker handles sustained outages
▸ Order: caller → retry wrapper → circuit breaker → timeout → downstream
  ↳ Each layer addresses a different failure pattern
▸ Real example: Netflix Hystrix combines all three; Resilience4j and Polly do the same
  ↳ gRPC interceptors and Istio service mesh provide these out of the box
📊 Layered onion - outer: caller, middle layers: retry → breaker → timeout, inner: downstream service

## Slide 438
Circuit Breaker - Trade-offs
▸ Fail-fast vs trying harder: fast failure improves overall system health
  ↳ But individual user requests fail sooner
▸ Threshold tuning is critical: too sensitive trips on noise; too lax fails to protect
  ↳ Start with 50% failure rate over 20-call window; adjust with data
▸ Cooldown duration: too short → flapping; too long → slow recovery
  ↳ 10-60s typical; tune per service
▸ Fallback strategy required: cached value, default response, degraded mode
  ↳ "Sorry, we cannot show recommendations right now" beats a 30s timeout
▸ Real example: Netflix Hystrix dashboard surfaced breaker state across hundreds of services
  ↳ Operators see cascading risk before it spreads
📊 Trade-off triangle - Sensitivity vs Recovery time vs User impact

## Slide 439
Topic 9: Back-of-the-envelope Estimation

## Slide 440
Estimation - Concept Introduction
▸ Quick math to size a system: requests/sec, storage, bandwidth, server count
  ↳ Within ~10x correctness; goal is sanity-check, not precision
▸ Demonstrates engineering judgment in interviews and design reviews
  ↳ "Will this fit on one server or do we need 100?"
▸ Foundation: powers of 2, latency numbers, rule-of-thumb assumptions
  ↳ Memorize these; do not derive from scratch each time
▸ Approach: state assumptions clearly, do math out loud, sanity-check at end
  ↳ Explicit reasoning matters more than the final number
▸ Real example: Twitter's original "140 chars × 500M tweets/day" math justified storage choices
  ↳ Same math justifies sharding strategy
📊 Napkin sketch with handwritten math: 1B users × 10 req/day / 86400 sec ≈ 116K req/sec

## Slide 441
Powers of 2 Reference - Deep Explanation
▸ 2^10 = 1,024 ≈ 1 thousand → 1 KB
▸ 2^20 = 1,048,576 ≈ 1 million → 1 MB
▸ 2^30 ≈ 1 billion → 1 GB
▸ 2^32 ≈ 4 billion → 4 GB (also IPv4 address space)
▸ 2^40 ≈ 1 trillion → 1 TB
▸ 2^50 ≈ 1 quadrillion → 1 PB
  ↳ Memorize so you can convert quickly
▸ ASCII char = 1 byte; UTF-8 ≈ 1-4 bytes; UUID = 16 bytes; timestamp = 8 bytes
  ↳ Use for record-size estimates
▸ Real example: 1B users × 1KB profile = 1 TB - fits on a single server's SSD
  ↳ Same data with images = 1 PB - needs distributed storage
📊 Reference table - power of 2, exact value, approximate label, common system context

## Slide 442
Latency Numbers Every Engineer Should Know
▸ L1 cache reference: 0.5 ns
▸ Branch mispredict: 5 ns
▸ L2 cache reference: 7 ns
▸ Mutex lock/unlock: 25 ns
▸ Main memory reference: 100 ns
▸ Compress 1KB with Zippy: 3,000 ns (3 μs)
▸ Send 1KB over 1 Gbps network: 10,000 ns (10 μs)
▸ Read 4KB random from SSD: 150,000 ns (150 μs)
▸ Read 1MB sequentially from memory: 250,000 ns (250 μs)
▸ Round trip within same datacenter: 500,000 ns (500 μs)
▸ Read 1MB sequentially from SSD: 1,000,000 ns (1 ms)
▸ Disk seek (HDD): 10,000,000 ns (10 ms)
▸ Read 1MB sequentially from HDD: 30,000,000 ns (30 ms)
▸ Send packet US → Europe → US: 150,000,000 ns (150 ms)
  ↳ Memory is ~100,000x faster than HDD; SSD is ~10x faster than HDD seek
📊 Logarithmic scale bar chart showing each operation as a horizontal bar, color-coded by category (cache, memory, network, disk)

## Slide 443
Traffic and Storage Estimates - Example/Intuition
▸ Traffic example: 1B daily active users, each makes 10 reads + 1 write per day
  ↳ Reads: 10B/day = 10B / 86400 ≈ 116K reads/sec average
  ↳ Peak (3x average): ~350K reads/sec
▸ Storage example: 1B users × 1KB profile = 1 TB; with 5-year retention and 10% growth = ~5 TB
  ↳ Replication factor 3 → 15 TB raw capacity
▸ Bandwidth example: 1M concurrent video streams × 5 Mbps = 5 Tbps
  ↳ Requires major CDN; not single-DC
▸ Always state: peak vs average, read:write ratio, retention period
  ↳ These assumptions drive the architecture
▸ Real example: YouTube uploads ~500 hours/min of video; average 50MB/min storage = 25TB/min raw
  ↳ Justifies massive distributed object storage (Bigtable + Colossus)
📊 Calculation worksheet showing assumptions on left, math in middle, results on right

## Slide 444
Estimation - Trade-offs
▸ Precision vs speed: 5-minute estimate guides the next 5 hours of design
  ↳ Aim for order-of-magnitude correct
▸ Average vs peak: design for peak; size capacity at 2-3x average
  ↳ Black Friday, viral content, time zones cause spikes
▸ Read-heavy vs write-heavy assumption changes architecture
  ↳ Caches help reads; sharding helps writes
▸ Round numbers aggressively: 86400 ≈ 100K seconds/day
  ↳ Speeds mental math without losing accuracy
▸ Real example: System design interviews score on reasoning, not the final number
  ↳ "1 in 100K precision is wrong but 1 in 10 is fine"
📊 Quick-reference card with daily seconds (86,400 ≈ 100K), monthly seconds (~2.5M), QPS conversions

## Slide 445
Topic 10: System Design Interview Framework

## Slide 446
Interview Framework - Concept Introduction
▸ A structured 5-step approach to handle any system design question
  ↳ Avoid jumping to solutions; demonstrate disciplined thinking
▸ Steps: Clarify → Estimate → High-level design → Deep dive → Bottlenecks
  ↳ Allocate roughly: 5min, 5min, 10min, 15min, 10min in a 45-min interview
▸ The framework is the answer
  ↳ Interviewers grade structure as much as the technical content
▸ Communicate trade-offs explicitly at every step
  ↳ "I'd choose X because Y, accepting trade-off Z"
▸ Real example: Asked "Design Twitter" - clarify scope (timelines? DMs? search?), estimate, sketch, deep dive on fanout, address hot users
  ↳ Same framework applies to URL shortener, ride share, chat app
📊 5-step horizontal flow with time allocations and sample questions at each stage

## Slide 447
Step 1 - Clarify Requirements
▸ Functional requirements: what the system does (features)
  ↳ "Users can post tweets, follow others, see a timeline"
▸ Non-functional requirements: how well it does it (qualities)
  ↳ Latency, availability, consistency, scalability, durability
▸ Constraints: scale (1M vs 1B users), region (single vs global), budget
  ↳ These shape every design choice that follows
▸ Out-of-scope items: explicitly call them out
  ↳ "I'll skip search and DMs to focus on core posting + timeline"
▸ Real example: Designing Uber - confirm: ride-hailing only? matching? payment? maps? surge pricing?
  ↳ Scope determines whether the answer covers 5 services or 50
📊 Two columns - Functional (feature checklist) vs Non-functional (latency budget, 99.99% SLA, etc.) with an "Out-of-scope" sectio...

## Slide 448
Step 2 - Estimate Scale
▸ Calculate: DAU, requests/sec (avg + peak), storage/year, bandwidth
  ↳ Use rule-of-thumb assumptions and powers of 2
▸ Read:write ratio shapes architecture
  ↳ 100:1 read-heavy → cache aggressively; 1:1 → focus on write throughput
▸ Storage: bytes per record × records per second × retention
  ↳ Multiply by replication factor for raw capacity
▸ Bandwidth: requests/sec × payload size, both ingress and egress
  ↳ Egress dominates for video, downloads, social feeds
▸ Real example: Designing Instagram - 500M DAU × 5 photos viewed = 2.5B reads/day, ~30K reads/sec average, ~100K peak
  ↳ Justifies CDN + read replicas
📊 Estimation worksheet with placeholder math: DAU ___, RPS ___, Storage/year ___, Bandwidth ___

## Slide 449
Step 3 - High-Level Design
▸ Draw boxes and arrows: client, load balancer, app servers, cache, DB, queue, workers
  ↳ 5-10 boxes; do not over-detail yet
▸ Identify the major data flows: read path, write path, async jobs
  ↳ One arrow per flow; label with key operation
▸ Choose major technologies with brief justification: SQL vs NoSQL, Redis vs Memcached, Kafka vs SQS
  ↳ Trade-offs in one sentence each
▸ Add CDN, API gateway, monitoring as supporting infrastructure
  ↳ Mention but do not dive in yet
▸ Real example: URL shortener high-level: Client → CDN → API Gateway → App Server → Redis cache → MySQL (sharded by hash)
  ↳ Add Kafka for analytics events
📊 Box-and-arrow architecture diagram with 7-8 components, color-coded by tier (edge, app, data)

## Slide 450
Step 4 - Deep Dive into Components
▸ Pick 1-2 critical components based on interviewer interest
  ↳ Usually data model, hot path, or unique scaling challenge
▸ Data model: tables/documents, indexes, partition key, access patterns
  ↳ Justify schema choices; show query examples
▸ Caching strategy: cache key, TTL, invalidation, hit ratio target
  ↳ Address thundering herd, stampede mitigation
▸ Sharding/partitioning: key choice, hot partition handling, rebalancing
  ↳ Use consistent hashing, range, or composite keys
▸ Real example: Twitter timeline - deep dive on fanout-on-write vs fanout-on-read, hybrid for celebrities
  ↳ Justify with celebrity follower count math (millions of fans)
📊 Zoom-in lens icon on one component from high-level diagram, exploding into detailed sub-architecture

## Slide 451
Step 5 - Identify and Address Bottlenecks
▸ Walk through the design asking: where does this break at 10x scale?
  ↳ Single DB → shard or replicate; one cache → distributed cache; one region → multi-region
▸ Common bottlenecks: hot keys, single point of failure, sync replication latency, expensive joins
  ↳ Prepare a mitigation for each
▸ Discuss trade-offs explicitly: stronger consistency vs lower latency, cost vs reliability
  ↳ Show you understand there is no free lunch
▸ Add observability: metrics, logs, traces, alerts on SLO breaches
  ↳ "How would I know this is failing?"
▸ Real example: Designing chat app - identify hot rooms (1M users in one room) → shard by sub-room or use pub/sub fanout
  ↳ Each bottleneck has a known pattern
📊 Bottleneck heatmap on the architecture diagram with red dots, each annotated with mitigation

## Slide 452
Common Follow-Up Questions
▸ "How would you handle 10x more traffic?"
  ↳ Horizontal scaling, caching layers, async processing, sharding
▸ "What if region X goes down?"
  ↳ Multi-region active-active or active-passive, data replication, DNS failover
▸ "How do you ensure data consistency?"
  ↳ Choose CP or AP per use case; transactions where needed; eventual consistency where acceptable
▸ "How would you monitor this?"
  ↳ RED metrics (Rate, Errors, Duration), USE method, dashboards, alerts on SLO
▸ "What if a celebrity user has 100M followers?"
  ↳ Hybrid fanout, special-casing, async pre-computation
▸ Real example: "Design Slack" follow-ups always include - presence, search, mobile push, file storage
  ↳ Anticipate them; have a 2-sentence answer ready for each
📊 Q&A flashcards layout - question on top, 2-3 bullet answer below, in a grid

## Slide 453
Interview Framework - Trade-offs
▸ Time vs depth: spending too long clarifying leaves no time for design
  ↳ Stick to budget; politely ask "let me move forward"
▸ Breadth vs depth: covering many components shallowly vs few components deeply
  ↳ Cover breadth in high-level, depth in 1-2 components
▸ Buzzwords vs reasoning: name-dropping Kafka without justification looks weak
  ↳ Always pair tech choice with one-sentence "because X"
▸ Generic vs tailored: applying the same template to every problem is robotic
  ↳ Adapt - some problems are write-heavy, some are real-time, some are storage-heavy
▸ Real example: Strong candidates often draw a quick scaling roadmap: "v1 single server → v2 add cache → v3 shard → v4 multi-region"
  ↳ Shows evolutionary thinking
📊 Time budget pie chart - Clarify 10%, Estimate 10%, High-level 25%, Deep dive 35%, Bottlenecks 20%

## Slide 454
Section 11 Wrap-Up

## Slide 455
Advanced Topics - Key Takeaways
▸ Consistent hashing minimizes remapping when nodes change
  ↳ Vnodes provide even distribution and weighted nodes
▸ Bloom filters trade certainty for space
  ↳ No false negatives; perfect for cache and DB skip-lookups
▸ Circuit breakers prevent cascading failures
  ↳ Closed → Open → Half-Open with proper thresholds and fallbacks
▸ Estimation skills guide architecture in 5 minutes
  ↳ Memorize powers of 2 and latency numbers
▸ Interview framework provides structure: Clarify, Estimate, Design, Deep dive, Bottlenecks
  ↳ The framework itself is half the answer
📊 5-icon summary - ring, bit array, breaker, calculator, framework arrow

## Slide 456
Interview Tips - Final
▸ Always start by clarifying scope; do not jump to a solution
  ↳ 30 seconds of clarification saves 30 minutes of wrong design
▸ Think out loud: interviewer follows your reasoning, not just the diagram
  ↳ Even when stuck, narrate options and trade-offs
▸ Use real-world examples to anchor abstract claims
  ↳ "Like how Cassandra uses vnodes" or "Netflix's Hystrix pattern"
▸ When asked about a specific tech, give 1-line definition + 2-line trade-offs
  ↳ Shows you know the tech and where it fits
▸ Wrap up with a recap and explicitly call out things you would do given more time
  ↳ Demonstrates self-awareness and prioritization
📊 Interview "do's and don'ts" list, color-coded green and red

## Slide 457
Common Pitfalls - Final
▸ Designing for a billion users when the problem is for a thousand
  ↳ Overengineering wastes time and money; start simple, evolve
▸ Forgetting non-functional requirements: latency, availability, durability
  ↳ These often drive design more than features
▸ Picking technologies without justifying fit
  ↳ "I'd use Cassandra because it's web-scale" is a red flag
▸ Ignoring failure modes: what happens when a node, region, or dependency fails?
  ↳ Senior engineers always have a "what if it breaks" answer
▸ Skipping monitoring and observability
  ↳ Production systems must answer "is it working?" "what is broken?" "how do I know?"
▸ Real example: Premature sharding adds operational pain without scale benefit
  ↳ Many systems run for years on a single beefy DB
📊 "Anti-pattern wall" - 6 common mistakes crossed out with red X, correct approach below each

## Slide 458
Closing - From Theory to Practice
▸ System design is iterative: ship simple, measure, evolve
  ↳ No design survives contact with real traffic unchanged
▸ Read engineering blogs: Netflix, Uber, Stripe, Discord, Cloudflare publish real war stories
  ↳ Pattern-match production decisions to interview frameworks
▸ Build small projects end-to-end: deploy, monitor, scale, fail, recover
  ↳ Theory + practice compounds faster than either alone
▸ Master fundamentals: consistency, partitioning, replication, caching, queues
  ↳ Every advanced system is a recombination of these primitives
▸ Real example: Discord scaled to 200M users by repeatedly applying Cassandra + Rust + careful sharding
  ↳ No magic; just disciplined application of fundamentals
📊 Spiral diagram - ship → measure → learn → evolve, with each loop labeled with a concept from the deck

## Slide 459
Resources for Further Study
▸ Books: "Designing Data-Intensive Applications" by Martin Kleppmann (essential)
  ↳ "System Design Interview" by Alex Xu (interview-focused)
▸ Engineering blogs: Netflix Tech Blog, Uber Engineering, High Scalability, AWS Architecture Blog
  ↳ Real systems at real scale
▸ Papers: Dynamo (Amazon), Bigtable (Google), Spanner (Google), Kafka, Raft
  ↳ Foundational reading; many modern systems trace back to these
▸ Practice: Pramp, interviewing.io, design problems on LeetCode
  ↳ Mock interviews build the muscle memory
▸ Communities: r/ExperiencedDevs, HackerNews, Discord communities, local meetups
  ↳ Learning compounds in good company
📊 Resource library shelf - books, papers, blogs, podcasts as icons